## Slide 1
Technology
Development & Prototyping Division
ANG-C5
RIRP Portfolio Update
Presented to: REDAC
Date: March 2015
Federal Aviation Administration

## Slide 2
Runway Incursion Reduction Program (RIRP)
Why do we do what we do?
FAA Strategic Priority 1 – Make Aviation Safer and Smarter
FAA Performance Metric 4 – Reduce Category A & B (most serious) runway incursions to a rate of no more than 0.395 per million operations, and maintain or improve through FY 2018.
FAA Mission Needs Statement 323 (circa 1998):
  Runway Incursions (RIs) are a major problem affecting the safe operations of the nation’s airports.
Destination 2025 (2011)
  2018 Performance Metrics: Maintain the rate of serious runway incursions at or below 20 per 1000 events.
NTSB Recommendation A-91-30
  Calls for the FAA to implement equipment aimed at reducing runway incursions
Notes: Runway Incursions have been recognized as a risk to aviation safety for at least twenty years. The Runway Incursion Reduction Program (RIRP) initiative is based on several recommendations and requirements.
The RIRP conducts research, development, and operational evaluation of technologies designed and developed to increase runway safety. Consistent with standing National Transportation Safety Board (NTSB) recommendations and initiatives identified in FAA Destination 2025, research emphasis will remain on technologies that provide for direct safety indications and alerts to pilots and air crews at large airports as well as those that can be applied cost effectively at small to medium airports.

## Slide 3
Runway Incursion Reduction Program (RIRP)
Why do we do what we do?
  March 27, 1977: Fatal collision between two Boeing 747 passenger aircraft on the runway of Los Rodeos Airport on Tenerife, one of the Canary Islands. This crash killed 583 people, making it the deadliest accident in aviation history.
  August 27, 2006: Comair Flight 5191 Lexington, KY, to Atlanta, GA, crashed on takeoff, just past the end of the runway, killing all 47 passengers and two of the three crew. The aircraft was assigned Runway 22 for the takeoff, but used Runway 26 instead.
Notes: These two accidents illustrate the need for enhanced situational awareness, improved signage and markings, improved training for flight crews, and the development of runway incursion prevention technologies.

## Slide 4
Runway Incursion Reduction Program (RIRP)
Why do we do what we do?
  April 24, 2014: Two planes nearly collided at Newark Liberty International Airport. United Express Flight 4100 was cleared to take off on runway 4R at the same time United Airlines Flight 1243 was landing on the intersecting Runway 29. The two aircraft passed within yards of each other.
  July 6, 2014: A passenger jetliner preparing to leave Barcelona’s El Prat airport taxied across a runway where another was about to land, forcing the arriving plane to abort its landing and climb sharply to avoid a possible disaster.
March 2015
Notes: Here are two more recent incidents that could have been prevented through the implementation of conflict alerting systems.

## Slide 5
Runway Incursion Reduction Program (RIRP) Projects
Low Cost Ground Surveillance (LCGS) - Cancelled by JRC
Enhanced FAROS (eFAROS) – Successful June 2014 Flight Check at BOS; pending approval for OpEval test from AFS.
Runway Safety Assessment (RSA) – conducting RI Prevention Shortfall Analysis; conducting on-site technical assessments for technologies selected from FY14 Market Survey.
Small Airport Surveillance Sensor (SASS) – evaluating technical performance of phased array surveillance sensor developed by MIT Lincoln Lab for real-time movement area coverage.
Notes: RIRP portfolio of current projects.
Projects are owned by Runway Safety Office, and are funded through F&E dollars. These projects are actively managed by ANG-C5, the Technology Development and Prototyping Division.

## Slide 6: Low Cost Ground Surveillance (LCGS)
RIRP Portfolio Update
Presented to: REDAC
Date: March 2015

## Slide 7
In August 2007, Runway Safety Call to Action identified LCGS as potential technical solution to increase in Runway Incursions
Runway Incursion Reduction Program Office requested LCGS Investment Analysis Readiness Decision (IARD) from the Executive Council on May 26, 2009.
ATO EC delayed making a final decision; EC met again on July 7, 2009, and made the following decision:
    Directed team to continue with contract awards for the prototype systems
    Directed team to operate the prototype systems for two years
    Directed team to return to the EC with results of the operational evaluation
JRC meeting 6/19/2013 determined that LCGS not viable as a program
All 5 sites were powered down by 09/01/2013
All LCGS displays were removed from ATCT cabs as of 9/30/2013
All LCGS cameras were removed from ATCT and radar towers as of 2/28/2014
Final equipment and infrastructure inventory and bar coding was completed as of 11/01/2014
LCGS Pilot Program History and Status

## Slide 8: Notional Removal Schedule

## Slide 9: Enhanced Final Approach Runway Occupancy Signal (eFAROS)
RIRP Portfolio Update
Presented to: REDAC
Date: March 2015

## Slide 10: Enhanced Final Approach Runway Occupancy Signal (eFAROS)
Enhanced-Final Approach Runway Occupancy Signal (eFAROS) uses surface surveillance with augmented safety logic to provide a visual warning to pilots on final approach that the runway is occupied and unsafe for landing. It does this by flashing the Precision Approach Path Indicator (PAPI) lights.
AJW-143 is providing design and engineering support for the development and implementation of eFAROS at RWSL test locations
Partners / Stakeholders
  Air Traffic Controllers
  AJW-14
  Airport Authorities (DFW, BOS)
  Local Tech-Ops personnel
Notes: 10

## Slide 11: Milestone Schedule
Develop quicklook report on shadow operations testing of the prototype eFAROS system at BOS. |  | Complete |  | 
Complete installation of the FPAPI units at BOS. |  | Complete | Complete | 
Conduct flight check of the FPAPI units installed at BOS, and commence 90-day Operational Evaluation of the prototype eFAROS system at BOS |  |  | Flight check Completed 06/22/2014 | 
FY 14 Milestones
Q1
Q2
Q3
Q4
August 2014
Notes: 11

## Slide 12: Milestone Schedule
Commence operational evaluation at BOS (pending final AFS consultation/decision). |  |  |  | 
Complete report on 90-day prototype Operational Evaluation test of eFAROS at BOS. |  |  |  | 
Develop preliminary requirements document, final benefit/cost analysis report (BCAR) and IARD documents for JRC readiness decision. |  |  |  | 
FY 15 Milestones
Q1
Q2
Q3
Q4
Notes: 12

## Slide 13: FY14/15 eFAROS Activities
FY14 Completed:
Conducted ATC training and pilot outreach for eFAROS at BOS – May/Jun 2014
Conducted successful Flight Check Test of eFAROS at BOS – Jun 21-22, 2014
FY15 Planned:
Commence “live” Operational Evaluation test of eFAROS at BOS – Mar 2015 (pending AFS-400 approval)
Publish initial Preliminary Requirements Document (PRD) for eFAROS – Sep 2015
Publish updated Cost-Benefit Analysis (CBA) for eFAROS – Sep 2015
August 2014

## Slide 14: Runway Safety Assessment (RSA)
RIRP Portfolio Update
Presented to: REDAC
Date: March 2015

## Slide 15: Runway Safety Assessment (RSA)
RSA is intended to address the NTSB recommendation A-00-66 that states: “Require, at all airports with scheduled passenger service, a ground movement safety system that will prevent runway incursions; the system should provide a direct warning capability to flight crews. In addition, demonstrate through computer simulations or other means that the system will, in fact, prevent incursions.”

## Slide 16: ANG-C Market Survey - Overview
ANG-C5 issued a Market Survey on July 23, 2013 for Runway Incursion Reduction Technologies (Contract Opportunity ID: 14673).
The Market Survey solicits input on feasible technologies from industry partners and interested vendors. This survey is not a formal contract solicitation and is not intended to result in a contract award.
The intended outcome of the Market Survey is to evaluate one or more technologies which may be applied, or enhanced through additional research, to prevent runway incursions.
Market Survey closed on Aug 23, 2013; a total of 30 qualifying responses were received.
August 2014

## Slide 17: ANG-C Market Survey - Assessment
Evaluation of the responses was conducted from 10/31/13 to 12/6/13.
The responses received were evaluated by a team of 8 FAA employees and contractors from ANG-C and AJI, consisting of SME’s in:
  ATC
  Engineering & Technology
  Program Management
  Runway Safety
The outcome of the evaluation process is focused on categorizing the responses by:
  the technical maturity of the proposal
  research viability within a 3-year timeframe
August 2014

## Slide 18: Milestone Schedule
Perform technical evaluation of feasible technologies identified in Market Survey responses. |  |  |  | 
Develop Runway Incursion Prevention Shortfall Analysis report. |  |  |  | 
Develop report on proposed solution set for new Runway Incursion reduction technologies. |  |  |  | 
FY 15 Milestones
Q1
Q2
Q3
Q4
Notes: 18

## Slide 19: FY15 Activities
Conduct Technical Feasibility Assessment of Candidate RI prevention technologies identified during market survey evaluation process. Q1-Q3FY15
Undertake data-driven analysis of coded historical Runway Incursion incidents to categorize RIs by causal factors. Q2-Q3FY15
Develop Runway Incursion Prevention Shortfall Analysis (RIPSA) report. Q3FY15
Develop “right-site-right-size” report on proposed solution set for new Runway Incursion reduction technologies based on RIPSA report and candidate technologies deemed feasible for evaluation. Q4FY15

## Slide 20: Candidate RI prevention technologies for Technical Evaluation
August 2014

## Slide 21: Searidge Technologies
IntelliDAR
  This system is based on real time video capture and processing for zone detection. It is primarily a surveillance tool with HMI capabilities for ATC, and is already being used in gate areas of airports in Canada such as Ottawa. It is currently under evaluation for Non-Movement Area (NMA) application at WJHTC.
August 2014

## Slide 22: Neptec Technologies
LiDAR
  Neptec proposes using its Opal family of LiDAR sensors in conjunction with its 3D change-detection software as a sensor system for runway incursion prevention systems. This proposed technology can collect points at a high resolution, can collect object shape information, and can detect any object, regardless of whether it is equipped with a transponder or not.
August 2014

## Slide 23: Aeropath Technologies
ARTI (Airport Real Time Information)
  Aeropath proposes using its ARTI system for ground surveillance at small to medium-sized airports. ARTI is based on a Garmin TCAS transponder unit that detects local airplane traffic via the airplane’s transponder. This is done in the airport control zone, defined as 5 to 10 miles and altitudes up to 3,000 feet AGL.
August 2014

## Slide 24: Thales
XSight
  Thales and its partner, Xsight Systems, provide Foreign Object Debris Detection technologies to airports such as BOS. They propose using this system that utilizes Surface Detection Units (SDUs) installed along both sides of the airport runway, as a runway surveillance sensor . Each SDU has a dual sensor head (DSH) that combines a Millimeter-Wave Radar sensor with a day/night Vision sensor.
August 2014

## Slide 25: Small Airport Surveillance System (SASS)
RIRP Portfolio Update
Presented to: REDAC
Date: March 2015

## Slide 26: Small Airport Surveillance Sensor (SASS)
SASS is a low-cost secondary surveillance solution
  Provides surface & airborne surveillance in airport vicinity
  Expected Surface accuracy ~30’, airborne targets ~20 nm out
Potential benefits
  Provides improved controller traffic situation awareness
  Improved safety & efficiency at towered airports
  Portability for disaster response (Haiti) & special events (Oshkosh)
Key design features
  High accuracy phased array antenna design
  COTS equipment use - Software Defined Radio (SDR) modules
  State-of-the-art digital signal processing leveraged from DoD work
  Requires only two sensors installed on airport property
Target airports
  GA airports with Class D airspace towers
  High traffic non-towered airports

## Slide 27: SASS System Diagram

## Slide 28: SASS Design Features
Phased Array Antenna
0.4 azimuth accuracy
Omni-directional reception
1 m
Software Defined Radio
Inexpensive COTS modules
Receiver, DDC, FPGA, I/Q output
Ettus X300 USRP dual channel ($4K)
TCAS Interrogator
Transponder disabled to prevent interference
COTS unit (~$20K)
Installation & Maintenance
Only two sensors required
Installed on airport property
Simplifies maintenance
Eligible for AIP funding
Surveillance Capabilities
30’ accuracy on airport surface
Airborne surveillance to 20 nm
Omni-directional reception
ADS-B (1090ES & UAT)
Runway Incursion Alerting
Reuse existing Safety Logic software (no development cost)
Leverage expertise in developing eFAROS systems including extensive field testing experience

## Slide 29: How SASS Works
Range bias determined from one interrogation and two replies

## Slide 30: SASS Master & Slave Hardware Design
1090 XPNDR
X300 USRP 1030 MHz @ 100 Msps
GPS Time
8 x N200 USRPs @ 10Msps
1090 Receiver
Omni Blade
TCAS Antenna
Dual Directional
Coupler
X300 USRP 1090 MHz @ 100 Msps
X300 USRP 1090 MHz @ 100 Msps
Monopole
AUX Antenna
Interrogation
time
q1
q2
TOA1
TOA2
GPS Time
TCAS
Unit
SASS Master Unit
SASS Slave Unit
8 x N200 USRPs @ 10Msps
1090 Receiver
New design uses low-cost USRP* modules
*Universal Software Radio Peripheral

## Slide 31: SASS Data Collection System
3.2 Gbps
1 X300 (50 Msps)
GPS (10 MHz Ref, PPS)
1-GigE port 10
10-GigE port 2
8 N200s (10 Msps)
1-GigE ports 1-8
10-GigE port 1
1-GigE port 9
RAID SSDs
(2.5 TB ≈ 55 min continuous recording for these 10 channels)
512 GB
512 GB
512 GB
512 GB
512 GB
2.56 Gbps
5.76 Gbps
RAM
(64 GB ≈ 90 sec recording)
8 GB
8 GB
8 GB
8 GB
8 GB
8 GB
8 GB
8 GB
Raid
Controller
(6 Gbps)
Thinkmate Server
1 X300 (50 Msps)
GPS (10 MHz Ref, PPS)
Boot SSDs
256GB
256GB
RAID Overhead
512 GB
512 GB
Intel Xeon Quad Core (2.5 GHz)
Intel Xeon Quad Core (2.5 GHz)
Data collection system design supports very high data recording rate
Additional channel
needed for receiving
UAT messages

## Slide 32: SASS Data Collection (Hanscom Field, 15 December 2014)
Array
Phased Array Antenna
Test Vehicle
Transponder
Antenna
GPS
Antenna
SASS Van
Vehicle Azimuth (DGPS)
Test vehicle with Mode S transponder & DGPS driven slowly around array
8-channel I & Q data from phased array collected using borrowed equipment
o
Array
Test vehicle
path
Vehicle Position (DGPS)

## Slide 33: FY15 Hanscom Data Collection
Test vehicle with DGPS &
transponder
MODSEF
(1.3 nm away)
ADS-B
equipped
aircraft
Installing sensors in vehicles with generators for FY15 data collection pending semi-permanent installations
Truth sources: DGPS, Lincoln Mode S radar (MODSEF), ADS-B equipped targets of opportunity & video cameras
WiFi
WiFi

## Slide 34: Milestone Schedule
Develop SOW and create new TASK for SASS project under current MIT LL contract |  |  |  |  | 
Build and test SASS hardware platform |  |  |  |  | 
Develop real-time signal processing software |  |  |  |  | 
Perform surveillance data collection at BED |  |  |  |  | 
Demo real-time surface surveillance at BED using SASS. |  |  |  |  | 
FY 15 Milestones
Q1
Q2
Q3
Q4
Q1
Notes: 34

## Slide 35: FY15 Activities
Build and test SASS Master and Slave mobile units. Q2FY15
Develop and test real-time signal processing software. Q2-Q3FY15
Conduct field tests at Hanscom Field (BED) using SASS Master & Slave mobile units. Q4FY15
Perform analysis to evaluate the performance of the SASS system against truth data. Q4FY15
Develop report on the performance of the SASS system against truth data. Q1FY16

## Slide 36
FY16 RIRP Proposed Activities

## Slide 37
Complete annual technical and operational evaluation report of existing RIRP prototype systems.
Complete annual report documenting results of human-in-the-loop (HITL) testing Human Factors (HF), safety logic, aircraft performance, or any uncertainty or deficiency pertaining to surface based RI indications.
Complete annual report on Runway Incursion (RI) prevention shortfall analysis.
Complete annual report on testing of safety logic enhancements to Runway Incursion (RI) detection and prevention products.
Publish the Project Plan and Resource Management Plan (RMP) for the utilization of a Small Airport Surveillance Sensor (SASS) as a sensor to drive the activation of direct to pilot alerting safety logic.

## Slide 38
FY17 RIRP Proposed Activities

## Slide 39
Complete annual technical and operational evaluation report of existing RIRP prototype systems.
Complete annual report documenting results of human-in-the-loop (HITL) testing HF, safety logic, aircraft performance, or any uncertainty or deficiency pertaining to surface based RI indications.
Complete annual report on testing of safety logic enhancements to Runway Incursion (RI) detection and prevention products.
Complete report documenting candidate site selection for a system to test the utilization of a Small Airport Surveillance Sensor (SASS) as a sensor to drive the activation of direct to pilot alerting safety logic.
Complete report on integration of a system to test the utilization of a Small Airport Surveillance Sensor (SASS) as a sensor to drive the activation of direct to pilot alerting safety logic.
Publish the initial Project Plan and Resource Management Plan (RMP) for the utilization of an advanced ground surveillance sensor to drive the activation of direct to pilot alerting safety logic

## Slide 40
BACKUP SLIDES

## Slide 41: Modeled Surface Surveillance Error (ft) (Hanscom Field in Bedford, MA)
30’ position error or less over entire surface movement area
SASS Sensor
SASS
Sensor
Model Assumptions
Range error: 10’ (1 ) Azimuth error: 0.4 (1 )

## Slide 42: Siting Options with Obstruction Surfaces

## Slide 43: Steps For Site Breakdown
1) Removal/Relocation of existing equipment racks located in shelter
2) Removal / crating of existing radar equipment located in shelter, including the disconnection of radar waveguide/transceiver/motor controller
3) Removal of electrical conduits between LCGS radar tower and shelter
4) Removal of copper ground leads to ground counterpoise
5) Removal of Ice Bridge connecting LCGS tower to shelter
6) Pull back of FAA single mode fiber from the shelter back to nearest pull box
7) Termination of existing power feed to FAA ATCT location (This will require support from the local Service Area)
8) Installation of Battery Operated Obstruction lights on LCGS radar tower until tower can be removed

## Slide 44: Site #1: Pine Hill T-Hangars
Box truck obtained for second SASS unit
  Allows identical tall rack to be installed
  Towed generator for power
Telescoping tower with trailer
  50’ extended height
  15’ retracted height

## Slide 45: Site #2: Salt Shed
Antenna attached to truck
  50’ extended, 20’ retracted
  Set up at SE corner of salt shed
  May attach antenna to shed (MassPort suggestion)
Truck
  Contains data recording system
  Towed generator for power

## Slide 46: Flight Facility Tower Cab
Will be used to mimic BED tower
  Good view of runways & taxiways (85’ tall)
  Near actual tower (550’)
View of airfield to North from Flight Facility tower cab