## Slide 1: FY 2016 Aircraft Safety PPT Portfolio Review
By: Ian Y. Won
Date: March 5, 2014
Structural Integrity Metallics (SIM)
Part of BLI A11.e Continued Airworthiness
Notes: The intent of the presentation is to provide the SAS members with enough information to evaluate the content of the proposed FY15 Aviation Safety R&D Portfolio for each BLI or BLI subsection. The presentation has two distinct parts.
Part One is a broader overview of the BLI, its overall purpose, how it supports the AVS mission area(s), the overall benefits, and a general review of how the research gets done. The overview explains the why, what, and how for a particular area of research and should set a solid foundation for Part Two.
Part Two presents a quad chart for each of the requirements in the proposed FY15 portfolio. Parts one and two should work together to present a cohesive picture of the program to the SAS members. The TAS presentation from the FY14 presentation to the SAS is used as an example.

## Slide 2
SIM-TCRG Members
Name | Organization | Function
Ian Won | TAD, ANM-115 | TCRG Lead, TAD Sponsor
Mark Freisthler | TAD, ANM-115 | TAD Sponsor
Carl Niedermeyer | TAD, ANM-115 | TAD Sponsor
Todd Martin | TAD, ANM-115 | TAD Sponsor
Walt Sippel | TAD, ANM-115 | TAD Sponsor
Patrick Safarian | TAD, ANM-120S | TAD Sponsor
Mike Reyer | SAD, ACE-113 | SAD Sponsor
Jim Kabbara | AIR-120 | AIR Sponsor
John Bakuckas | FAA-TC, ANG-E281 | Performer – Transport
Dave Westlund | FAA-TC, ANG-E281 | Performer – Transport
Ed Weinstein | FAA-TC, ANG-E281 | Performer – Flight Loads
Steve Edgar | TAD, ANM-110 | TAD OPI
Mark Orr | SAD, ACE-114 | SAD OPI

## Slide 3: SIM Program Overview
Research supports AVS general mission areas:
Continued Operational Safety (COS) - Assess and ensure the long-term airworthiness of existing aircraft structure. Research provides data and tools
  Transport Airplane Risk Assessment Methodology,
  Bonded Repair Technology,
  Small Airplane Risk Analysis,
  Structural Health Monitoring)
Standards and Policy – Create and amend as necessary the rules, regulations, and regulatory guidance that provide the airframe structural safety standards. Promotes efficient use of FAA resources thru maintenance and distribution of tools, data and standards
  MMPDS and NASGRO)
Certification - Issue initial and amended type certificates that allow manufacturers to build aircraft and organizations to provide maintenance services. Data needed to assess certification of airplane structures utilizing novel designs and emerging materials(e.g.
  Aluminum-Lithium
  Additive Manufacturing
  Active Flutter Suppression)

## Slide 4: SIM Program Overview
What is this program?
Purpose
  Prepare for new technologies by:
    Providing data in order to enhance existing regulations and standards
    Encourage the implementation of new technologies that improve operational safety
    Leveraging FAA assets by partnering with other stakeholders
  Promote the efficient use of FAA resources:
    Development, maintenance and distribution of well recognized tools, data and standards
  Promote standardization in methods and data through industry-wide tools and resources (e.g., MMPDS, NASGRO)
  Maintain FAA knowledge base to assess and ensure the long-term airworthiness of existing and next generation aircraft structure

## Slide 5: SIM Program Overview
SIM Benefits/Output: Data and analytical tools that support rulemaking, policy and guidance development, aircraft certification, continued airworthiness, certification compliance, education and training
  Rulemaking (e.g., WFD RAMs Survey)
  Guidance Material (e.g., AC 25.629, Structural Health Monitoring TBD)
  Certification
    New materials (e.g., Bombardier C-Series, Airbus A380 and A350 use of Aluminum Lithium)
    Special Conditions
    Active Flutter Suppression System for B747-8/8F
  COS: Bonded Repair – (e.g., Boeing Commercial investigating usage –MD80 AD repair); Structural Health Monitoring
  Standardization:
    MMPDS (Draft AC 20.613, MMPDS-X: e.g. Additive Manufacturing, Advanced Joining Methods (FSW), New Alloys (Al-Li), etc.)
    NASGRO

## Slide 6
SIM-TCRG Research Portfolio
Assess and ensure the long-term airworthiness of existing aircraft structure
Efficient use of FAA resources: maintenance and distribution of tools, data and standards
Emerging Technologies
Aluminum Lithium
Bonded Repair Technology
Emerging Metallic Structures R&D
Active Flutter Suppression
Advanced Metallic Fuselage Structure
SMS/TARAM Risk Methods for COS
Risk Management for Small Airplanes
RAM Survey for WFD
Continued Operational Safety
Safety Regulations & Standards
MMPDS (MIL-HDBK-5) –
[addressing changes in technology]
NASGRO
Property Standards Emerging Materials
Ongoing: FY14
Near Term: FY15
Future Plan: FY16
Operational Safety
Airworthiness Assurance
In-House Programs
Full-Scale Aircraft Structural Test Evaluation and Research (FASTER)
FAA-Drexel Fellowship Program
Prepare for new technologies
Outputs
Rulemaking
Regulatory Guidance
Policy
Certification
TARAM data
MMPDS
Research infrastructure

## Slide 7: SIM Program In-House Capabilities
People: 2 FTEs
Laboratories :
  Full-Scale Aircraft Structural Test Evaluation and Research (FASTER) Lab
  Material Characterization Lab
  Support:
    HIASUN: 2 Engineers and 2 Technicians
    FAA-Drexel Fellowship: Fellowship students and access to Drexel facilities
Fuselage Panel Test
Material Characterization
Fractographic Examinations
Notes: In this slide the sponsor and provider, describe how the research in the program area is supported by people, labs, and partnerships. Describe, where applicable, collaborations with other government agencies and Centers of Excellence. Note that partnerships are where two or more organizations carry on a joint venture in which each brings resources to the table and shares in the risk of the venture. A relationship in which the FAA solely provides resources to an organization that then performs the research for the FAA is not a partnership.
People should include FAA personnel and the current contractors, both those working in the FAA laboratories and off site. Present how Aviation Safety RE&D resources are being spread, and who is actually doing the research.

## Slide 8: SIM Program Partnerships
    Boeing: Bonded Repairs
    NASA: Aluminum-Lithium and NASGRO
    Navy: MMPDS and Aluminum-Lithium
    Bombardier: Aluminum-Lithium
    Constellium: Aluminum-Lithium
    Delta Air Lines: Structural Health Monitoring
    MMPDS Industry Steering Group (ISG): Consortium of 22 major material users and suppliers worldwide
ISG
Material
Users
Suppliers
Notes: In this slide the sponsor and provider, describe how the research in the program area is supported by people, labs, and partnerships. Describe, where applicable, collaborations with other government agencies and Centers of Excellence. Note that partnerships are where two or more organizations carry on a joint venture in which each brings resources to the table and shares in the risk of the venture. A relationship in which the FAA solely provides resources to an organization that then performs the research for the FAA is not a partnership.
People should include FAA personnel and the current contractors, both those working in the FAA laboratories and off site. Present how Aviation Safety RE&D resources are being spread, and who is actually doing the research.

## Slide 9: List of FY16 Requirements
9
No. | Title | Status
A11E.SIM.1 | Risk Assessment and Risk Management Methods for Small and Transport Airplane COS | Follow on
A11E.SIM.3 | Emerging Technology – Active Flutter Suppression | New
A11E.SIM.4 | Metallic Materials Properties Development and Standardization (MMPDS) | Follow on
A11E.SIM.5 | Damage Tolerance and Durability Issues for Emerging Technologies | Follow on
A11E.SIM.6 | Probabilistic Approach to Detecting Fatigue Damage Before Developing an Unsafe Condition | Follow on

## Slide 10: Risk Assessment and Risk Management for Small and Transport Airplane COS (A11E.SIM.1)
Research Requirement
Description: Provide probabilistic input data and methodology for calculating risk due to fatigue cracking in small and transport airplanes.
What is research question: What data is needed and available to successfully implement the risk analysis requirements
How is requirement answering question: Collect and develop data needed to assess risk due to structural fatigue in small and transport airplanes.
Sponsor POC: Michael Reyer (ACE-113)
Performer POC: Ed Weinstein and John Bakuckas (ANG-E281)
Annual updates to NASGRO analysis and database
FY 14 Database of small airplane fatigue characteristics, Phase IV data from component testing
FY 16: Prototype fatigue management programs (control programs) using probabilistic data and software tools
FY15: Survey Findings Report - Document damage reported from actual transport airplane service history (maintenance records, inspection records, tear-down reports, accident/incident reports, service difficulty reports, etc.).
Outputs
Out Year Funding Requirements
Outcomes and Implementation
Outcomes:
  Improved process for calculating risk associated with continued-operational-safety (COS) issues
  Optimize FAA resources:
    Assess and approve data submittals
    Respond to safety issues
    Improved confidence in data for decision-making
Implementation:
  Revised AC 91-82A (FY 17)
  Revised AC 23-13A (FY 17)
  Revised Small Airplane Risk Analysis Handbook (FY 14)
For use by Aviation Safety Engineers (ASE) performing or overseeing transport-airplane risk analysis as part of the Order 8110.107, Monitor Safety – Analyze Data
FY14 | FY15 | FY16 | FY17 | FY18
$500K | TBD | $200K | TBD | TBD
Notes: Purpose: Develop a standardized COS risk assessment method for small and transport airplanes consistent with the AIR safety management principles, with emphasis on materials, loads, and fatigue
Why It’s Needed: The general aviation (GA) fleet includes about 150,000 airplanes that were certificated with no fatigue evaluation requirements, with an average age of about 40 years, and little information exists regarding airworthiness limitations for this aging GA fleet.
Outputs: A database of loads data specific to GA airplane design and operations, and develop risk assessment/management tools and software based on probabilistic techniques to aid in COS decision making
Links: AVS SG #3 System Safety Management
AIR Continuing Airworthiness

## Slide 11: Emerging Technologies - Active Flutter Suppression (A11E.SIM.3)
11
Outputs
Outcomes and Implementation
Research Requirement
Out Year Funding Requirements
Description: Prepare for implementation of Active Flutter Suppression (AFS) in commercial aircraft.
What is research question: What technical, philosophical, certification, and compliance issues does AFS pose the FAA and industry.
How is requirement answering question: Will determine to what extent AFS is appropriate for transport category airplanes, and how to safely implement this emerging technology via new regulatory requirements & guidance.
Sponsor POC: Ian Won and Carl Niedermeyer (ANM-115)
Performer POC: Dave Westlund and John Bakuckas (ANG-E281)
Revise § 25.629, “Aeroelastic Stability Requirements”
Update AC 25.629-1A, “Aeroelastic Stability Substantiation of Transport Category Airplanes”
Policy Statement?
Special Conditions?
Review flutter and aeroservoelastic research involving AFS, including Military application of the technology.
Predictive analysis and test of USAF/NASA “MAD” X-56A aeroelastic (flutter) UAV with an AFS system installed.
Determine applicability of existing regulations and need for additional requirements.
Develop regulatory guidance material specific to compliance of AFS to existing regulatory requirements.
By FY 2019, develop technical data to assess methods to preclude and suppress flutter
Leverage resources through Multi-Utility Aeroelastic Demonstration Program (MAD):
  USAF
  NASA
  Lockheed Martin
FY14 | FY15 | FY16 | FY17 | FY18
 |  | $500K | $500K | $500K
Notes: Requirement Description: This multi-year requirement prepares for the use of new technologies that optimize airplane design, improve operational safety, ensure continued airworthiness, and prevent and mitigate accidents. This research would be focused on the conventional type of Transport Category airplanes that are being designed today and in the near future. Much of the research that has been done to date has been aimed at High Speed Civil Transport (HSCT) designs which are not economically viable (nor environmentally viable) at this time due to their near sonic or supersonic cruise speeds.
The next generation of transports will utilize advanced Fly-By-Wire (FBW) technology that will be capable of providing Active Flutter Suppression (AFS) to reduce the impact of flutter requirements on the airplane design. The introduction of AFS systems requires the evaluation of: 1) relevant technical issues, 2) certification requirements and compliance issues, and 3) philosophical issues dealing with the application of this technology to commercial transports.
The FAA needs to maintain a proactive role and be involved with industry as they introduce AFS systems in the next generation of advanced transport airplanes. Data is needed to allow the FAA to develop new regulations and to adjust regulatory guidance as needed to preserve current aviation safety standards.
Sponsor Outcome: Assess the viability of analytical and experimental tools, ensure the effectiveness and reliability of AFS systems, and identify the need for new certification requirements and regulatory guidance material to preserve current aviation safety standards
Description of Work: This requirement will leverage resources with other stakeholders, in particular, NASA and USAF in the X-56A multi-utility aeroelastic demonstrator (MAD) program. This is multi-year level of effort with following phases:
Phase 1. Develop Active Flutter Suppression (AFS) Research Plan: Determine the current state of AFS through surveys, interviews with airplane manufactures and operators, and discussions with technology developers. Review flutter and aeroservoelastic activities involving AFS including Military application of the technology. Using the results from the survey and analysis, identify R&D tasks that need to be carried out to provide the necessary technical information to enable the FAA to evaluate and assess AFS technologies for compliance with certification and continued airworthiness requirements. Establish partnerships with NASA and USAF (FY13)
Phase 2. Execute Near-Term Tasks of the AFS Research Plan: (FY13-15)
Phase 3. Summarize Results and Submit Data: Provide data to allow for the review of pertinent regulations and guidance material, and prepare recommendations, it needed, for new, modified, or otherwise improved criteria. (FY16)
  Product/Output will be final reports submitted to sponsor after each task that summarizes results from test and analysis; used to determine the adequacy of existing regulations.

## Slide 12: Metallic Materials Properties Development and Standardization (MMPDS) (A11E.SIM.4)
12
Outputs
Outcomes and Implementation
Research Requirement
Out Year Funding Requirements
Description: Provide standardized acceptable design and certification compliance data and tools necessary to enable the FAA to operate efficiently.
What is research question: What guidance material and data is available to comply with requirements for material properties and design values (§§ 25.603, 25.605, 25.613)
How is requirement answering question: Leverage resources (shared funding) with government / industry organization to develop statistically based allowables required by CFR
Sponsor POC: Mark Freisthler (ANM-115), Jim Kabbara (AIR-120)
Performer POC: John Bakuckas (ANG-E281)
Promote uniform level of safety in developing and maintaining safety standards through a widely recognized government/industry organization
Optimize FAA resources:
  Assess and approve data submittals
  Respond to safety issues
  Improved confidence in data for decision-making
  MMPDS is referenced is practically every certification project involving metallic structure.
Draft AC 20.613
Address new materials and processes
FAA involvement/leadership means FAA acceptance of published design values (14 CFR 2x.613 compliance)
MMPDS Handbook Revision
  4 to 5 new design values (e.g. Al-Li 2196 and 2198)
  Re-evaluation of properties of existing alloys and fastener design allowables
  Industry generated data
Commercial distribution of Handbook and products
  Electronic databases
  Website access
Guidance, technical information and data:
  Design allowables that satisfy CFR
  Standardized/Acceptable statistical methods
Anticipate Continued External Funding Sources (FY14):
  Industry Steering Group (+$200K)
  Commercialization ($90K)
  Government Steering Group ($55K Navy)
60-70% funded by Industry and other gov’t resources
FY14 | FY15 | FY16 | FY17 | FY18
$125K | TBD | $125K | $125 | $125K
Notes: Requirement Description: Standardized acceptable design and certification compliance data and tools necessary to enable the FAA to operate in cost effective and efficient manner, while providing a level-playing field and uniform standards for all certification agents. This requirement leverages FAA resources through government – industry consortia in the development of the Metallic Materials Properties Development and Standardization (MMPDS) handbook, recognized worldwide as the premier source of metallic allowables. As part of the FAA’s charter to maintain international leadership role, support of MMPDS supports commitments to standardize and maintain metallic material and joint design properties on which aerospace industry depends.
This requirement also allows the FAA to better support the introduction of new metallic materials and joining process (e.g., Aluminum Lithium, laser additive materials, friction stir welding, GLARE, fiber-metal laminates, and metal matrix composites). For these emerging materials, research is being conducted under the Damage Tolerance and Durability Issues for Emerging Technologies requirement to define required specification controls and identify key material properties needed for design. Once identified and agreed to, the material properties will be published and maintained under this requirement, MMPDS.
Sponsor Outcome:
      • Provide uniform level of safety in developing and maintaining safety standards through a widely recognized government/industry organization
      • Optimize FAA resources:
      - share resources with other government organizations and industry
      - assess and approve data submittals
      - respond to safety issues
      - improved confidence in data for decision-making
Implementation Plan: Implement through certification policies and guidance. Several policy memos (AIR-1 2000, AVS-1 2003, AIR-100 2006) and Advisory Circular (AC-25-613-1) have been issued recognizing the MMPDS as an essential source for design values which support certification and continued airworthiness of aviation products. These policy memos also cite the importance of the FAA’s leadership role in the continued operation of the MMPDS. A new Advisory Circular AC 20.613-xx is currently in work for FAA wide implementation of MMPDS.
Description of Work: Provide for the planning, coordination, and implementation activity which is necessary to maintain the MMPDS Handbook as the source for design allowables and related information needed for aerospace vehicle design, certification and continued airworthiness. The effort includes: an assessment of the design data requirements of the aerospace industry; liaison with appropriate Government agencies, military services, aerospace contractors, and metallic material and mechanical fastener suppliers; collection of data; and statistical analysis of data to determine design allowable properties.
      • Fall and Spring Coordination Meetings
      • Meeting Agenda and Minutes
      • MMPDS Handbook and Derivative Products
Support task from SIM-15-5:
Material Property Standards for Emerging Materials. The purpose of this task is to coordinate with industry through the MMPDS steering and working groups, to develop processes and procedures which would allow the publication of design information relevant to “highly process dependent” metallic materials, (e.g., laser additive materials, electronic beam additive materials, GLARE, etc.). For the purpose of this task “highly process dependent” refers to materials which a manufacturer cannot purchase in stock form from an outside supplier, but are created by a manufacturer from one or more constituent materials. For these materials current industry material and heat treatment specifications may not be adequate descriptors for of these material forms.
    Phase 1: Develop Guidelines for Inclusion for Emerging Materials, FY13-14: Develop procedures and guidelines for establishing design values for these highly process dependent materials
    Phase 2: Develop Guidelines on the Use of the MMPDS Handbook, FY15-17: Develop guidance for user for using data provided in Phase 1

## Slide 13: Durability and Damage Tolerance Issues for Emerging Technologies (A11E.SIM.5)
13
Outputs
Outcomes and Implementation
Research Requirement
Out Year Funding Requirements
Description: Address certification and continued airworthiness issues arising from the use of emerging technologies including advanced materials, construction and repair methods, and production and health monitoring technologies
What is research question: What is the durability and damage tolerance performance of emerging technologies
How is requirement answering question: Leverage resources to generate fracture and fatigue data to ensure safe implementation of emerging technologies in aircraft products
Sponsor POC: Ian Won and Mark Freisthler (ANM-115)
Performer POC: John Bakuckas (ANG-E281) and Paul Swindell (ANG-E282)
Ensure safe and efficient implementation of new technologies in new aircraft products (e.g., Bombardier C-series, Lear Jet)
Enable the use of new technologies that improve operational safety, ensure continued airworthiness, and prevent and mitigate accidents (incl. SHM)
Final reports, data, analytical tools, and guidance material that support Aircraft Certification, Continued Airworthiness, and Education and Training
Provide technical information supporting the development of policy memos and other rulemaking activities
Implementation - MMPDS
Data to allow FAA to assess relevance of existing regulations and to adjust regulatory guidance to preserve current aviation safety standards:
FY14, Develop technical data to assess the application of advanced aluminum-lithium alloys for aircraft primary structure
FY15-FY16, In partnership with Boeing, develop capabilities for full-scale testing of wing structure
FY16, Develop technical data to assess the fatigue and environmental durability of bonded repairs to metallic structure
FY16, Complete proof-of-concept structural health monitoring (SHM) certification project
FY17, Develop property standards for emerging process intensive materials
FY18, Conduct test on an advanced metallic fuselage structure to access durability and damage tolerance of emerging technologies including unitized welded structure, new metallic alloys, and hybrid bonded construction.
Anticipate Continued External Cost-Share:
  Boeing (350K in FY14) (Bonded Repairs)
  Bombardier and Alcan (Al-Li)
  NASA (Al-Li and Emerging Materials)
  Delta Air Lines (SHM)
  Alcoa (Advanced metallic fuselage)
Note: FASTER Lab and FAA-Drexel Fellowship Cost Included
FY14* | FY15 | FY16 | FY17 | FY18
$1050K | TBD | $1435K | $TBD | $TBD
Notes: Requirement Description: This requirement addresses certification and continued airworthiness issues arising from the introduction of emerging materials and construction methods (e.g, friction stir welding, advanced metallic alloys and hybrids, metallic fatigue enhancement processes such as laser peening, fiber-metal laminates, bonded structure) which industry is seeking to use for aircraft structures in new fatigue critical applications. In order to insure that the regulations and guidance stay current the FAA needs to maintain a proactive role and stay informed of potential applications as industry introduces advances in materials and new fabrication and construction methods. Data is needed to allow the FAA to assess the continued relevance of existing regulations, impose additional safety standards (via Special Conditions/rulemaking), and provide additional regulatory guidance (advisory materials/policy memorandums) as needed to maintain the current level of safety afforded by the existing airworthiness standards. This requirement cuts across wide areas of metallics, metallic hybrids (metallic/composite construction), metallic construction and processing, inspection/monitoring methods, and therefore will be coordinated with the SIC and M&I TCRGs. This requirement leverages FAA resources with other government agencies and industry through cooperative research and development agreements.
Sponsor Outcome: This requirement would enable the use of new technologies that improve operational safety; reduce design, production, and operating costs; support maintenance of continued airworthiness; and prevent and mitigate accidents. The requirement will also ensure the safe and efficient implementation of new technologies in aircraft products.
Implementation Plan: Implement through certification of new products (e.g., issue papers, equivalent safety findings, etc.), rulemaking (e.g., special conditions) and development of regulatory guidance material (e.g., policy memorandums, advisory circulars). Partner with manufacturers to ensure the fatigue and residual strength performance of new material systems is well understood prior to introduction into service through fracture mechanics test and analysis. The sponsor plans to use the outputs from this research for the development of rulemaking, regulatory guidance, and industry standards.
Description of Work: There are several task areas and phases to this multi-year requirement. The FAA’s FASTER Facility is a primary mechanism to leverage resources with other stakeholders including NASA, DoD, and industry partners (e.g., Boeing, Bombardier, etc.). The following six activities are being undertaken:
Emerging Metallic Structures Technology (EMST) Roadmap: Develop a 10 year research and development (R&D) plan addressing EMST for transport airplanes defining metrics, milestones and project phases. In developing the roadmap, a survey will be conducted to summarize the advanced metallic materials, new fabrication and construction methods being introduced by manufacturers in upcoming products. The roadmap will identify R&D tasks and priorities that need to be carried out to provide technical data that will enable the FAA to support industry introduction of new technologies supporting compliance with existing and new certification and continued airworthiness requirements. The roadmap will document technical approaches, the scope and objectives of each major task area, allow prioritization of research activities, schedule of milestones and deliverables, and outline partnerships to leverage resources with industry and other government stakeholders. Complete final version of roadmap which was initiated in FY13.
Bonded Repair Technology: In a cost-share partnership with Boeing, address safety and structural integrity issues of bonded repair technologies using the FAA’s FASTER facility The current project phases include the following phases:
  Phase 1 (Complete, FY08-FY10): Baseline fatigue and residual strength performance of bonded repairs of metallic fuselage structure : Generated data to calibrate analytical tools used to design bonded repairs on damaged aircraft structure. Demonstrated that a properly designed and installed repair patches are durable and capable of containing large damage (2-bay crack with central stiffener severed) under extreme loading conditions in excess of ultimate load requirements.
  Phase 2 (Complete, FY10-FY12): Effect of repair deficiencies on fatigue performance of bonded repairs: Utilized under designed, flawed and weakened patches to permit damage growth: cracks and disbonds. Explored the application of prototype Structural Health Monitoring (SHM) and commercially available Non-Destructive Inspection (NDI) systems to determine repair integrity. Demonstrated: 1. Reduced fatigue performance as repair patch quality degrades; 2. Capability of a prototype SHM system to reconstruct crack growth history; and 3. Capability of under designed repairs to contain impact damage after 20,000 cycles.
  Phase 3 (Ongoing, FY12-FY15): Effects of environment on durability and damage tolerance: Conduct studies of environmental effects on the durability of bonded repairs. Identify potential gaps in regulatory guidance and requirements to support introduction into service. The following activities are being conducted:
    FY12-13: Develop Test Plan and Modify Fixture
    FY13-15: Conduct static and fatigue tests of bonded repairs subjected to mechanical-temperature-humidity loading profiles. Monitor durability and fatigue performance.
    FY16: Summarize Results and Submit Data
  Product/Output will be final reports submitted to sponsor after each task that summarizes results from test and analysis; used to determine the adequacy of existing regulations in preserving safe airframe designs incorporating bonded repair technology.
Assess the Properties of Advanced Aluminum-Lithium (Al-Li) for Primary Structure: This task serves as an independent assessment of durability and damage tolerance capabilities of 2196 and 2198 Al-Li being considered by Bombardier for the fuselage of their new C-Series aircraft. The purpose is to assess the unique mechanical properties of advanced aluminum-lithium alloys when used for airplane primary structure. This task is leveraging resources and using the expertise of several organizations including Constellium, Bombardier, NASA, Navy and UDRI to assess several properties including static properties, fatigue life and fatigue crack growth performance, corrosion resistance, as well as the damage and durability aspects of latest generation aluminum lithium alloys. It is not the intent of this plan to develop any MMPDS published allowables, but only to develop the knowledge base to ensure the safe implementation and application of Al-Li material for airplane primary structure. The following activities are being conducted:
    Phase 1, FY11-12: Conduct a survey and develop a test plan
    Phase 2, FY12-14: Conduct tests
    Phase 3, FY14: Summarize results and submit data
  Product/Output will be final reports submitted to sponsor after each task that summarizes results from test and analysis; used to determine the adequacy of existing regulations in preserving safe airframe designs incorporating aluminum-lithium
Material Property Standards for Emerging Materials. The purpose of this task is to coordinate with industry through the MMPDS steering and working groups, to develop processes and procedures which would allow the publication of design information relevant to “highly process dependent” metallic materials, (e.g., laser additive materials, electronic beam additive materials, GLARE, etc.). For the purpose of this task “highly process dependent” refers to materials which a manufacturer cannot purchase in stock form from an outside supplier, but are created by a manufacturer from one or more constituent materials. For these materials current industry material and heat treatment specifications may not be adequate descriptors for of these material forms.
    Phase 1: Develop Guidelines for Inclusion for Emerging Materials, FY13-14: Develop procedures and guidelines for establishing design values for these highly process dependent materials
    Phase 2: Develop Guidelines on the Use of the MMPDS Handbook, FY15-17: Develop guidance for user for using data provided in Phase 1
  Product/Output: Final report used and referenced by the FAA advisory material or policy memos regarding data used in title CFR parts 23/25/27/29.603, 605 and 613. It is the intention of the FAA to incorporate procedures and guidance developed by this task into the MMPDS, or in supplementary documents maintained by the MMPDS organization.
Advanced Metallic Fuselage Structure: In partnership with industry, conduct a full-scale test on an advanced metallic fuselage structure to access durability and damage tolerance of emerging technologies including unitized welded structure, new metallic alloys (Aluminum Lithium), and hybrid construction. Verify new analytical tools and generate data to support certification, and continued airworthiness of these emerging materials, structures and fabrication methods. Explore applicable inspection methods including integrated Structural Health Monitoring (SHM). Data is needed for these emerging technologies include: 1. Multiple load path (concern with reduced damage tolerance); 2. Crack arresting features (concern with reduced fatigue performance); 3. Identifying damage containment features; 4. Selective reinforcement with fatigue-insensitive material; and 5. Identify applicable NDI and SHM This requirement will leverage resources with SIC and M & I TCRGs and other government and industry stakeholders in a planned four year level of effort. Anticipate industry partners with NIAR, ALCOA, ALCAN, and an OEM. The following activities are planned:
    Task 1: Conduct, survey, develop test plan and establish partnerships, FY14
    Task 2: Conduct coupon level test and analysis by performing organization(FAA and TBD). Fabricate full-scale panels to be tested, FY14-FY15
    Task 3: Conduct full-scale panel tests in FASTER lab, FY16-FY18
    Task 4: Summarize results and submit data, FY19
  Product/Output will be final reports submitted to sponsor after each task that summarizes results from test and analysis; used to determine the adequacy of existing regulations in preserving safe airframe designs incorporating emerging metallic technologies, construction and hybrids
Structural Health Monitoring (SHM) - Provide data needed by AVS to allow assessment of the state of SHM in commercial transport airplanes for NextGen applications including fatigue monitoring and condition based maintenance. This includes analysis and experiments for determining the ability of proposed SHM systems to perform structural diagnosis and prognosis. Includes all types of structures made from conventional metals and advanced materials. This requirement will leverage resources with other gov’t, and industry stakeholders in an anticipated 6 year level of effort . In particular the following phases will be undertaken:
    Phase 1: Working with the Aerospace Industry Steering Committee (AISC) for SHM, develop a SHM R&D roadmap for transport airplanes. The roadmap will identify R&D tasks that need to be carried out to provide technical data that will enable the FAA to evaluate and assess SHM technologies for compliance with existing and new certification and continued airworthiness requirements. In particular, the roadmap will document technical approaches, the scope and objectives of each major task area, schedule of milestones and deliverables, and outline partnerships to leverage resources with industry and other government stakeholders. FY11.
    Phase 2: Execute Near Term Research as defined in the Roadmap. Assess candidate SHM technologies scheduled to be implemented in the near term on legacy aircraft and upcoming products. This includes developing Operator-OEM-Regulator team and leverage resources in proof-of-concept SHM certification project. FY12-16.
  Product/Output will be final reports submitted to sponsor after each task that summarizes results from test and analysis; used to determine the adequacy of existing regulations in preserving safe airframe designs incorporating this technologies.

## Slide 14: Probabilistic Approach to Detecting Fatigue Damage Before Developing an Unsafe Condition (A11E.SIM.6)
14
Outputs
Outcomes and Implementation
Research Requirement
Out Year Funding Requirements
Description: Provide data input to assess airplane structure fatigue problems using Transport Airplane Risk Assessment Methodology (TARAM). Inputs includes good estimates of ND: Conditional probability that an occurrence of a defect will not be detected before becoming unsafe.
What is research question: What are guidelines and data needed to accurately estimate ND.
How is requirement answering question: Conduct survey to collect in-service cracking issues from actual airplane service history and develop guidelines on using data to estimate ND
Sponsor POC: Ian Won and John Craycraft (ANM-115)
Performer POC: John Bakuckas (ANG-E281)
Update to Transport Airplane Risk Assessment Methodology (TARAM) Handbook, AIR-100.
Improved process for calculating risk associated with continued-operational-safety (COS) issues
For use by Aviation Safety Engineers (ASE) performing or overseeing transport-airplane risk analysis as part of the Order 8110.107, Monitor Safety – Analyze Data
Survey Findings Report, FY15: Document damage reported from actual airplane service history (maintenance records, inspection records, tear-down reports, accident/incident reports, service difficulty reports, etc.).
Address sparse data issues that affects the ability to successfully implement the risk analysis requirements
Improved method to determine input data needed for TARAM risk assessment
FY14 | FY15 | FY16 | FY17 | FY18
 |  | $150K | TBD | TBD
FY14 and FY15 funding through A11E.SIM.1
Notes: 1 Objective
The objective of this work is to conduct research that results in data and guidance to support engineers as they make estimates of an important conditional probability of not detecting (ND) airplane structural fatigue damage that is used in the risk analysis for airplane structure fatigue issues. The early stages of this research will, as needed, lead to recommendations for subsequent stages.
2 Background
The risk analysis process for transport category airplanes is the Transport Airplane Risk Assessment Methodology (TARAM). TARAM defines a process for calculating the risk of transport airplane type design safety issues. It applies to all engineering disciplines, e.g., flight controls, structures, etc.
One of the parameters used in the TARAM analysis of an airplane structure fatigue issue is ND, which is the conditional probability that an occurrence of the defect (fatigue crack) will Not be Detected (ND) before the defect leads to an unsafe outcome (airplane accident). There is a tendency for analysts to be extremely conservative in their estimates of ND. Since the calculated risk is directly proportional to ND, large errors in estimating ND will lead to large errors in the calculated risk. The calculated risk values are used to make safety decisions and to determine acceptable compliance times. Excessively conservative values for ND could lead to unnecessary ADs and/or ADs with unnecessarily aggressive compliance times. This is contrary to the intent of a TARAM risk analysis, which is to provide the best estimate of what the risk actually is and base safety decisions and risk management on the actual risk.
Historically the overwhelming majority of all fatigue cracks are discovered before they lead to an accident. This is indicative that ND is typically orders of magnitude less than 1. Many of the cracks are not found by a directed inspection looking for that particular crack, but are instead incidentally discovered during normal operation and routine maintenance. These incidental discoveries are an important source of safety which should be recognized in the risk analysis by the numerical value assigned to ND.
3 Purpose and Scope
The purpose of this Statement of Work (SOW) is to obtain data and guidance in the estimation of ND for airplane structure fatigue problems that require TARAM risk analysis. The scope is limit to primary structure of transport category airplanes. Secondary structure is specifically excluded from this research
4 General Requirements
  Monthly Progress Reports: A monthly progress will be submitted on the 20th day of each month summarizing the previous month’s progress, status, problems encountered and anticipated accomplishments.
  Quarterly Project Meetings: Quarterly Project Review Meetings will be held to discuss project status, accomplishments, findings, technical issues, and planned activities.
  Final Review Meeting: At the completion of the period of performance, a final review meeting will be held to summarize all the work performed.
5 Technical Tasks
The research covered under this SOW shall involve a base program and an optional program. Under the base program, an estimate of ND based on actual in-service cracking issues will be made. The optional program would focus on applications and properties not adequately covered in the base program as outlined in Section 8. The following lists the technical tasks for the base program covered in this SOW
Task 1. Detailed Work Plan: A Detailed Work Plan (DWP) shall be developed in coordination with the FAA outlining responsibilities of participating organizations, scope and objectives of each major task area, schedule, and expected results will be developed. In developing the DWP, a background section should be included that outlines the TARAM risk assessment methodology and limitations. A Gantt chart showing all tasks and milestones will be included and shall be updated by the performer through out the period of performance of the contract. The detailed work plan address the formal proposal requirements as outlined in this SOW.
  Deliverables: One month after contract award (MACA), a written Detailed Work Plan (DWP) per Task 1. The DPW will be presented at a Kick-off meeting with FAA sponsors.
Task 2. In-Service Damage Survey: A survey shall be performed to collect and document damage reported from actual airplane service history (maintenance records, inspection records, tear-down reports, accident/incident reports, service difficulty reports, etc.). This includes documenting crack size, distribution, location and flight cycles and flight hours from an in-service issue. For each in-service issue, record how many cases of crack findings there are, crack lengths found, airplane age (flights or flight-cycles), how often is the area visible, how was the crack discovered and other data as deemed appropriate. Each occurrence identify the airplane make and model, as well as the structure name and location on the airplane.
  Deliverables: A written Survey Report with a record of all references and data.
Task 3. Data Analysis to Determine ND: Provide a list of in-service crack issues of primary structure to be analyzed based on available information. For each issue listed, make an estimate of the time (in flights or flight-hours) to grow from the observed crack to an estimate of the accident critical damage size. It should be recognized that accident critical damage size is not the same as the limit load critical crack length that is used in certification damage tolerance analysis, but rather it is a bit longer and more extensive. The analysis shall determine and use an appropriate and rational means to account for the reduction of ND from the additional time to detect the observed damage, had it been undiscovered, before it could lead to an accident (cracks vary significantly in the probability of their discovery before an accident). The main output would be an estimate of the overall average ND of all primary structure cracking issues analyzed.
  Deliverables: A written Data Analysis Report to Determine ND.
Task 4. Final Report: Submit a written a report of the findings and recommendations. Included in the final report will be a section containing data and guidance that a working FAA engineer can use to estimate ND for the structure fatigue issue under analysis. The data to estimate ND could be presented in the form of tables, flow charts, equations or graphs, or other devices as deemed adequate and useful, or combinations thereof. In preparing this section the consider and use the appropriate use level of complexity that is needed to make an adequate estimate of ND. Some possibilities to consider are aircraft zone, structure type (wing, fuselage, landing gear, etc.), sub-assembly type (skin, frame, beam, lug, etc.), structure material, type of fatigue loading, wide spread fatigue damage susceptibility, single or multiple load path, damage tolerant or safe-life structure, etc.
  Deliverables : Three months prior to the end of the contact, a draft final report will be submitted summarizing Task 2-3. The FAA will review and provide feedback in final review meeting two months prior to the contact end date. The final report will be submitted one month
6 Schedule
The total period of performance for the base program defined in this statement of work shall be 36 months after the date of the contract award