## Slide 1: COLLINS AEROSPACE Update on SatVoice Implementation
April 2023
Prepared for ISPACG

## Slide 2: SatVoice one stage dialing
Implementation update
Collins Aerospace has been implementing a closed-loop Voice over IP network to support implementation of SatVoice one-stage dialing in U.S. Airspace for Air Traffic Services
The network is intentionally diverse from the Collins datalink infrastructure to ensure diversity from FANS
The system uses the Session Initiation Protocol (SIP) for call setup and telephony signaling, a widely used telephony protocol but configured to include octal and priority call elements

## Slide 3: Results
Initial results – lab testing
  Audio latency reduced about 10% from 0.89 sec to 0.80 sec
    Observed during testing w/Inmarsat. Iridium testing is forthcoming.
  GtA call setup time reduced from 20 sec to < 1 sec
    PSTN setup was observed from 2019 Pacific Voice Trials

## Slide 4: One stage dialing - Current state
SIP Core
Annapolis, MD
Islip, New York (NYC)
Comm Center
Verizon
Livermore (SFO)
Comm Center
New York
Tempe 1
Inmarsat
Iridium

## Slide 5: One stage dialing - future state
SIP Core
Annapolis, MD
Telco 2
Islip, New York (NYC)
Comm Center
Verizon
Livermore (SFO)
Comm Center
Amsterdam
New York
Tempe 1
Tempe 2
Inmarsat
Iridium

## Slide 6: Phase I Trials
FedEx over Inmarsat callback checks
  Iridium equipped aircraft to be added in the future
Callback checks only, no ATC
Test short codes map to VoIP network
  Live short codes continue routing through PSTN
Objective is to exercise the system and collect hundreds or thousands of calls
Single server at Collins core, single network connections to core nodes
Success criteria to move to Phase II?
  No unresolved trouble tickets
  Number of one-stage calls? AtG, GtA, Iridium/Inmarsat?

## Slide 7: Phase II Trial
(Under Development)
Limited ATC use authorized by FAA for ATC to a limited number of trial participants
Callback check in conjunction with SELCAL check and HF frequency assignment
Use test short code or move operation short code to SIP?
Success criteria to move to go-live
  Collins has redundant SIP services at Annapolis core
  All core nodes have redundant network connections
  No unresolved trouble tickets
  Number of calls