## Slide 1
Presented by: Federal Aviation Administration
THE THIRTY-SEVENTH MEETING OF THE
INFORMAL SOUTH PACIFIC ATS CO-ORDINATING GROUP (ISPACG/37)
FANS Interoperability Team Meeting
(FIT/30)
Papeete, Tahiti
26 April 2023
FAA PBCS Monitoring Updates
Oceanic Data Link

## Slide 2: Overview
Analysis of performance issues observed by media delivery path
Summary of monthly aircraft monitoring results for 2023
Conclusions

## Slide 3: Performance by message delivery path – observed below 95%
FAA-Oakland Reporting on ADS-C Actual Surveillance Performance (ASP) |  |  |  | 
Period: July to December 2022 |  |  |  | 
Color key: |  |  | 95% RSP 180 Benchmark | 99.9% RSP 180 Benchmark
Meets criteria |  | Message Counts | ASP | ASP
99.0%-99.9% |  |  | <=90 sec | <=180 sec
Under criteria |  |  |  | 
Message Delivery Path ID Media Type |  |  |  | 
AOE6 | SAT | 708 | 92.66% | 95.20%
XXN | SAT | 1324 | 90.94% | 95.47%
OTH | VHF | 4678 | 94.44% | 98.35%
STS7 | VHF | 4055 | 92.73% | 96.23%
STS8 | VHF | 2145 | 92.54% | 95.90%
UIL8 | VHF | 494 | 93.93% | 99.80%
H01 | HF | 1334 | 54.42% | 69.19%
H02 | HF | 3144 | 60.75% | 74.68%
H05 | HF | 200 | 57.00% | 73.50%
H09 | HF | 187 | 63.10% | 76.47%
H10 | HF | 113 | 40.71% | 54.87%
H16 | HF | 401 | 58.35% | 69.83%

## Slide 4
Satellite Service Provider (SSP) | Satellite | Service | Ground Station Location | ARINC ACARS Identifiers | SITA ACARS Identifiers
Inmarsat | AORE (3F5 at 54°W) | Classic Aero | Burum, Netherlands | XXN | AOE6

## Slide 5: NAT OPS Bulletin 2019_003 Rev 1 Data Link Performance Improvement Options
Maximizing access to the Classic Aero Ground Earth Station (GES) services:
In the Inmarsat SATCOM system, there are a multitude of transmission paths available via the different ground stations and satellites. If one path fails, the aircraft may be able to switch to an alternate path provided the Operator Requirement Table (ORT) in the SATCOM terminal is correctly configured.
Proper configuration of the ORT table is therefore vital for maximizing availability of SATCOM services.
Below are some links to the SATCOM manufacturers' information portals:
  Cobham: https://sync.cobham.com/satcom/
  Honeywell: https://myaerospace.com/
  Thales: https://www.thalesgroup.com/en/customer-online
  Rockwell Collins: https://www.shopcollins.com

## Slide 6: PBCS monitoring – aircraft report
Airspace: Oakland |  |  | 
Monitoring period: | Jan 2023 | Feb 2023 | Mar 2023
Total aircraft observed using data link​ | 3590 | 3550 | 3479
Have 100 or more ADS-C downlink reports and/or CPDLC transactions​ | 2564 | 2488 | 2428
Observed below 95% for RSP180 and/or RCP240​ | 56 | 65 | 75
Filed P2/RSP180​ | 37 | 46 | 52
# Aircraft reported to applicable regional monitoring agency (RMA) - PARMO | 12 | 14 | 32

## Slide 7: Conclusions
AOE6/XXN SAT delivery paths continue to be associated with lower performance for those aircraft that are configured to use them, although not a significant number of messages observed
There are some aircraft showing up as repeat offenders are being observed making it unclear if reports are getting to the State and/or Operator
Most common problems being observed are:
  delays in VHF/SAT transition areas
  delays related to HF data link
  delays related to Inmarsat satellite to satellite transitions (possible ORT changes needed)
  delays that appear related to Iridium avionics