## Slide 1: Long Range Air Traffic Flow Management (LR-ATFM)
18 – 22 March 2019
ISPACG 33
Chris McCormack
ATC Line Manager

## Slide 2: The case for change
Long Range Air Traffic Flow Management
Current network challenges
  Strong growth of international demand at peak periods for Australia’s major airports
  Pre-tactical demand and capacity management applies to domestic operations only
  International flights often arrive without a reserved priority spot
  = Disruption of tactical arrivals management, low predictability and delays for all flights
A unique opportunity in Australia
  Large airspace
  Single system across all ATC domains (oceanic and continental)
  Mature ATFM implementation
  Towards regional ATFM
Integration of international flights into air flow traffic management processes through new network control lever = Long Range ATFM

## Slide 3: How it works – from the west
Long Range Air Traffic Flow Management
ARBEY
LR-ATFM delay is communicated to the flight crew as an AF CTO for ARBEY
Aircraft accepts AF CTO for ARBEY and advises ATC of revised cruise speed
Entering into the terminal arrivals airspace, LR-ATFM delay absorbed enroute is credited and offset against any airborne delay
Identification of delay requirement based on demand and capacity at the destination airport

## Slide 4: How it works – from the east
Long Range Air Traffic Flow Management
BOREE
Once in the Australian FIR, ATC advises AF CTO for MARLN
Aircraft accepts AF CTO for BOREE and advises ATC of revised cruise speed
Entering into the terminal arrivals airspace, LR-ATFM delay absorbed enroute is credited and offset against any airborne delay
Flight is assigned an arrival slot by Harmony with potential delay required based on demand and capacity at the destination airport
AOCs (if agreeable) can see allocated AF CTO via a Harmony web browser and can pass on to their aircraft via datalink

## Slide 5: Anticipated benefits
Long Range Air Traffic Flow Management
Long Range ATFM
Early provision of anticipated landing time
Expanded demand and capacity management
Reduced controller workload
Safety
Reduced tactical delay
Reduced fuel burn
Efficiency
Capability
Service Improvement
Outcome
Benefit
Reduced GDP delay
Efficiency
Efficiency
Predictability of operations
Equity in allocating network delay
Orderly flow into tactical arrival management environment
Improved network performance
Environment
Efficiency

## Slide 6: Timeline & next steps
Business Case approved by the Airservices Board – December 2018
Detailed design underway based on Concept of Operations
Project team in place & implementation planning underway
Long Range Air Traffic Flow Management