## Slide 1: Un-Announced Speed Changes
IPACG PM21
Dustin Byerly
SM IAP
Oakland ARTCC

## Slide 2: Mach Speed Variation
The FAA has presented papers at IPACG and ISPACG which outline the dangers of unannounced speed changes.
At the last ISPACG Meeting all agreed to continue the trial procedure and identify the data.
The data used is the first 10 days of every month.
2

## Slide 3: ICAO Annex 2 3.6.2.2 change
3.6.2.2 Deviations from the current flight plan. In the event that a controlled flight deviates from its current flight plan, the following action shall be taken:
a) Deviation from track: if the aircraft is off track, action shall be taken forthwith to adjust the heading of the aircraft to
regain track as soon as practicable.
b) Deviation from ATC assigned Mach number/indicated airspeed: the appropriate air traffic services unit shall be
informed immediately.
c) Deviation from Mach number/true airspeed: if the sustained Mach number/true airspeed at cruising level varies by
plus or minus Mach 0.02 or more, or plus or minus 19 km/h (10 kt) true airspeed or more from the current flight plan, the appropriate air traffic services unit shall be so informed.
3

## Slide 4: ICAO Annex 2 3.6.2.2 change
d) Change in time estimate: except where ADS-C is activated and serviceable in airspace where ADS-C services are provided, if the time estimate for the next applicable reporting point, flight information region boundary or destination aerodrome, whichever comes first, changes in excess of 2 minutes from that previously notified to air traffic services, or such other period of time as is prescribed by the appropriate ATS authority or on the basis of regional air navigation agreements, the flight crew shall notify the appropriate air traffic services unit as soon as possible.

## Slide 5: Speed Change NOTAM
A1445/15 - ATTN ALL AIRCREWS-NEW PROCEDURAL REQUIREMENT FOR FLIGHTS OPERATING IN OAKLAND OCEANIC CONTROL AREA (KZAK). IN ORDER TO SUPPORT COST INDEX OR ECON SPEEDS AND MAINTAIN ATC SEPARATION SPACING AIRCREWS ARE REQUIRED TO USE THE FOLLOWING PROCEDURES IN THE KZAK FIR. A PILOT MUST INFORM ATC VIA VOICE OR CPDLC EACH TIME THE CRUISING MACH NUMBER VARIES OR IS EXPECTED TO VARY BY A VALUE EQUAL TO OR GREATER THAN 0.02 MACH FROM:
(1) THE MACH NUMBER AT FIR ENTRY; OR
(2) ANY SUBSEQUENT SPEED CHANGE NOTIFIED TO ATC IN FLIGHT
IF YOU HAVE ANY QUESTIONS CONTACT DUSTIN BYERLY(510)745-3543
5

## Slide 6: Speed Change Procedure
Procedurally when an aircraft wants to change by .02 Mach number (or more), they will downlink DM18 with the requested speed (Mach number).
If ATC requires a speed assignment for separation, an appropriate speed assignment would be assigned ie UM106 MAINTAIN Speed.
If ATC did not require a speed assignment, the following could be Uplinked:
UM ROGER
UM169 Speed change to M0.84 approved
This advises the aircraft that the requested speed change is approved but no speed restriction has been assigned.
6

## Slide 7: Speed Change Procedure
2051Z-FDX60: REQUEST M084, DUE TO AIRCRAFT PERFORMANCE
2056Z- ATC: SPEED CHANGE TO M84 APPROVED
2056Z-FDX60: ROGER
2142Z-FDX60: REQUEST M080, DUE TO TURB
2142Z-ATC: MAINTAIN M080
2143Z-FDX60: WILCO
2242Z-FDX60: REQUEST M084
2244Z- ATC: SPEED CHANGE TO M84 APPROVED
2244Z- FDX60: ROGER
7

## Slide 8: Speed Changes associated with Wx
The data shows that in many cases weather was a factor for those flights.
  CPDLC messages in the time frame of the speed change indicate SIGMET notifications, Turbulence AIREPs or Weather Deviation requests.
Many Aircraft are making a CPDLC request at the time of the speed change. The aircrew should include a speed change request with their other request.

## Slide 9: Un-announced Speed Changes
Chart: 
| 17-Jan | 17-Feb | 17-Mar | 17-Apr | 17-May | 17-Jun | 17-Jul | 17-Aug | 17-Sep | 17-Oct | 17-Nov | 17-Dec
Percentage of Speed Changes Attributed to WX | 0.48131 | 0.21277 | 0.2335 | 0.068966 | 0.23232 | 0.12048 | 0.34043 | 0.27273 | 0.41304 | 0.2931 | 0.3 | 0.14352
Total Unannounced Speed Changes | 214 | 235 | 197 | 87 | 99 | 83 | 94 | 77 | 92 | 116 | 130 | 216

## Slide 10: Un-announced Speed Changes
Chart: 
| 18-Jan | 18-Feb | 18-Mar
Percentage of Speed Changes Attributed to WX | 0.14876 | 0.020134 | 0.16779
Total Unannounced Speed Changes | 242 | 149 | 149

## Slide 11: Un-announced Speed Changes
Chart: 
| MIL | HAL | DAL | UAL | KAL | PAL | JAL | ANA | QFA | ASA
17-Jun | 9 | 4 | 2 | 3 | 18 | 2 | 7 | 4 | 4 | 5
17-Jul | 10 | 4 | 3 | 3 | 7 | 8 | 4 | 2 | 14 | 1
17-Aug | 12 | 8 | 3 | 0 | 6 | 8 | 3 | 4 | 0 | 0
17-Sep | 16 | 6 | 11 | 7 | 6 | 4 | 5 | 1 | 10 | 2
17-Oct | 9 | 5 | 11 | 4 | 12 | 14 | 8 | 5 | 7 | 3
17-Nov | 9 | 12 | 10 | 8 | 12 | 4 | 14 | 9 | 5 | 5
17-Dec | 18 | 21 | 12 | 23 | 8 | 8 | 12 | 14 | 9 | 23

## Slide 12: Un-announced Speed Changes
Chart: 
| MIL | HAL | DAL | UAL | KAL | PAL | JAL | ANA | QFA | ASA
18-Jan | 7 | 40 | 29 | 22 | 14 | 5 | 10 | 11 | 6 | 15
18-Feb | 3 | 26 | 12 | 7 | 15 | 8 | 5 | 9 | 2 | 11
18-Mar | 7 | 4 | 16 | 24 | 6 | 19 | 8 | 5 | 13 | 3

## Slide 13: Conclusion
The data so far indicates that aircrews are not fully complying with the procedure.
Oakland will work to raise pilots’ awareness and compliance with the procedure.
The data has been given to FAA Flight Standards, IATA and IFALPA to help gain operator compliance.
Flight Standards Inspectors will be contacting operators to get them to comply with the procedure.

## Slide 14: Conclusion
As the FAA studies reducing separation standards, ZOA will recommend the assignment of speeds on any pair of aircraft separated by 35 miles or less.
For example if a separation standard of 20 miles longitudinal were adopted, aircraft would be assigned a speed upon application of that standard.
It has become increasingly difficult to support Econ Speeds with the number of unannounced speed changes that occur in the KZAK FIR.

## Slide 15
Discussion!!
QUESTIONS