## Slide 1: Performance Based Communication and Surveillance (PBCS) Requirements and Status April 9, 2018 Avionics Design Center Dung Nguyen - dung.q.nguyen@boeing.com

## Slide 2: PBCS Concept
Provides a framework for managing communication and surveillance performance in accordance with globally accepted Required Communication Performance (RCP) and Required Surveillance Performance (RSP) specifications
The RCP/RSP specifications provides the means to:
  Initially qualify different sub-systems , i.e. Aircraft, Network and ATS Unit
  Manage operational end-to-end system performance in continued operations

## Slide 3: PBCS Approval Required for Horizontal Separation Minima
Airspace using or planning to use one or more of the above
  NAT FIRs: Gander, Shanwick, Reykjavik, New York, Santa Maria
  Asia: Some routes over Bay of Bengal and South China Sea
  PAC FIRs: Anchorage, Auckland, Brisbane, Fukuoka, Nadi, Oakland, Port Moresby, Tahiti
Dimension of Separation | Separation Minima | RCP Requirement | RSP Requirement
Lateral | 23 nm (or 30 nm) | 240 | 180
Longitudinal | 5 min | 240 | 180
Longitudinal | 30 nm | 240 | 180
Longitudinal | 50 nm | 240 | 180

## Slide 4: RCP240/RSP180 Spec – Aircraft Allocations
Transaction Time - Nominal (95%) and Expiration (99.9%) | RCP240 | 95% within 10 sec
 |  | 99.9% within 15 sec
 | RSP180 | 95% within 3 sec
 |  | 99.9% within 5 sec
Availability | RCP240 RSP180 | 0.999
Integrity | RCP240 RSP180 | Undetected error: 10-5 per flight hour
Safety Requirements | RCP240 RSP180 | 25 Monitoring and Alerting criteria

## Slide 5: PBCS Operational Approval
Operators desiring to use performance-based separation standards from 29 March 2018 and beyond will need to meet the requirements for RCP240 and RSP180
Statement of Compliance (SoC) is required to obtain PBCS operational approval from State of Operator/State of Registry
Requirements for SoC per FAA AC 90-117 Section 3.3
  should be provided in the AFM, AFM Supplement, or other acceptable document (e.g. Boeing’s ATS SR&O)
  must indicate the aircraft data link system meets the aircraft-allocated requirements of RCP and RSP specifications

## Slide 6: Aircraft without PBCS operational approvals (non-PBCS aircraft)
PBCS is not a Mandate. Operators will be able to continue using their datalink system in all airspaces
The only airspace currently planning to implement tracks that will require PBCS is in the NAT Organized Track System (OTS). There will still be non-PBCS tracks in the OTS for which PBCS will not be required
All other airspace will allow aircraft with and without PBCS to enter and use the airspace in a mixed-mode operation (i.e. with different separation standards) with no change in route
  PBCS aircraft pair will have 30 longitudinal else 80nm/10min

## Slide 7: RCP240/RSP180 Compliance Models
Compliance demonstrated at certification
    787
    MD11 with -923
Compliance being demonstrated for certification
    737 with U14 – certification planned for 1Q2019
    747-400 with BP4 NG FMC – certification planned for 1Q2019
    747-8 with BP4 – certification planned for 1Q2019
    757/767 with Peg II – certification planned for 2Q2018
    777 with AIMS-2 hardware and BP17B for 1Q2019
Certified prior to PBCS requirements
    737 U13 With C1 hardware
    737 U12 with A4 hardware
    747-400 Load 16a with legacy FMC hardware
    747-400/747-8 NG FMC with BP3.1
    757/767 Peg 09 with Peg 1 hardware
    777 BP16 with AIMS-1 hardware

## Slide 8: Plan for PBCS compliance
To support operators getting operational approval, Boeing is planning to demonstrate RCP240/RSP180 compliance on those datalink systems that have not been demonstrated
Lab testing will be done to collect the Transaction Time (Nominal and Expiration Times)
  ATS SR&O will be revised to include the statement of compliance, the collected Transaction Time and to address the Availability, Integrity and Safety Requirements
  The AFM will not be revised since it already refers to the ATS SR&O
The plan is to perform compliance in two phases, Phase I and Phase II
Phase I completed, March 2018
Phase II testing started in March 2018 with estimated completion date by late May 2018

## Slide 9: Phase I Test Results
Model | FMC | CMU | PBCS P/F *
737 NG/Max | A4 HW with U12 | RC 822-1239-151 | Pass
 |  | HI 965-0758-006 | Fail
 | C1 HW with U13 | RC 822-1239-151 | Pass
 |  | HI 965-0758-006 | Fail
747-400 | Legacy FMC with BP16A | RC 822-1239-151 | Fail
 | NG FMC with BP3.1 | RC 822-1239-151 | Pass
747-8 | NG FMC with BP3.1 | RC 822-1239-151 | Pass
 |  | HI 963-2431-021 | Pass
757/767 | Peg I HW with Peg 09 | RC 822-1239-151 | Pass
777 | AIMS1 HW with BP16 | n/a | Fail
MD11 | 923 | RC 822-1239-151 | Fail
 |  | HI 965-0758-001 | Pass
Note:
The actual expiration time is less than the required 99.9% but better than 99.0%. The 99.0% is used for pass/fail criteria.
The 747-400 with BP16A failed due to the lack of Latency Timer

## Slide 10: Next Steps for Failed Configurations
737NG/Max with HI CMU 965-0758-006
  Upgrade FMC U14 with improved timing performance, 1Q2019
  Upgrade HI CMU with improved timing performance, 1Q2019
747-400 with Legacy FMC
  Not compliant due to lack of Latency Timer function
  No plan to upgrade Legacy FMC
  PBCS capability available with NG FMC upgrade
777 AIMS-1/AIMS-2
  No plan to upgrade AIMS-1
  PBCS capability available with AIMS-2 upgrade
  AIMS-2 currently has PBCS operational approval via FAA’s Approval for Alternate Means of Compliance
  AIMS-2 with BP17B will be certified with PBCS capability, 1Q2019
MD11 with RC CMU 822-1239-151
  Plan to re-test in May

## Slide 11: PBCS Global Requirements and Regional Implementation Status
  June 2016 - North Atlantic Systems Planning Group (NAT SPG) set March 29, 2018 implementation date
  Sept 2016 - Asia Pacific Air Navigation Planning and Implementation Regional Group (APANPIRG) set March 29, 2018 implementation date
November 2016 - ICAO Annex 6 (Operation of Aircraft) and Annex 11 (Air Traffic Services) and the Doc 4444 Procedures for Air Navigation Services (PANS-ATM)
February 2017 - Doc 10037, Global Operational Data Link (GOLD) Manual, Edition 1
June 2017 - Doc 9869, Performance-based Communication and Surveillance (PBCS) Manual, Edition 2
2017- Aeronautical Information Publication (AIP) from Canada (Jan), United Kingdom (Jun) and United States (Oct)

## Slide 12: Boeing PBCS Communications
Boeing PBCS effort has been communicated through Fleet Team Digest (FTD)
  737-FTD-34-17001
  737MAX-FTD-34-18001
  747-FTD-34-17001
  757-FTD-34-17002
  767-FTD-34-17003
  777-FTD-34-17001
Multiple Operator Message MOM-MOM-17-0176 (DEC2017) requested the Operators to provide their data link configurations for analysis to support PBCS Phase 2 Effort
MOM-MOM-18-0129 provides latest PBCS Phase 1 Results
777-FTD-34-17001 provides information on AIMS-1 and AIMS-2 PBCS issues
Boeing has begun to provide operators (who have asked) the updated MD-11, 737, 747 and 757/767 ATS SR&Os

## Slide 13: Phase II Testing Configurations
Model | FMC | CMU | Test Status
737NG/MAX | U13 | HI 965-0758-001 | In-work
 |  | HI 965-0758-002 HI 965-0758-006 | Done
747-400/8 | BP3.1 | HI 965-0758-002 HI 965-0758-006 | Done
 |  | HI 965-0758-001 | In-work
 |  | RC 822-0666-003 | In-work
 |  | RC 822-1239-101 | In-work
757/767 | Peg 09 | RC 822-1239-101 | Done
 |  | HI 965-0758-001 | In-work
 |  | MU-DLM-716C | In-work
 |  | RC 822-0666-003 | In-work
MD11 | 923 | RC 822-1239-101 | In-work
 |  | HI 965-0758-001 | In-work

## Slide 14: All Models Compliance Status
Model | FMC Build | Compliance Status | ATS SR&O update | AFM update
737 NG/Max | U13/U12 | Yes (with RC CMU -151) | Yes | No
737 NG/Max | U14 EIS | Planned 1Q2019 | Planned for EIS | Will be included at EIS
747-400 w/ Legacy FMC | BP16A | No (lack of Latency Timer) | No | No
747-400 w/ NG FMC | BP3.1 | Yes | Yes | No
747-400 w/ NG FMC | BP4 EIS | Planned 1Q2019 | Planned for EIS | Will be included at EIS
747-8 | BP3.1 | Yes | Yes | No
747-8 | BP4 EIS | Planned 1Q2019 | Planned for EIS | Will be included at EIS
757/767 w/ Peg I | Peg '09 | Yes | Yes | No
757/767 w/ Peg II | BP1 EIS | Planned 2Q2018 | Planned for EIS | Will be included at EIS
777 AIMS 1 | BP16 | No | No | No
777 AIMS 2 | BP17B | Planned 1Q2019 | Planned for EIS | Will be included at EIS
787 | EIS | Yes | Already done | Already included
777X | EIS | Planned1Q2020 | Planned for EIS | Will be included at EIS
MD-11 | 923 | Yes (with HI CMU -001) | Yes | No

## Slide 15
Question?
Thank you!