## Slide 1: PR Review
Presented by
J.F.BOUSQUIE
Flight Test Engineer

## Slide 2
New PRs

## Slide 3: PRs not addressed
Traces not yet received :
2575 and 2574 – Error: end service with pending messages
2554 – Connection Failure
2547 – Climb clearance
2548 – No data in the Predicted Route Group for the entire flight
2523 – Delayed reports – VHF/SATCOM transition/SATCOM spotbeam
No trace for investigation => Proposal: Close PRs
2515 - CPDLC Uplink not delivered to aircraft
2516 - CPDLC Uplink not delivered to aircraft

## Slide 4: PR 2371: A332 - Incorrect estimate in ADS-C Waypoint Event
Issue:
Receipt of one ‘Waypoint change’ ADS-C report containing erroneous time estimate for Next waypoint (error of grossly 46 minutes)
Issue detected whereas the aircraft was operating on a weather deviation
Issue limited to a single report: previous reports as well as the following ones contain correct time estimate
Analysis:
Air/ground traces confirm wrong time estimate in a WCE report
Issue related to bad FMS prediction computations but investigations and tests did not allow allow reproducing and identifying any root cause
TO BE MONITORED

## Slide 5: PR 2381/2415: A320 performance on Iridium SATCOM well below RSP180 requirements
Issue:
Strong latencies (up to 28 min) observed for ADS-C downlink transmission performed via Iridium, resulting in non-compliance with RSP180 performance requirements
Analysis:
Both PRs refer to the same aircraft whose Satcom was installed by the airline via STC => no possible Satcom investigation on Airbus side
Performance issues have been reported to the airline but no feedback was received
TO BE INVESTIGATED BY IRIDIUM
PROPOSAL: CLOSE THE PR FOR AIRBUS

## Slide 6: Thales FMS issue: Erroneous ADS-C Predicted route information
Issue:
Transmission of ADS-C report including erroneous position information for NEXT and NEXT+1 waypoints (Predicted Route data group).
Issue limited to one or two reports => Content of subsequent reports is normal
  Corresponding PRs: 2391 and 1368/1660/2301/2323 (NAT PRs)
Analysis:
Issue corresponding to one FMS anomaly occurring during predicted route computation (e.g. following temporary insertion):
N and N+1 waypoints can be wrongly replaced by the 21st and 22nd next waypoint or any other modulo 20 waypoint
Correct predicted route information are obtained after the next prediction computation (~1min)
Applicability:
  Issue applicable to all Thales FMS standards in service but issue occurrence rate may vary from one standard to the other
Fixing available in FMS Thales S8/T6 (certification 2018)

## Slide 7: PR 2393/2394: A332 - Erroneous ADS-C estimate(s) from A332
Issue:
Receipt of ADS-C reports including erroneous time estimate (by 6 -7 minutes) for waypoints to be reached within 50- 60 min.
Issue suspected to be due to having no wind loaded/entered for prediction computation
Analysis:
Air/ground trace analysis confirms wrong time estimate detected in ADS-C reports.
Missing wind data in FMS seems the most probable assumption to explain reported issues but investigations could not confirm it
Observed issues and recommendations to load wind information were reported to the airline => Significant improvements reported by controllers since PR creation
TO BE CLOSED

## Slide 8: PR 2416: A388 - Performance deterioration on A388 through March 2017
Issue:
Deteriorated ADS-C performance reported by NZZO, falling below RSP180 requirements
(Example: March 2017 – Criterion ‘99.9% - delay <180s’ only met for 77.06% of ADS-C transmissions)
Analysis:
Degraded performances result from Satcom unavailability during long time intervals
=> As the aircraft was out of VHF coverage, all ATC traffic (AFN/CPDLC/ADS-C) was transmitted via HF, but with strong delays, due to the poor performance of the media
No root cause for Satcom unavailability identified (no Satcom log available)
Satcom issues were reported in 2016 for the same aircraft to Airbus customer service which recommended Satcom replacement (see also NAT PR 2253)
Airline contacted again to check if Satcom issues are still detected with the aircraft but no feedback received
TO BE MONITORED

## Slide 9: PR 2431: A332 - 8-minute error in ADS-C predicted estimate over 1 hour flight leg
Issue:
An ADS-C report included a grossly erroneous time estimate of 8 minutes for the next waypoint.
For following reports, time estimate was revised by 2 minutes and correct estimate was finally obtained when approaching next waypoint.
Issue suspected to be due to lack of wind inserted in the FMS.
Analysis:
Air/ground traces confirm wrong time estimate
Issue related to bad FMS prediction computations but no root cause identified as no FMS internal data could not be retrieved for investigating
TO BE MONITORED

## Slide 10: PR 2433: A388 - Unable to CPDLC to/from Brisbane/YBBB
Issue:
After establishing one CPDLC connection, Brisbane YBBB reported to be unable to exchange any CPDLC UL/DL message (issues reported on May 03, from 14:50)
Analysis:
Air/ground logs do not show any communication issue or avionics misbehaviour
CPDLC connection with YBBB is established at 15:03 and all following CPDLC exchanges are nominally performed: all ULs were received and answered by the crew ; downlink requests were also properly received and answered by YBBB
Wrong date or aircraft identification suspected
NOMINAL BEHAVIOUR FROM AIRCRAFT SIDE
=> PROPOSAL: PR TO BE CLOSED FOR AIRBUS

## Slide 11: PR 2448: A333 - Uplink clearance not received by aircraft
Issue:
After sending a CPDLC clearance to climb to FL380, YBBB did not receive any answer from the aircraft
The crew reported by voice that the uplink clearance had not been received
Analysis:
Air/ground traces confirm that the uplink clearance was properly received and acknowledged (at ACARS level) by the aircraft and no answer was sent by the crew.
Investigations do not put into light any avionics misbehaviour or air/ground communication issue
No root cause identified but reported issue not related to the known ACK and TOSS issue
TO BE CLOSED

## Slide 12: PR 2461: A346 - Aircraft logged on ZWWW-CPDLC unsuccessfully
Issue:
Unsuccessful notification attempts with Chinese centers ZWWW and ZLLL during one flight from VHHH (Hong Kong) to EDDM(Munich).
ZWWW had to guide the aircraft out of China through voice
Analysis:
Before entering ZLLL airspace, the aircraft was connected with ZUUU which designated ZLLL as NDA
Notification and CPDLC connection establishment steps were successfully performed with ZLLL
ZUUU sent afterwards one CPDLC Disconnection request => as per compliance with ED100A, the aircraft terminated CPDLC links with ZUUU and ZLLL
Next notification requests sent by the crew to ZLLL were received on ground but never answered by the ATC center (AFN notification issues have also been reported by CSP ARINC with ZLLL, ZWWW and ZPPP)
Notification sequence performed afterwards with ZWWW was successful but CPDLC connection requests were rejected on-board with a DR1 message => avionics anomaly but no root cause identified
AFN Notification failure => TO BE INVESTIGATED WITH ZLLL
A/C CPDLC Connection rejection Issue => TO BE MONITORED

## Slide 13: PR 2482: A320 - Ground Speed Errors
Issue:
Colombo Oceanic reports receipt of ADS-C reports including wrong time estimate and wrong ground speed information.
Ground speed information is also reported to be missing in some reports.
Analysis:
Analysis of air/ground traces does not show erroneous or missing ground speed transmission in ADS-C reports
However, traces show continuous transmission of default values for ADS-C predicted route, fixed projected intent and intermediate project intent data groups
=> Issue related to bad FMS prediction computations but no root cause could be identified due to missing operational data (i.e. FMS data)
ATC Center VCCC => Check ground decoding/processing for ground speed
Missing ADS-C Predicted Route/ Intent Data => TO BE MONITORED

## Slide 14: PR 2513 : A333 - Unexpected WILCO
Issue:
FAA (KZAK) reported a WILCO receipt with a MRN information matching none of the uplinks previously sent
Analysis:
After receipt of UM117 CONTACT + UM 161 End Service from RJJJ, WILCO and DR1 messages were only sent two hours later by the crew and whereas NDA KZAK had started sending uplinks (uplinks were discarded on-board)
WILCO and DR1 were then wrongly sent to KZAK instead of RJJJ
=> Avionics issue known as ‘Spurious Wilco’ (Issue A23 in FANS 1/A Problem Solution Tracker file) :
=> If a message is received from the NDA while the message CONTACT+ END SERVICE is displayed to the pilot, then NDA and CDA communication links will be inverted.
While WILCO (and DR1) response have not been answered, KZAK was still identified as NDA but the center repeatedly sent CPDLC messages to the aircraft in spite of receiving DM63- NOT CURRENT DATA AUTHORITY
‘Spurious Wilco’ fixed on CSB9/CLR9 (A320,A330 and A340)
Correction at next opportunity on A380 and A350
Ground Behaviour to be clarified with KZAK

## Slide 15: PR 2555: A333 - Connection failure
Issue:
Failed CPDLC connection establishment attempts reported by WAAF
The issue was resolved after the crew initiated a notification sequence
Analysis:
Analysis of air/ground traces does not show any avionics misbehaviour:
The first connection requests from WAAF were rejected because the aircraft was connected with YBBB but no NDA had been declared.
WAAF was then declared as NDA but did not send any connection request.
YBBB then sent an END SERVICE, leaving the aircraft without CDA for 30 min until a new log on was performed the crew and a new connection request was then initiated by WAAF.
CONNECTION ISSUES TO BE INVESTIGATED BY WAAF
PROPOSAL: PR TO BE CLOSED FOR AIRBUS

## Slide 16: PR 2560: A332 - Aircraft sends 00:00:00 in predicted route group instead of correct estimate
Issue:
Incorrect predicted time estimate (set at 00:00:00) in ADS-C reports received shortly before midnight. After midnight, the estimates become correct again.
Analysis:
Scenario corresponding to the already known Airbus ‘FMS midnight issue’ due to a Flight Management System anomaly occurring under the following conditions:
  Current time at PPOS (Present Position) is before midnight
  FMS computed Estimated Time of Arrival (ETA) for next waypoint is after midnight
In such case, the ETA provided in ADS-C report for the Next waypoint is incorrectly set to 00:00:00.
Issue referred to as A13 in FANS1/A Problem solution tracker file
Corrected on Thales/GE FMS S5
(for SA since 2009) / T3 (for LR since 2010)
PR TO BE CLOSED

## Slide 17: Proposal for PR Closure
PRs presented during previous FIT meetings with nominal avionics behaviour
  PR 1515 – Unable to load UM80 - A332
  PR 1573 - Position not updated after giving demand contract
PRs presented during previous FIT meetings with no traces to investigate
  PR 1912 - Uplinked CPDLC route clearance - No LOAD prompt or error message