## Slide 2
#1 on the list of Contributing Factors for General Aviation Accidents is Inadequate Preflight Preparation/Planning
AIM, Section 7-6-1 (2022 Version)

## Slide 3: Advisory Circular 91-92 Pilot’s Guide to a Preflight Briefing
Encourages pilots to conduct preflight self-briefings
Shows pilots how to conduct a regulatory compliant preflight self-briefing using automated resources
Assists pilots in complying with Title 14 of the Code of Federal Regulations (14 CFR) part 91, §§ 91.103 that states each pilot in command shall become familiar with all available information concerning their flight before departure

## Slide 4: Benefits of Self-Briefing Skills
  Enhances the pilots’ weather interpretation and risk management skills to better understand real time weather data affecting their route of flight
  Pilots become more comfortable with using available weather resources
  Assists pilots in making better “go-no-go” decisions
  Prepares pilots to assess risk of constantly changing weather conditions while in flight
There are several reasons why developing the knowledge and skill to conduct a preflight self-briefing using online weather resources is an advantage and highly recommended by the FAA:

## Slide 5
FAA Flight Service Preflight Self-Briefing WINGS Courses
VFR & Student Pilots
IFR Student & IFR Pilots
faasafety.gov/wings
ALC-889: Conducting Preflight Self-Briefings for IFR Pilots
faasafety.gov/wings
ALC-683: Conducting Preflight Self-Briefings for Student and VFR Pilots

## Slide 6: The Preflight-Planning Process Flow
1
2
3
4
5
Five Steps to Safety
Conduct Steps 1,2,3,4 as early as possible before the flight
After Step 4
  If needed, go to Step 1 (e.g., add a fuel stop)
  Repeat Steps 2,3,4 in the days and hours prior to the flight
A Go decision is never final. Apply Steps 2,3,4 again right before departure and determine if it’s still safe to fly
Once airborne continue to collect and process the weather and aeronautical information for the remaining flight segments
  As risks evolve or present, develop mitigations
  The “Go-No-Go” decision becomes a “Continue-on” or “Divert/Land” decision

## Slide 7: Preflight Self-Briefing Checklist

## Slide 8: 1800wxbrief.com Weather Log
Click “Evaluate” button on Flight Plan Form to generate weather log
Flight Plan Form
Weather Log

## Slide 9
Source: Risk Management Handbook FAA-H-8083-2
Risk Identifying, Assessing and Mitigating Tools
Mitigating the Risk
Wait until the weather is VFR
Take an IFR current & IFR proficient pilot
Cancel the flight
Consider driving
Notes: PAVE & I’M SAFE tool to identify risk before each flight (Chapter 3 Risk Management Handbook FAA-H-8083-2)
Assessing Risk (Risk Assessment Matrix Tool Chapter 4 (Risk Management Handbook (FAA-H-8083-2)

## Slide 10: FAA Resources for the Flight Instructor
VFR/IFR WINGS Course
WINGS Student Worksheet
WINGS Instructor Companion Document
AC 91-92

## Slide 12: AC 91-92 Resource List

## Slide 13: WINGS Courses Government Preflight Self-Briefing Resource List
Note: Third-party online resources may also be used to conduct preflight self-briefings
1800wxbrief.com | Leidos Flight Service – FAA Contract Vendor
weathercams.faa.gov | FAA Weather camera network
aviationweather.gov | NOAA/Government aviation weather website
fly.faa.gov/rmt/nfdc_preferred_routes_database.jsp | FAA Preferred Routes
nasstatus.faa.gov | FAA Flight Delay Information
nhc.noaa.gov | National Hurricane Center (NHC)
notams.aim.faa.gov/notamSearch | Federal NOTAM System (FNS) NOTAM Search
spc.noaa.gov | NOAA Storm Prediction Center (SPC)
ssd.noaa.gov/VAAC/vaac.html | Volcanic Ash Advisory Centers (VAAC)
sua.faa.gov | Special Use Airspace (SUA)
tfr.faa.gov/tfr2/list.html | Temporary Flight Restrictions (TFR)
weather.gov | National Weather Service Forecast Office
weather.gov/aawu | Alaska Aviation Weather Unit (AAWU)
weather.gov/hfo | NWS Forecast Office Honolulu, HI
wpc.ncep.noaa.gov | Weather Prediction Center (WPC)

## Slide 14: Research

## Slide 15: Transition Strategy for Safe Self-Briefings
If you are new to self-briefing or currently call Flight Service for preflight planning, it’s important to make the transition to self-briefing in a safe manner
Follow a transition strategy to measure and refine your skills
  Using a checklist, conduct a self-briefing and identify the risks for the flight, then make your “go-no-go” decision
  Discuss with your flight instructor your decision logic, the weather products you used, and your final assessment. Compare your assessment with that of your flight instructor
  If needed, call Flight Service to discuss or confirm meteorological or aeronautical information obtained through online resources
  When your assessments become consistent with those of the flight instructor or briefer, you have developed the skills necessary to begin trusting your own judgement
As you add/encounter new or more complex items during flight planning, revert to the transition strategy to ensure your skills and assessments continue to improve

## Slide 16: Weather Camera Program
FAA Camera Sites
  230 Alaska
  11 Hawaii
3rd Party Hosted Sites
  6 Alaska
  219 NAV Canada
  43 Colorado
  1 Michigan
Preflight Planning Website
  Images, METARS, TAFS
  Satellite, RADAR, RCO/RCAGs
  Airports, Sectionals, NOTAMs
  2 Mississippi
  8 Montana
  1 Utah
Notes: Mentions mission and goals

## Slide 17: Know Before You Go & Check Enroute
A self-briefing resource to enhance preflight planning and improve decision making before and after takeoff
Clear-Day Comparison Image
Current Image

## Slide 18: Weather Camera Impact
85% reduction in weather-related accidents
69% reduction in weather-related flight interruptions
Recommended by the NTSB
Recommended by the Senate Transportation Housing and Urban Development (THUD) Committee

## Slide 19: Program Expansion
Applications
  Near mountains/high terrain
  Common flight routes with gaps in certified weather stations
  Heliports/Hospitals
  Lakes/Rivers with float-plane operations
  Validate airport conditions
Feedback Welcome
  Do you have an opinion on a recommended location?
  Send me an email and tell me where and why at:
Daniel.C.Pope@faa.gov