## Slide 1
Edmonton Area Control Centre presentation to the CROSS POLAR WORKING GROUP “Polar Collaborative Decision Making” Paris, France November 2-5, 2010 Presented by: Bryon Carlson, Edmonton ACC North High Supervisor
Notes: Also Present at CPWG –
Butch March, Manager Area Control Centre Operations, Edmonton
Dave Rose, Manager International Operations, Ottawa

## Slide 2: Polar Collaborative Decision Making
Edmonton currently uses the GRL to prioritize altitude assignments for Polar flights.
Normally, flights that are on, or closest to, their GRL times are given altitude priority.
Notes: Edmonton currently uses the GRL to prioritize altitude assignments for Polar flights.
Normally, flights that are on, or closest to, their GRL times are given altitude priority.

## Slide 3: Polar Collaborative Decision Making
Can this process be more effectively and efficiently managed?
The following table and next slides illustrate a scenario that occurred in July, 2010 involving ACA031 and UAL897 at RAMEL.
Flight | GRL time/altitude | Initial estimate | Initial Altitude
ACA031 | 0101/FL340 | 0102 | FL300
UAL897 | 0112/FL340 | 0102 | FL340
Notes: Can this process be more effectively and efficiently managed?
The following table and next slides illustrate a scenario that occurred in July, 2010 involving Air Canada 031 and United 897

## Slide 4: Polar Collaborative Decision Making
ACA031 was “on time,” and UAL897 was ~10 minutes early – ACA gets FL340 & UAL gets a “penalty.”
UAL dispatch was contacted, and was asked to consider “higher” (FL360/380), “lower” (FL320), or “slower” (about M.80 for ~ 4 hours).
After conferring with the crew, dispatch advised that UAL897 was unable FL360/380 and “lower” would result in excessive fuel burn - therefore “slower” was the only acceptable option.
A plan was put in place that assigned ACA031 maximum speed (A.83+), and assigned UAL897 A.80.
Notes: ACA031 was “on time,” and UAL897 was ~10 minutes early – ACA gets FL340 & UAL gets a “penalty.”
UAL dispatch was contacted, and was asked to consider “higher” (FL360/380), “lower” (FL320), or “slower” (about M.80 for ~ 4 hours).
After conferring with the crew, dispatch advised that UAL897 was unable FL360/380 and “lower” would result in excessive fuel burn - therefore “slower” was the only acceptable option.
A plan was put in place that assigned ACA031 maximum speed (A.83+), and assigned UAL897 A.80.

## Slide 5: Polar Collaborative Decision Making
As the next few hours passed, ACA031 increased speed to A.85, and UAL897 varied speed within a range of A.78 to A.81.
10’ longitudinal spacing was achieved around 80N, opening up FL340 for both flights once ACA031 requested it (at 141W).
Notes: As the next few hours passed, ACA031 increased speed to A.85, and UAL897 varied speed within a range of A.78 to A.81.
The Air Canada crew agreed to increase speed after becoming very concerned while hearing transmissions to/from UAL897.
10’ longitudinal spacing was achieved around 80N, opening up FL340 for both flights once ACA031 requested it (at 141W).

## Slide 6
RAMEL
141W
AS IT HAPPENED………….
FL340
FL320
Conflict identified
+1 hour
+2 hours
+3 hours
Notes: ACA031 was “on time,” and UAL897 was 10 minutes early.
The plan was to get ACA031 to FL340 - UAL897 would take a “penalty.”
UAL dispatch was contacted, and was asked to consider “higher” (FL360/380), “lower” (FL320), or “slower” (about M.80 for ~ 4 hours).
After conferring with the crew, dispatch advised that UAL897 was unable FL360/380 and “lower” would result in excessive fuel burn - therefore “slower” was the only acceptable option.
A plan was put in place that assigned ACA031 maximum speed (A.84+), and assigned UAL897 A.80.
As the next few hours passed, ACA031 increased speed to A.85, and UAL897 varied speed within a range of A.78 to A.81.
The Air Canada crew agreed to increase speed after becoming very concerned while hearing transmissions to/from UAL897.
10’ longitudinal spacing was achieved around 80N, opening up FL340 for both flights once ACA031 requested it (at 141W).

## Slide 7: The Result…………….
The GRL benefited the flight closest to its GRL time.
ACA031 got FL340 when requested.
UAL897 also got FL340, but at a greatly reduced speed which resulted in ~10 minutes more flying time.
Followed up with ACA dispatch in the following days, and inquired whether or not FL320 until at least Russian landfall would have been an acceptable option on that day.
Response: On that day, the flight would have made destination (ZBAA), with an additional fuel burn of ~1400kg flying FL315/9600m to SULOK.
Notes: The GRL benefited the flight closest to its GRL time.
ACA031 got FL340 when requested.
UAL897 also got FL340, but at a greatly reduced speed which resulted in ~10 minutes more flying time.
Followed up with ACA dispatch in the following days, and inquired whether or not FL320 until at least Russian landfall would have been an acceptable option on that day.
On that day, the flight would have made destination (ZBAA), with an additional fuel burn of ~1400kg flying FL315/9600m to SULOK

## Slide 8: Going Forward………….
In this case, could ACA dispatch have been contacted when the conflict was identified, and asked them if FL320/FL315/9600m would have been acceptable?
If so, the speed restrictions on UAL & ACA would have been negated.
Instead of mainly relying on the GRL to resolve conflicts, we have been using a more collaborative approach. Is this preferred?
Notes: In this case, could ACA dispatch have been contacted when the conflict was identified, and asked them whether or not FL320 would have been acceptable?
If so, the speed restrictions on UAL & ACA would have been negated.
Instead of mainly relying on the GRL to resolve conflicts, we have been using a more collaborative approach. Is this preferred?

## Slide 9: Polar Collaborative Decision Making
Comments/Questions??