## Slide 1
CPWG/11
June 7-10, 2011
St. Petersburg, Russia
State ATM Corporation of Russia
RVSM Implementation in Russia

## Slide 2: RVSM Implementation in Russia
The first meeting of EURASIA RVSM TF/1 on RVSM implementation in the eastern part of the ICAO European region took place on Sep 1-3, 2009 in Moscow.
EURASIA RVSM TF agreed:
- to implement RVSM simultaneously on November 17, 2011 in Kazakhstan, Kyrgyzstan, Mongolia, Russian Federation, Tajikistan, Turkmenistan and Uzbekistan;
- RVSM implementation shall be carried out under coordination and cooperation with all interested States in the framework of EURASIA RVSM project;
- two working groups were set up:
а) ATM working group.
б) Monitoring working group.
Develop and approve EURASIA RVSM Master Plan (developed in December 2009).
EURASIA RVSM project member-States shall develop safe RVSM transition plans.
Adopt the management structure of RVSM implementation program.

## Slide 3: RVSM Implementation Management
RVSM Implementation National Coordinators |  |  |  |  |  | 
Kazakhstan | Kyrgyzstan | Mongolia | Russian Federation | Tajikistan | Turkmenistan | Uzbekistan
EURASIA RVSM TF
ATM WG
RMA WG
ICAO

## Slide 4: RVSM Program Set-up
RVSM Program Manager (Office)
R0 project – RVSM program confirmation
& acceptance
R1 program – airspace user training &
performance validation
R2 program – ATM training
R3 program – ensure RVSM flight safety
R4 project– information, communication and
program arrangements

## Slide 5: RVSM Implementation Actions
EURASIA RVSM ATM WG/1 on November 17 – 19, 2009 in Almaty, Kazakhstan. The meeting developed main actions regarding the coordinated activities by the member-States in order to harmonize ATS procedures and prepare their respective ATM & ASM systems for RVSM implementation
RVSM workshop on February 4 -5, 2010 in St. Petersburg, Russia. The workshop focused on problematic issues, which need to be tackled during RVSM implementation.
EURASIA RVSM ATM WG/2 on March 23 – 25, 2010 in Bishkek, Kyrgyzstan. The meeting developed the main actions for system modernization, assessed the airspace structure in the view of its harmonized utilization, reviewed possible separation aspects and AIC issuance.
Promulgation of AIC 03/10 on ICAO RVSM transition between FL290 and FL410.
EURASIA RVSM ATM WG/3 on June 21-23, 2010 in St. Petersburg, Russia. The meeting reviewed the progress on RVSM implementation plans, training of air traffic controllers and aviation personnel, looked into development of system modernization plans and writing of personnel handbooks

## Slide 6: RVSM Implementation Actions
State ATM Corp coordination meeting on August 17 – 19, 2010, Krasnoyarsk, Russia. The meeting involved deputy directors of State ATM Corp’s regional branches and heads of ATC & airway facility maintenance units. The meeting reviewed the current status of RVSM preparations in the branches and developed an effective RVSM implementation guidelines. There were also developed proposals for amendment of operational procedures and ATC radio exchange in RVSM environment.
EURASIA RVSM ATM WG/4 on November 16 -19, 2010, Dushanbe, Tajikistan.
The meeting was tasked to coordinate efforts on RVSM implementation, determine practical actions between the States aimed at efficient RVSM implementation and attainment of the objectives in 2011.
EURASIA RVSM TF/4 and EURASIA RVSM ATM WG/5 on December 13 – 14, 2010, Paris, France. The meeting focused on the operational issues of RVSM implementation and preparatory actions based on the single target date for RVSM implementation.

## Slide 7: RVSM Implementation Actions
State ATM Corp coordination meeting on March 14, 2011 Khabarovsk, Russia. The meeting involved deputy directors of State ATM Corp’s regional branches and heads of ATC & airway facility maintenance units. The meeting reviewed the progress reports from the branches on RVSM implementation, studied technical & operational issues of RVSM implementation and amendment of the exisiting LOAs with adjacent ACCs.
EURASIA RVSM TF/5 and EURASIA RVSM ATM WG/6 on March 15 – 18, 2011 Khabarovsk, Russia. The meeting reviewed the outcomes of actions accomplished in 2010 and scheduled steps of EURASIA RVSM program implementation at the final phase in 2011.
EURASIA RVSM ATM WG/7 on May 16, 2011 Moscow, Russia.
The meeting validated outcomes of traffic simulation at Russia/Kazakhstan interface and confirmed the accuracy of implemented actions related to EURASIA RVSM master plan. The proposals based on the simulation results were included in the meeting report.
EURASIA RVSM ATM WG/8 on June 13 – 17, 2011 Riga, Latvia
The meeting reviewed coordination and interaction issues between ACCs in Europe and Russia as well as EURASIA RVSM member States in the view of RVSM implementation.

## Slide 8: Operational Actions
All aircraft operators approved for RVSM should include “W” in item 10 of FPL irrespective of the requested flight level; military, police and customs aircraft operators shall insert “M” in item 8 of FPL.
Aircraft operators who intend to operate formation flights such as GAT regardless of their RVSM approval status should include “STA/NONRVSM” in item 18.
«STS/NONRVSM» stipulates a request for a special service from ATS units, namely a request to ensure a vertical separation minimum of 2000 feet between this aircraft and other aircraft flying in the RVSM airspace.

## Slide 9: Operational Actions
Civil aircraft operators who do not have RVSM approval
shall insert a requested en-route flight level below FL290 after the entry point within the lateral limits of RVSM airspace and exit point beyond the lateral limits of RVSM airspace (borders of responsibility area of a particular ACC).
State aircraft operators who do not have RVSM approval
shall not insert «W» in item 10 of FPL. If requesting FL290 or above, STS/NONRVSM shall be included in item 18 of FPL.
State aircraft operators who do not have RVSM approval but intend to operate a flight with RVSM airspace shall insert entry/exit points and a requested flight level in item 15.
State aircraft operators who have RVSM approval
Operators of state, police or customs aircraft approved for RVSM and intending to operate a flight in RVSM airspace, shall insert «М» in item 8 of FPL.
State aircraft operators who intend to operate a flight in the RVSM airspace shalll insert entry/exit points and a requested flight level in item 15.

## Slide 10: Cruise Flight Level Table
True track angle 000 - 179 |  |  |  |  |  | True Track Angle 180- 359 |  |  |  |  | 
VFR flights |  |  | IFR flights |  |  | VFR flights |  |  | IFR flights |  | 
Flight level | Altitude |  | Flight level | Altitude |  | Flight level | Altitude |  | Flight level | Altitude | 
 | Meters | Feet |  | Meters | Feet |  | Meters | Feet |  | Meters | Feet
010 | 300 | 1000 | - | - | - | 020 | 600 | 2000 | - | - | -
030 | 900 | 3000 | 035 | 1050 | 3500 | 040 | 1200 | 4000 | 045 | 1350 | 4500
050 | 1500 | 5000 | 55 | 1700 | 5500 | 060 | 1850 | 6000 | 65 | 2000 | 6500
070 | 2150 | 7000 | 75 | 2300 | 7500 | 080 | 2450 | 8000 | 85 | 2600 | 8500
090 | 2750 | 9000 | 95 | 2900 | 9500 | 100 | 3050 | 10000 | 105 | 3200 | 10500
110 | 3350 | 11000 | 115 | 3500 | 11500 | 120 | 3650 | 12000 | 125 | 3800 | 12500
130 | 3950 | 13000 | 135 | 4100 | 13500 | 140 | 4250 | 14000 | 145 | 4400 | 14500
150 | 4550 | 15000 | 155 | 4700 | 15500 | 160 | 4900 | 16000 | 165 | 5050 | 16500
170 | 5200 | 17000 | 175 | 5350 | 17500 | 180 | 5500 | 18000 | 185 | 5650 | 18500
190 | 5800 | 19000 | 195 | 5950 | 19500 | 200 | 6100 | 20000 | 205 | 6250 | 20500
210 | 6400 | 21000 | 215 | 6550 | 21500 | 220 | 6700 | 22000 | 225 | 6850 | 22500
230 | 7000 | 23000 | 235 | 7150 | 23500 | 240 | 7300 | 24000 | 245 | 7450 | 24500
250 | 7600 | 25000 | 255 | 7750 | 25500 | 260 | 7900 | 26000 | 265 | 8100 | 26500
270 | 8250 | 27000 | 275 | 8400 | 27500 | 280 | 8550 | 28000 | 285 | 8700 | 28500
290 | 8850 | 29000 | - | - | - | 300 | 9150 | 30000 | - | - | -
310 | 9450 | 31000 | - | - | - | 320 | 9750 | 32000 | - | - | -
330 | 10050 | 33000 | - | - | - | 340 | 10350 | 34000 | - | - | -
350 | 10650 | 35000 | - | - | - | 360 | 10950 | 36000 | - | - | -
370 | 11300 | 37000 | - | - | - | 380 | 11600 | 38000 | - | - | -
390 | 11900 | 39000 | - | - | - | 400 | 12200 | 40000 | - | - | -
410 | 12500 | 41000 | - | - | - | 430 | 13100 | 43000 | - | - | -
450 | 13700 | 45000 | - | - | - | 470 | 14350 | 47000 | - | - | -
490 | 14950 | 49000 | - | - | - | 510 | 15550 | 51000 | - | - | -
etc | etc | etc | - | - | - | etc | etc | etc | - | - | -