## Slide 1
Edmonton Area Control Centre presentation to the CROSS POLAR WORKING GROUP “GRL Spacing” Санкт-Петербург, Россия June 7-10, 2011 Presented by: Брион Карлсон (Bryon Carlson) Edmonton ACC North High Supervisor
Notes: <number>
<number>
Also Present at CPWG –
Butch March, Manager Area Control Centre Operations, Edmonton

## Slide 2
20’/15’ GRL Spacing
Polar fix spacing 20’ – left over from CAATS implementation. Recently reduced to 15’.
Many CAATS issues resolved, including most affecting Polar flights.
CAATS superior to previous system in wind model, conflict prediction, planning, and automated passing of estimates.
Should the GRL spacing be reduced to 10’ or 15’ permanently??
Notes: Polar fix spacing 20’ – left over from CAATS implementation. Recently reduced to 15’.
Many CAATS issues resolved, including most affecting Polar flights.
CAATS superior to previous system in wind model, conflict prediction, planning, and automated passing of estimates.
Should the GRL spacing be reduced to 10’ or 15’ permanently??

## Slide 3: 10’ GRL Spacing “Pro’s”
GRL estimates now more accurately reflect “reality” compared to before
Will have increased future accuracy with DOTS++ etc..
Very good “optics” and apparent efficiency gains
Potential altitude penalties will be less with RVSM throughout whole flight
Notes: GRL estimates now more accurately reflect “reality” compared to before
Will have increased future accuracy with DOTS++ etc..
Very good “optics” and apparent efficiency gains
Potential altitude penalties will be less with RVSM throughout whole flight

## Slide 4: 10’ GRL Spacing “Con’s”
“Overtake situations” require more than the minimum 10’.
Different wind components from converging routes, different wind components from aircraft at different altitudes on the same route, actual vs. forecast winds – all affect estimates
Different methods of calculating estimates – CZEG vs. ZANC, ATC vs. aircraft, ATC vs. dispatch, aircraft vs. dispatch.
The “rounding off of seconds” in a position report can make 10’ on estimates become 8’, 9’, 11’ or 12’ quickly, without having changed any part of a clearance.
Unrealistic expectations? GRL estimates now more accurately reflect “reality” compared to before.
Notes: “Overtake situations” require more than the minimum 10’.
Different wind components from converging routes, different wind components from aircraft at different altitudes on the same route, actual vs. forecast winds – all affect estimates
Different methods of calculating estimates – CZEG vs. ZANC, ATC vs. aircraft, ATC vs. dispatch, aircraft vs. dispatch.
The “rounding off of seconds” in a position report can make 10’ on estimates become 8’, 9’, 11’ or 12’ quickly, without having changed any part of a clearance.
Unrealistic expectations? GRL estimates now more accurately reflect “reality” compared to before.

## Slide 5
RAMEL
N
UAL CZEG Estimate = 0058z
UAL ZANC Estimate = 0058z
UAL Airline Estimate = 0100z
ACA CZEG Estimate = 0108z
ACA ZANC Estimate = 0107z
ACA Airline Estimate = 0110z
“Best Case scenario” = 12’
“Worst case scenario” = 7’
“Average” = 9.67’
Minimum Separation = 10’
141W
Estimate differences

## Slide 6
ORVIT
N
A.82
Actual=0100z
A.83
Actual=0110z
A.86
Actual=0120z
Required separation between #1 & #2 is 12’
Required separation between #2 & #3 is 15’
Likely speed adjustments for #1 and #3; or, #2 gets different altitude or reroute - despite ALL being “on time!”
Overtake Scenario
141W
Notes: Required separation between #1 & #2 is 12’
Required separation between #2 & #3 is 15’
Likely speed adjustments for #1 and #3; or, #2 gets different altitude or reroute - despite ALL being “on time!”

## Slide 7
15’ GRL Spacing “Con’s”
Poor Optics. Lost efficiency??
Reduced track loading for each fix
Notes: Poor Optics. Lost efficiency??
Reduced track loading for each fix

## Slide 8
15’ GRL Spacing “Pro’s”
Would factor in most of the scenarios and concerns in previous slides, and would be a realistic target for the airlines and for ATC
Flight Planned altitudes would be achieved more often, and airlines would be better protected for less than optimal altitudes
Notes: Would factor in most of the scenarios and concerns in previous slides, and would be a realistic target for the airlines and for ATC
Flight Planned altitudes would be achieved more often, and airlines would be better protected for less than optimal altitudes

## Slide 9
Going forward…….
Edmonton will support either 10’ or 15’ spacing (or anything in between - 12’ ??)
Customers need to be aware of the benefits/detriments of each
Customer input needed to determine the way forward
Notes: Edmonton will support either 10’ or 15’ spacing (or anything in between - 12’ ??)
Customers need to be aware of the benefits/detriments of each
Customer input needed to determine the way forward

## Slide 10: Questions/Discussion
??