## Slide 1
Edmonton Area Control Centre presentation to the CROSS POLAR WORKING GROUP “Polar Tactical Re-routes” Санкт-Петербург, Россия June 7-10, 2011 Presented by: Брион Карлсон (Bryon Carlson) Edmonton ACC North High Supervisor
Notes: <number>
Also Present at CPWG –
Butch March, Manager Area Control Centre Operations, Edmonton

## Slide 2: Polar Tactical Re-routes
The daily, “normal use,” of tactical re-routes has been discussed many times in the past.
Has been discussed, or referenced to, in CP06-12, CP08-08 and CP09-03.
Could be used for Emergency situations, traffic/conflict resolution, and for the re-evaluation of flight planned routes by crew/dispatch while already airborne.
Notes: <number>
The daily, “normal use,” of tactical re-routes has been discussed many times in the past.
Has been discussed, or referenced to, in CP06-12, CP08-08 and CP09-03.
Could be used for Emergency situations, traffic/conflict resolution, and for the re-evaluation of flight planned routes by crew/dispatch while already airborne.

## Slide 3
NIKIN
ORVIT
RAMEL
NALIM
DEVID
PILUN
LISKI
Common scenario in Edmonton
Based on Jan. 6, 2011
“Slower” in front - A346/B772/B77W, M.82 or M.83
“Medium” in the middle - B772/B77W, M.83 or M.84
“Faster” in the back - B744, M.85 or M.86
All going to the same fix (RAMEL), estimating within 20’ of each other, and all requesting FL340/10600m!
Wouldn’t have worked very well!!
N
Notes: Based on Jan. 6, 2011
“Slower” in front - A346/B772/B77W, M.82 or M.83
“Medium” in the middle - B772/B77W, M.83 or M.84
“Faster” in the back - B744, M.85 or M.86
All going to the same fix (RAMEL), estimating within 20’ of each other, and all requesting FL340/10600m!
Wouldn’t have worked very well!!

## Slide 4
NIKIN
ORVIT
RAMEL
NALIM
DEVID
PILUN
LISKI
Common scenario in Edmonton
Typical solutions:
1) Assign all ~A.83. Faster than some want, slower than some want
2) Lower or Higher altitude than optimal for 1 or 2 flights
N
141W
Notes: Typical solutions:
1) Assign all ~A.83. Faster than some want, slower than some want
2) Lower or Higher altitude than optimal for 1 or 2 flights

## Slide 5
NIKIN
ORVIT
RAMEL
NALIM
DEVID
PILUN
LISKI
Jan. 6, 2011 scenario in Edmonton
Lengthy process was started to re-route China Eastern, and Air China was reduced to A.83 (B744)
A relatively good solution, but still not 100% efficient, and very difficult to execute with current rules and procedures…….
N
141W
Notes: Lengthy process was started to re-route China Eastern, and Air China was reduced to A.83 (B744)
A relatively good solution, but still not 100% efficient, and very difficult to execute with current rules and procedures…….

## Slide 6
NIKIN
ORVIT
RAMEL
NALIM
DEVID
PILUN
LISKI
Jan. 6, 2011 scenario in Edmonton
N
Current process is very challenging
3+ hours required, including coordination with dispatch, dispatch with flight, dispatch with ZANC and Russia etc..
Due to great distance between current fixes, some flights might not be able to take a re-route.
Subject to late approval/denial
Ideally this would be a much more efficient process………
420NM
220NM
110NM
160NM
Notes: Current process is very challenging
3+ hours required, including coordination with dispatch, dispatch with flight, dispatch with ZANC and Russia etc..
Due to great distance between current fixes, some flights might not be able to take a re-route.
Subject to late approval/denial
Ideally this would be a much more efficient process………

## Slide 7
NIKIN
ORVIT
RAMEL
NALIM
DEVID
PILUN
LISKI
Addition of new fixes……..
NEW
NEW
NEW
NEW
NEW
Addition of new fixes will make tactical re-routes easier and more viable
Shorter distance between current and new fixes means most flights should be able to take a re-route if needed &/or requested.
N
141W
Notes: Addition of new fixes will make tactical re-routes easier and more viable
Shorter distance between current and new fixes means most flights should be able to take a re-route if needed &/or requested.

## Slide 8
NIKIN
ORVIT
RAMEL
NALIM
DEVID
PILUN
LISKI
Addition of new fixes……..
Better Solution? Tactical reroutes for 1 or 2 flights.
In this example, likely reroute the 2nd and 3rd aircraft – perhaps one to the north and one to the south? Both to the north? Both to the South? Many options available.
Will result in higher probability of every flight attaining requested speed and altitude, even with RVSM throughout entire flight.
NEW
NEW
NEW
NEW
NEW
N
141W
Notes: Better Solution? Tactical reroutes for 1 or 2 flights.
In this example, likely reroute the 2nd and 3rd aircraft – perhaps one to the north and one to the south? Both to the north? Both to the South? Many options available.
Will result in higher probability of every flight attaining requested speed and altitude, even with RVSM throughout entire flight.

## Slide 9: Going Forward…..
NavCanada will continue to identify conflicts and make re-route recommendation(s) to airline(s). Willing to participate in future Polar reroute trials.
Airlines: 1) A willingness to go through the reroute process, 2) Greater use of GRL, ETMS/ASD/DOTS++ etc. to “file away” from busy fixes to “less busy” fixes (easier with new fixes closer together); and, 3) in lieu of accepting a re-route, deciding on an altitude and/or speed adjustment instead.
FAA/Russia – Streamline current procedures to be more timely and efficient.
Notes: NavCanada will continue to identify conflicts and make re-route recommendation(s) to airline(s). Willing to participate in future Polar reroute trials.
Airlines: 1) A willingness to go through the reroute process, 2) Greater use of GRL, ETMS/ASD/DOTS++ etc. to “file away” from busy fixes to “less busy” fixes (easier with new fixes closer together); and, 3) in lieu of accepting a re-route, deciding on an altitude and/or speed adjustment instead.
FAA/Russia – Streamline current procedures to be more timely and efficient.

## Slide 10: Questions/Discussion
??