## Slide 1: FANS-1A Over Iridium and Performance Based Communications Concept
PARC CWG
Recommendations
Presented to: CPWG/11
Presented By: Federal Aviation Administration

## Slide 2: INTRODUCTION
Since 2007, use of the Iridium satellite voice and data communication services have been supporting air transportation.
ACARS over Iridium (AOI) for aeronautical operational control (AOC).
In 2010, ICAO issued Doc 9925, Manual on the AMS(R)S, to provide the guidance material on the use of Iridium for communications supporting air traffic services (ATS).
Air navigation service providers (ANSPs) are looking at Iridium as a viable solution to improve air traffic control (ATC) communications.
PARC recommendations address the use of Iridium in FANS 1/A operations for communications and surveillance

## Slide 3: DISCUSSION
HISTORY
  The Performance-based Operations Aviation Rulemaking Committee Communications Working Group (PARC CWG) initiated the FANS 1/A over Iridium (FOI) project in 2008.
  Purpose to advance communication technology and leverage existing capabilities to meet operational needs.
  The project, completed in August 2010, substantiates recommendations provided in this report.

## Slide 4: Performance-based Operations Aviation Rulemaking Committee Communications Working Group (PARC CWG)
The PARC CWG is evaluating:
  Iridium SBD – Alternative to I3 Inmarsat Classic Aero (current);
  Inmarsat – I4 Classic Aero and Swift Broadband (next generation);
  ARINC – High frequency data link (HFDL) for some performance-based operations and backup to satellite data; and
  Satellite Voice Communications (Iridium and Inmarsat)
  NextGen - Communications supporting the next generation air transportation system (NextGen).

## Slide 5: RECOMMENDATIONS
  Recommendation 1. Expedite the steps necessary to remove restrictions on current FOI operations to realize immediate gains in efficiency and safety benefits.
  Rationale. Iridium is viable for CPDLC/RCP 240 and ADS‑C/type 180 operations.
  Reduced separations. Apply reduced ADS‑C based separations between FOI aircraft and other aircraft. Aircraft have been certified with FOI capability and operators have received their authorization to use the FOI. The operators also have their RNP 4 authorization.
  Position reporting and identification. Coordinate with Japanese Civil Aviation Bureau (JCAB) and the Civil Aviation Authority of the Fiji Islands on the possibility of removing additional position reporting and identification requirements for FOI aircraft. For FOI aircraft to participate in FANS 1/A operations.
  FANS 1/A over Iridium Evaluations: Evaluations were conducted on ADS‑C report delivery and CPDLC transaction latencies, in accordance with the GOLD. The evaluations considered latency on ADS-C reports, actual communication technical performance (ACTP), actual communication performance (ACP), and pilot operational response time (PORT).

## Slide 6: RECOMMENDATIONS
RECOMMENDATION 2 - In the near and mid terms, plan for and implement a performance-based framework for RCP and surveillance performance specifications.
Rationale. Implementation of a performance-based framework will enable ANSPs to apply different service levels to eligible operators and leverage “less capable” aircraft in the same airspace.
Timely implementation. Begin implementing a performance-based framework now and in the near term. Based on ICAO Doc 9869, Manual on Required Communication Performance (RCP), initial performance specifications are already provided in the ICAO GOLD,
The NAT Region, the Asia-Pacific Region, and the South Atlantic Sub-Region have formally accepted the GOLD.
The performance-based framework is flexible to add performance specifications in the near and mid terms to support other operational needs.

## Slide 7: RECOMMENDATION 2
Global coordination. Globally coordinate with ICAO and regional ATS coordinating groups to specify and prescribe airspace and service provision requirements and to recognize and use guidance material to qualify operators and aircraft capability for seamless operations, performance and interoperability. As a minimum, changes are needed to:
  Procedures for Air Navigation Services — Air Traffic Management (PANS-ATM, ICAO Doc 4444) using performance specifications to provide global communication, navigation and surveillance (CNS) criteria for the performance-based operation, and the criteria for flight plan formats to identify aircraft equipment and capability.
  Regional Supplementary Procedures (Regional SUPPs, ICAO Doc 7030,) to provide the applicable airspace where and when a State or Region implements a performance-based operation, and to include any supplemental requirements for the operator, the aircraft equipage, flight planning, and the air traffic service provision.

## Slide 8: RECOMMENDATION 2
Specify criteria for the intended performance-based operation.
  Revise ICAO Doc 4444 and other documents, as necessary, to specify the communication and surveillance capability and performance criteria based on the ICAO Doc 9869, Manual on RCP and the GOLD, together with the performance-based navigation criteria provided by ICAO Doc 9613, Performance-based Navigation (PBN) Manual.

## Slide 9: FAA ACTION
  The FAA has accepted the recommendations of the PARC-CWG. All restrictions to the use of Iridium in the FAA controlled Oceanic airspaces are being removed. The use of FANS-1A over Iridium and the Performance capability of RCP-240, as well as RSP-180, with RNP-4 will allow Ocean 21 to apply 50nm longitudinal or 30 / 30nm separation standard on a “target of opportunity” basis.
  The development of a Performance Based Communication Concept has been commenced and will be reflected in our guidance material and certification process.

## Slide 10: ACTION BY THE MEETING
The meeting is requested to consider the removal of all restrictions to the use of FANS over Iridium and to assist in the implementation of a Performance Based Communication Concept.