## Slide 1
Edmonton Area Control Centre presentation to the CROSS POLAR WORKING GROUP “CAATS Efficiency Gains In Polar Operations” Санкт-Петербург, Россия June 7-10, 2011 Presented by: Брион Карлсон (Bryon Carlson) Edmonton ACC North High Supervisor
Notes: <number>
<number>
Also Present at CPWG –
Butch March, Manager Area Control Centre Operations, Edmonton

## Slide 2: CAATS
Three main efficiency gains in Polar Operations from the introduction of CAATS.
1) Reduction of longitudinal separation standard from 15’ to 10’ in most instances.
2) Automated estimate passing; and,
3) Introduction of the “Planning function.”
Notes: Three main efficiency gains in Polar Operations from the introduction of CAATS.
1) Reduction of longitudinal separation standard from 15’ to 10’ in most instances.
2) Automated estimate passing; and,
3) Introduction of the “Planning function.”

## Slide 3: Longitudinal Separation
Previously, in the case of aircraft not on identical tracks, 15’ was needed at the common point, unless able to manually determine the common point, and unless able to prove ≥10’ through use of distance and groundspeed checks.
In areas of poor comm. (polar), this was difficult to do.
Now CAATS automatically calculates the estimates at the common point (even it is not a mutual filed point), allowing Controllers to apply 10’ standard without additional calculations..........
Supporting the continued use of random routes, and
Allowing greater time to provide other services.
COALL
Notes: Previously, in the case of aircraft not on identical tracks, 15’ was needed at the common point, unless able to manually determine the common point, and able to prove ≥10’ through use of distance and groundspeed checks.
In areas of poor comm. (polar), this was difficult to do.
Now CAATS automatically calculates the estimates at the common point (even it is not a mutual filed point), allowing Controllers to apply 10’ standard without additional calculations..........
Supporting the continued use of random routes, and
Allowing greater time to provide other services.

## Slide 4: Automated Estimate Passing
The introduction of automated estimate passing (NAMICD) has reduced Controller workload.
Allows more time to provide other services.
Notes: The introduction of automated estimate passing (NAMICD) has reduced Controller workload.
Allows more time to provide other services.

## Slide 5: Planning Function
Use of the “Planning Function” in CAATS allows for greater opportunities to identify, and solve, potential traffic conflicts earlier & in a more optimal manner.
Allows Controllers to effectively re-calculate estimates, at different speeds and altitudes, and on different routes, without interfering with the aircraft’s actual flight plan.
A combination of the two improvements (on previous slides) has allowed more time for this function.
Notes: Use of the “Planning Function” in CAATS allows for greater opportunities to identify, and solve, potential traffic conflicts earlier & in a more optimal manner.
Allows Controllers to effectively re-calculate estimates, at different speeds and altitudes, and on different routes, without interfering with the aircraft’s actual flight plan.
A combination of the two improvements (on previous slides) has allowed more time for this function.

## Slide 6: CAATS
Three seemingly small, but very substantive, efficiency gains!
All a direct result of CAATS implementation
Notes: Three seemingly small, but very substantive, efficiency gains!
All a direct result of CAATS implementation

## Slide 7: Questions ??
??