## Slide 1: Introduction to Required Communication Performance (RCP) and Required Surveillance Performance (RSP)
Trent Bigler, FAA, Aviation Safety Inspector
7 December 2011
Notes: Read Slide.

## Slide 2: Introduction
Guidance & Directives
2. Required Communication Performance
  - RCP 400
  - RCP 240
3. Required Surveillance Performance
  - RSP 400
  - RSP 180
Notes: Today’s presentation we will discuss the current guidance and directives concerning Required Communication Performance (RCP)/RCP 400 and RCP 240 and Required Surveillance Performance (RSP)/ RSP 400 and RSP 180 specifications.

## Slide 3: Guidance Publications For RCP and RSP
ICAO Doc 4444 and ICAO Annexes 2,6,10, and 11
Global Operational Data Link Document (GOLD), 14 June 2010
-- Derived from these documents
    RTCA DO-306 Safety and Performance Standard for Air Traffic Data Link Services in Oceanic and Remote Airspace (Oceanic SPR Standard), 11 October 2007
    ICAO Document 9869, Manual on Required Communication Performance, First Edition, 2008
Notes: Guidance Publications for RCP and RSP:
- Global Operational Data Link Document (GOLD), 14 June 2010. This is the Internationally endorsed Data Link resource. Currently second edition is being vetted in Paris October 2011.
- RTCA DO-306 Safety and Performance Standard for Air Traffic Data Link Services in Oceanic and Remote Airspace (Oceanic SPR Standard),
11 October 2007.
- ICAO Doc 4444 and ICAO Annexes 2,6,10, and 11.
- ICAO Document 9869, Manual on Required Communication Performance, First Edition, 2008
These listed guidance and directives were used to develop a simplistic presentation defining RCP and RSP.

## Slide 4: Authorization Requirement
ICAO Annex 6, Chapter 7
7.1.3 For flights in defined portions of airspace or on routes where an RCP type has been prescribed, an aeroplane shall, in addition to the requirements specified in 7.1.1:
  a) be provided with communication equipment which will enable it to operate in accordance with the prescribed RCP type(s); and
  b) be authorized by the State of the Operator for operations in such airspace.
Notes: Authorization Requirement:
ICAO Annex 6, Chapter 7 states:
7.1.3 For flights in defined portions of airspace or on routes where an RCP type has been prescribed, an aeroplane shall, in addition to the requirements specified in 7.1.1:
  a) be provided with communication equipment which will enable it to operate in accordance with the prescribed RCP type(s); and
  b) be authorized by the State of the Operator for operations in such airspace.

## Slide 5
S
N
C
Performance Based Operations
Balances capability & performance of:
ATM
RCP
RNP
RSP
Navigation
Communications
Surveillance
Air Traffic Management (ATM)
(RNP)
(RCP)
(RSP)
RNP – required navigation performance
RCP – required communication performance
RSP – required surveillance performance
Notes: Performance Based Operations concept is based on Communications, Navigation and Surveillance or CNS elements. Consider each a leg of the ATM stool. All legs of the stool need to be defined and fully functional to support the NAS.
Required Navigation Performance RNP has been well advanced with GNSS equipage and defined RNP4/RNP10 aircraft equipage. This is a strong, well defined leg of the PBO Stool.
Now in this presentation we will explain RCP and RSP requirements:
- Required Communication Performance (RCP)
- Required Surveillance Performance (RSP)
Which are the other two legs of the stool. These RCP and RSP specifications will further advance and define requirements.
ATM will use in all three of these legs or performance specifications to safely utilize the entire airspace and increase capacity and efficiency.

## Slide 6
Required Communication Performance
A statement of communication performance necessary for a particular operation or service.
  Operationally derived and not based on any specific techniques, technologies and/or architecture.
  Defined for an operational communication transaction (two-way)
  Includes both human and technical elements
  Applies to both voice and data link communications
Notes: Read slide.
Operationally derived simply means that as long as the equipment meets or exceeds the required performance standards that equipment is deemed acceptable. For example, if I build a avionics data link box for my airplane in my garage and it meets the required performance specifications it is acceptable.
Defined for an operational communication transaction (two-way), this is commonly referred to as End-to-End communication. This End-to-End message loop will be more clearly defined later in this presentation.
Includes both Human and Technical Elements:
Humans are involved in the message loop
Technical elements refer to the ground and aircraft systems that provide the data link passageway up to the aircraft and back to the ground.
This applies to voice and data link communications.

## Slide 7: GOLD / RTCA DO-306
RCP Specifications | Intended uses for which RCP specification is applicable
RCP 400 | - Technology other than HF voice radio is normal means of communications -- Lateral separation ≥ 50 NM -- Time-based longitudinal separation (10 min or greater)
 | - Technology other than HF voice radio is alternative means of communications -- Lateral separation = 30 NM lateral -- Reduced longitudinal separation minima
RCP 240 | - CPDLC is the primary means of communications -- Lateral separation = 30 NM -- Reduced longitudinal separation minima
Notes: IAW the guidance documents previously mentioned:
Only Two RCP Specifications are defined either RCP 400 or RCP 240.
The numbers 400 or 240 in the list refer to the maximum End-to-End message loop in seconds.
So, for RCP 400 that means the maximum elapsed time for the message is 400 seconds or 6.667 minutes. RCP 400 row from the chart is the specifications defined for the aircraft separation standards of:
- Lateral Separation of 50 nm or greater
- Time-based longitudinal Separation 10 minutes or greater.
+++ This is how we fly in the Oceanic today.
RCP 240 row from the chart is the specification defined for the aircraft separation standards of:
- Lateral Separation of 30 nm
- Reduced Longitudinal Separation Minima.

## Slide 8: RCP specification is…
A label that defines a performance standard for operational communication transactions (e.g. RCP 400)
Provides allocations to the air traffic service provider (ATSP), communication service provider (CSP), aircraft operator and aircraft system
Denotes operational values for:
  Communication transaction time
  RCP Continuity
  RCP Availability
  RCP Integrity
Notes: Read slide
Under the operational values for:
Communication Transaction Time
RCP Continuity
RCP Availability
RCP Integrity
These last three terms, Continuity, Availability and Integrity are used in RNP, RCP and RSP which are the other two legs of the three leg CNS stool.
I will further define these terms on the next slide.

## Slide 9
RCP Communication Transaction Time - The maximum time for the completion of the transaction after which the initiator should revert to an alternative procedure.
RCP definitions
RCP Continuity - Probability that a transaction can be completed within the communication transaction time given that the service was available at the start of the transaction.
- Either expiration time (ET) or nominal time (TT) of 95%
RCP Availability - Probability that a transaction can be initiated when needed.
RCP Integrity - Probability that a transaction is completed with no undetected errors.
Operational communication transaction - The process a human uses to send an instruction, a clearance, flight information and/or a request. The process is completed when that human is confident that the transaction is complete.
Notes: Read the entire slide:
Note — Whilst RCP integrity is defined in terms of the “goodness” of the communication capability, it is specified in terms of the likelihood of occurrence of malfunction on a per flight hour basis, e.g. 10-5, consistent with RNAV/RNP specifications.
Integrity - (Probability of an undetected system-induced failure of message transmission.)
ET = expiration time
TT = nominal time
ET and TT will be further discussed in upcoming slides.

## Slide 10: Oceanic RCP specifications (applies to CPDLC)
RCP Specification | Transaction Time (sec) | Continuity | Availability | Integrity
400 | 400 --------------- 350 | 0.999 ----------------------- 0.95 | 0.999 | Malfunction = 10-5 per flight hour
240 | 240 ----------------- 210 | 0.999 --------------------- .95 | 0.999 (safety) 0.9999 (efficiency) | Malfunction = 10-5 per flight hour
CPDLC – Controller Pilot Data Link Communication
Notes: READ Slide:
RCP 400 communication service availability
0.999 for safety, per DO-306/ED-122
–On a per Oceanic ATC Centre (OAC) basis (0.999)
•No more than 24 outages greater than 20 minutes for any 12 month period
•Failures causing outages for multiple OACs are not counted more than once
•No more than 9 hours of total downtime for any 12 month period
RCP 240 communication service availability
0.999 for safety, per DO-306/ED-122
0.9999 for operational efficiency
–On a per Oceanic ATC Centre (OAC) basis (0.9999)
•No more than 4 outages greater than 10 minutes for any 12 month period
•Failures causing outages for multiple OACs are not counted more than once
•No more than 50 minutes of total downtime for any 12 month period
Monitoring and alerting requirement
–RCP 240 –After an outage begins, the communications service shall provide ATC automation with a positive indication that there is an outage within 5 minutes
–RCP 400 –After an outage begins, the communications service shall provide ATC automation with a positive indication that there is an outage within 10 minutes

## Slide 11
RCP Type
Intervention
clearance
issued
Controller /
HMI
ATSU
System
TRN
RCTP
CSP
System
Flight Crew /
HMI
Aircraft
System
Aircraft
System
CSP
System
ATSU
System
Controller /
HMI
Controller
confident
transaction
complete
RCTP
communication transaction time
PORT
Clearance
acknowledgement
received
RCP 400
99.9% ≤ 60 sec
95% ≤ 60 sec
RCP 400
99.9% ≤ 310 sec
95% ≤ 260 sec
RCP 400
99.9% ≤ 370 sec
95% ≤ 320 sec
RCP 400
99.9% ≤ 400 sec
95% ≤ 350 sec
ATM System
RCTP – Required Communication Technical Performance
PORT – Pilot Operational Response Time
TRN – Monitored Operational Performance
HMI – Human Machine Interface
Notes: OK – here’s a depiction of a typical communication between ATC and the pilot. In this example we’re looking at RCP 400.
ATC decides an intervention clearance needs to be issued and types it in their system then hits send. The data flows from controller, through the Air Traffic Servicing Unit system through the Communication Service Provider (ARINC/SITA) to the aircraft. If you look at the orange color, the time it takes the clearance to get from the ATC system to the flight deck is Required Communication Technical Performance (RCTP). Since this is an end-to-end loop, we have to account for both sides of the loop giving us the RCPT allocation shown in the orange box.
Once the flight deck is informed of the incoming message, they have up to 60 seconds (no matter what RCP value operating under) to answer ATC. This is called Pilot Operational Response Time or PORT (shown in light blue). This allocation has been one of the areas we consistently see not being met due to various reasons (i.e. pilot awareness of the allocation, company re-clearance procedures, etc).
Adding the RCPT and PORT together gives the Monitored Operational Performance (green). The portion of the transaction time (used for intervention) that does not include the times for message composition or recognition of the operational response.
Once the operational response gets back to the controller (and they are confident the transaction is complete) the loop is complete giving us the RCP value (dark blue).
You’ll notice there are 30 seconds missing. This time is allocated to the initiator to acknowledge communication transaction is complete.
Be advised, all time allocations are monitored. The monitoring agency provides reports showing if the RSP values are being met and where in the process the allocations are not being met. To date, certain aircraft have been identified as having improper functioning equipment and fro maintenance purposes, the company has been informed.

## Slide 12
RCP Type
Intervention
clearance
issued
Controller /
HMI
ATSU
System
TRN
RCTP
CSP
System
Flight Crew /
HMI
Aircraft
System
Aircraft
System
CSP
System
ATSU
System
Controller /
HMI
Controller
confident
transaction
complete
RCTP
communication transaction time
PORT
Clearance
acknowledgement
received
RCP 240
99.9% ≤ 60 sec
95% ≤ 60 sec
RCP 240
99.9% ≤ 150 sec
95% ≤ 120 sec
RCP 240
99.9% ≤ 210 sec
95% ≤ 180 sec
RCP 240
99.9% ≤ 240 sec
95% ≤ 210 sec
RCTP – Required Communication Technical Performance
PORT – Pilot Operational Response Time
TRN – Monitored Operational Performance
HMI – Human Machine Interface
Notes: This example is the same as the previous on except this shows RCP 240.

## Slide 13: RCP Availability Criteria
Availability parameter | Efficiency | Safety | Compliance means
Service Availability (A CSP) | N/A | .999 | Contract/service agreement terms
Unplanned outage duration limit (min) | N/A | 20 | Contract/service agreement terms
Maximum number of unplanned outages (per year) | N/A | 24 | Contract/service agreement terms
Maximum accumulated unplanned outage time (min/yr) | N/A | 520 | Contract/service agreement terms
Unplanned outage notification delay (min) | N/A | 10 | Contract/service agreement terms
Specification RCP 400/D | Application: CPDLC | Component: CSP
CPDLC – controller pilot data link communications
CSP – communication service provider
Notes: Read Slide:
Reading across chart, this is a Specification for RCP 400/D (data), Application is for CPDLC and the component Communication Service Provider (CSP). This tells the CSP the requirements for the RCP 400/Data. Meaning the End-to-End for the RCP 400/D defines under the Safety row the .999 Availability. Further, any unplanned outage duration can last no longer then 20 minutes. 24 is the Number of Maximum unplanned outages per year. Maximum accumulated unplanned outage time is 520 minutes per year. Unplanned outage notification delay of 10 minutes.

## Slide 14: RCP Availability Criteria
Availability parameter | Efficiency | Safety | Compliance means
Service Availability (A CSP) | .9999 | .999 | Contract/service agreement terms
Unplanned outage duration limit (min) | 10 | 10 | Contract/service agreement terms
Maximum number of unplanned outages (per year) | 4 | 48 | Contract/service agreement terms
Maximum accumulated unplanned outage time (min/yr) | 52 | 520 | Contract/service agreement terms
Unplanned outage notification delay (min) | 5 | 5 | Contract/service agreement terms
Specification RCP 240/D | Application: CPDLC | Component: CSP
Notes: Read Slide:
Reading across chart, this is a Specification for RCP 240/D (data), Application is for CPDLC and the component Communication Service Provider (CSP). This tells the CSP the requirements for the RCP 240/Data.
Meaning the End-to-End for the RCP 240/D defines under the Safety row the .999 Availability. Further, any unplanned outage duration can last no longer then 10 minutes. 48 is the Number of Maximum unplanned outages per year. Maximum accumulated unplanned outage time is 520 minutes per year. Unplanned outage notification delay of 5 minutes.
This more stringent time requirement of End-to-End for the RCP 240/D defines under the Efficiency row the .9999 Availability. Further, any unplanned outage duration can last no longer then 10 minutes. Number of Maximum of 4 unplanned outages per year. Maximum accumulated unplanned outage time is 52 minutes per year. Unplanned outage notification delay of 5 minutes.
This Efficiency column, as you can see, is a very stringent requirement that the CSP must ensure they can attain.

## Slide 15: And here we conduct our flight
En Route
Oceanic
Terminal
En Route
Terminal
TOD
RCP 10/V - Basic
RCP 60/D - IC
RCP 400/V - Basic
RCP 240/D - RHSM
RCP 10/V - Basic
RCP 400/D – IC
RCP 60/D - TAP
SATCOM radio fails
5. Ground side monitors communication service
6. Air side monitors aircraft system
7. Pilot/controller receives alerts for communication failures
2. Eligible Operators file for service level(s)
3. Pilot/controller know RCP type, just as they know RNAV/RNP type
1. RCP types for service level(s) published in AIPs and charts
4. Pilot/controller operates according to RCP type
GES Outage
/D - Data
/V - Voice
IC – Increased capacity
RHSM – Reduced horizontal separation minima
TAP – Tailored Arrival Procedure
Notes: Here we see possible future RCP applications associated with phases of flight. As a reminder, only RCP 400 and RCP 240 are currently defined.
During the flight, we see the following:
RCP types for service level(s) will be published in AIPs and/or charts.
Eligible Operators will file for service level(s) they are authorized to use.
Aircrew and controller will know RCP type just like they know RNAV/RNP type
Ground Side (ATC) and Air Side (Crew) will monitor their respective systems (Aircraft or communication service).
When either receive an alert for communication failures, they will notify the other
New level of service will be established based on error type, etc.

## Slide 16
      Any questions on RCP?
Notes: Read slide

## Slide 17: Evolution of Surveillance
Voice Position Report
Secondary surveillance radar (SSR)
ADS-C
Primary surveillance radar
Notes: Before we move on to RSP (Required Surveillance Performance), let’s review the history of current surveillance methods. As you know, the original surveillance method was pilot position reports. Something like: “I’m over Tower Rock heading north to the coliseum.”
With the advent of radar, the need for pilot reports in domestic airspace is no longer needed. ATC monitors flight progress using primary and secondary radar. But what happens if you are in oceanic or remote airspace and radar is not available? ATC reverts back to procedural surveillance using pilot reports. This method has worked fine for many years, but today, I’m sure you’ve all experienced it or heard about using the HF radio in the North Atlantic Track System. It is not uncommon to see frequency saturation or just plain frequency unavailability due to atmospheric conditions.
Today’s aviation environment (and future planning) have forced industry to develop ways to increase safety, capacity and efficiency. Voice reports have proven to be a drawback to those three areas. So instead, industry has developed a real-time way of surveillance call ADS-C (Automatic Dependent Surveillance – Contract). Don’t get ADS-C confused with ADS-B. ADS-B constantly emits information and requires ground-based antennas. ADS-C monitors your aircraft systems and reports information to ATC on request (i.e. by contract). ATC can request a combination of data delivered either periodically, on demand or by event.
To get the most out of this system, just like the Navigation (RNP) and Communication (RCP) leg of the ATM stool, the Surveillance “leg” is being defined by RSP.

## Slide 18: Required Surveillance Performance - RSP
Defines high-level surveillance system performance requirements.
Operationally derived and not based on any specific techniques, technologies and/or architecture.
Includes both ground and airborne systems.
Supports a particular ATM application (e.g. reduced separation)
Notes: Read slide:
High-level system performance requirements for surveillance applications independent of technology and architecture. Remember building the box in my garage example.
The surveillance requirements according to the airspace involved. The surveillance system must provide the updated aircraft position in order to ensure a safe separation. In low- traffic oceanic / remote airspace, position information should be updated every 12 seconds. In high-traffic airspace, position information should be updated every 4 seconds. The surveillance system should allow users to select the preferred en-route flight path and conform fully to emergency procedures, contribute to search and rescue operations, and to allow for the application of separation in a defined airspace. RSP (Required Surveillance Performance) defines high-level system technical performance requirements independent of technology and architecture to be met by a surveillance system in order to support a particular ATM application.
An ATM surveillance application uses the information delivered by the surveillance system to provide an ATM service.
RSP could be set for both existing and new applications of surveillance information, both on the ground and in the air.
RSP is a set of high level system requirements independent of techniques in order to keep the maximum of flexibility for the design of the surveillance system. Requirements should therefore be on the final output of the surveillance system. RSP applies to a system which includes ground and airborne sub-systems.
RSP is a set of technical requirements which will be used by regulatory authorities. In support of these authorities RSP will be used to establish technical system design and in procurement, commissioning, and monitoring of surveillance systems. Performances requirements shall therefore be measurable and verifiable.
RSP is established per ATM application in order to understand the reasons driving the performance requirements. It also avoids the implementation of over-specified surveillance systems. Indeed, the required RSP for the surveillance system will in that way be limited to those surveillance applications which will make use of the system.

## Slide 19
RSP specification | Intended uses for which surveillance type is applicable
400 | - ADS‑C or FMC WPR is the normal means of surveillance -- Lateral separation ≥ 50 NM -- Time-based longitudinal separation (10 min or greater)
 | - Technology other than HF voice radio provides an alternative means of surveillance, e.g. position reporting via satellite voice -- Lateral separation = 30 NM -- Reduced longitudinal separation minima
180 | - ADS-C is the normal means of surveillance -- Lateral separation = 30 NM -- Reduced longitudinal separation minima
GOLD / RTCA DO-306
Notes: IAW the guidance documents previously mentioned:
Only Two RSP Type Specifications are defined either Type 400 or Type 240.
The numbers 400 or 180 in the list refer to the maximum End-to-End surveillance loop in seconds.
So, for Type 400 that means the maximum elapsed time for the surveillance is 400 seconds or 6.667 minutes. Type 400 row from the chart is the specifications defined for ADS-C or FMC WPR (flight management Computer Waypoint Position Reporting) aircraft separation standards of:
- Lateral Separation of 50 nm or greater
- Time-based longitudinal Separation 10 minutes or greater.
+++ This is how we fly in the Oceanic today.
Type 180 row from the chart is the specification defined for ADS-C aircraft with separation standards:
- Lateral Separation of 30 nm
- Reduced Longitudinal Separation Minima.

## Slide 20: RSP specification is…
A label (e.g. type 400) that represents the values assigned to surveillance performance parameters for:
  Surveillance data transit time
  RSP Continuity
  RSP Availability
  RSP Integrity
Provides allocations to the air traffic service provider, communication service provider, aircraft operator and aircraft system
Notes: Read slide:
Remember Continuity, Availability and Integrity.

## Slide 21: RSP definitions
Surveillance data transit time - The required time for surveillance data delivery.
RSP Continuity - The required probability that surveillance data can be delivered within the delivery time parameter given that the service was available at the start of delivery.
- Either Overdue Time (OT) or nominal delivery time (DT) of 95%
RSP Availability - The required probability that surveillance data can be provided when needed.
RSP Integrity - The required probability that surveillance data is delivered with no undetected error.
Notes: Read slide:
Note.— Surveillance integrity includes such factors as the accuracy of time, correlating the time at aircraft position, reporting interval, data latency, extrapolation and/or estimation of the data.
OT = overdue delivery time The maximum time for the successful delivery of surveillance data after which the initiator is required to revert to an alternative procedure.
DT = nominal delivery time The maximum nominal time within which 95% of surveillance data is required to be successfully delivered.

## Slide 22: Oceanic Surveillance Performance Specification (applies to ADS-C)
RSP Specification | Surveillance delivery time (Sec) | Continuity | Availability | Integrity
400 | 400 ----- 300 | 0.999 --------- 0.95 | 0.999 | Navigation FOM (see note below)
 |  |  |  | Time at position accuracy ± 1 sec (UTC)
 |  |  |  | Data Integrity Malfunction = 10 -5 per flight hour
180 | 180 ----- 90 | 0.999 --------- 0.95 | 0.999 (safety) ------------ 0.9999 (efficiency) | Navigation FOM (see note below)
 |  |  |  | Time at position accuracy ± 1 sec (UTC)
 |  |  |  | Data Integrity Malfunction = 10 -5 per flight hour
Note: The navigation figure of merit (FOM) is specified on the navigation criteria associated with this specification.
Notes: The navigation figure of merit (FOM) is specified based on the navigation criteria associated with this spec. For example, if RNP 4 is prescribed, then for ADS-C surveillance service, the FOM level would need to be 4 or higher. In all cases, when the navigation capability no longer meets the criteria specified for the operation, the flight crew is responsible for reporting the non-compliance to ATC in accordance with ICAO procedures.

## Slide 23: RSP 400 – time / continuity
Flight Crew /
HMI
Aircraft
System
CSP
System
ATSU
System
Controller /
HMI
Surveillance Data Delivery
RSP
400
Surveillance
Data
RSTP AIR
RSTP
RSTP ATSP
RSTP CSP
Time at position,
or, for ATSU
System
monitoring, time
expected at
Position.
RSP 400
99.9% ≤ 30 sec
95% ≤ 15 sec
RSP 400
99.9% ≤ 340 sec
95% ≤ 270 sec
RSP 400
99.9% ≤ 30 sec
95% ≤ 15 sec
RSP 400
99.9% ≤ 400 sec
95% ≤ 300 sec
RSTP – Required Surveillance Total Performance
Notes: This slide isn’t as fancy as the corresponding RCP slide, but here’s a breakdown of RSP 400 allocations.
In this example, the aircraft is at a position and is automatically relaying the position report to ATC (according to the ATC contract through ADS-C) . As the data moves from system to system (Aircraft to ATC) there are times that must be met (required surveillance total performance) according to either the 99.9 or 95 percentile. Add all these times (allocations) and you get the RSP.
Just like RCP, RSP is monitored and reports are generated.

## Slide 24: RSP 180 – time / continuity
Flight Crew /
HMI
Aircraft
System
CSP
System
ATSU
System
Controller /
HMI
Surveillance Data Delivery
RSP180
Surveillance
Data
RSTP AIR
RSTP
RSTP ATSP
RSTP CSP
Time at position,
or, for ATSU
System
monitoring, time
expected at
Position
RSP 180
99.9% ≤ 5 sec
95% ≤ 3 sec
RSP 180
99.9% ≤ 170 sec
95% ≤ 84 sec
RSP 180
99.9% ≤ 5 sec
95% ≤ 3 sec
RSP 180
99.9% ≤ 180 sec
95% ≤ 90 sec
RSTP – Required Surveillance Total Performance
Notes: This example is the same as the previous one except it shows RSP 180 allocations.

## Slide 25: Surveillance Availability Criteria
Availability parameter | Efficiency | Safety | Compliance means
Service Availability (A CSP) | N/A | .999 | Contract/service agreement terms
Unplanned outage duration limit (min) | N/A | 20 | Contract/service agreement terms
Maximum number of unplanned outages (per year) | N/A | 24 | Contract/service agreement terms
Maximum accumulated unplanned outage time (min/yr) | N/A | 520 | Contract/service agreement terms
Unplanned outage notification delay (min) | N/A | 10 | Contract/service agreement terms
Specification Type 400 | Application ADS-C | Component: CSP
Notes: Read Slide:
Reading across chart, this is a Specification for Type 400, Application is for ADS-C and the component Communication Service Provider (CSP). This tells the CSP the requirements for the Type 400. Meaning the End-to-End for the Type 400 defines under the Safety row the .999 Availability. Further, any unplanned outage duration can last no longer then 20 minutes. 24 is the Number of Maximum unplanned outages per year. Maximum accumulated unplanned outage time is 520 minutes per year. Unplanned outage notification delay of 10 minutes.

## Slide 26: Surveillance Availability Criteria
Availability parameter | Efficiency | Safety | Compliance means
Service Availability (A CSP) | .9999 | .999 | Contract/service agreement terms
Unplanned outage duration limit (min) | 10 | 10 | Contract/service agreement terms
Maximum number of unplanned outages (per year) | 4 | 48 | Contract/service agreement terms
Maximum accumulated unplanned outage time (min/yr) | 52 | 520 | Contract/service agreement terms
Unplanned outage notification delay (min) | 5 | 5 | Contract/service agreement terms
Specification Type 180 | Application ADS-C | Component: CSP
Notes: Read Slide:
Reading across chart, this is a Specification for Type 180, Application is for ADS-C and the component Communication Service Provider (CSP). This tells the CSP the requirements for the Type 180.
Meaning the for Type 180 defines under the Safety row the .999 Availability. Further, any unplanned outage duration can last no longer then 10 minutes. 48 is the Number of Maximum unplanned outages per year. Maximum accumulated unplanned outage time is 520 minutes per year. Unplanned outage notification delay of 5 minutes.
This more stringent time requirement for Type 180 defines under the Efficiency row the .9999 Availability. Further, any unplanned outage duration can last no longer then 10 minutes. Number of Maximum of 4 unplanned outages per year. Maximum accumulated unplanned outage time is 52 minutes per year. Unplanned outage notification delay of 5 minutes.
This Efficiency column, as you can see, is a very stringent requirement that the CSP must ensure they can attain.

## Slide 27: RCP / RSP is not the same as RNP
Some similarity, but…
Item | RNP | RCP / RSP
Specifications | exclusive to aircraft and operator | end-to-end system requirements
Monitoring and alerting | real time monitoring and alerting | real-time monitoring and alerting post-implementation monitoring (statistical) and corrective action
 | aircraft and operator | shared between aircraft and ATSP / ATSU
Notes: To review, while there are many similarities with RNP and RCP/RSP, it is important to note the differences between RNP and RCP/RSP. This chart reading across at specifications one can see that RNP is exclusive to aircraft and operator compared to the RCP/RSP is a all encompassing End-to-End System Requirements. Next, reading across the chart at the Monitoring and Alerting row, one can observe RNP has real time monitoring and alerting to the aircraft and operator compared to the RCP/RSP is a shared Monitoring and Alerting between aircraft and ATSP/ATSU (Air Traffic Service Unit).

## Slide 28: Summary
1. Guidance & Directives
2. Required Communication Performance
  - RCP 400
  - RCP 240
4. Required Surveillance Performance
  - RSP 400
  - RSP 180
Notes: In summary, today’s presentation we discussed the current guidance and directives, Required Communication Performance (RCP)/RCP 400 and RCP 240 and Required Surveillance Performance (RSP)/ RSP Type 400 and RSP Type 180 specifications.

## Slide 29
Notes: <number>
Do you have any questions or comments?