## Slide 1: Cross Polar Working Group NAV CANADA Update
Beijing, China
December 6-9, 2010

## Slide 2
Traffic Movements
Yukon Random Route Trial
Technology Improvements
ADS-B
DOTS Plus On-line
CPDLC
RVSM
Topics
<number>

## Slide 3: Edmonton ACC Traffic
Historical Traffic: 2007 – 2011
Notes:   Traffic pattern growth by month.

## Slide 4: Edmonton ACC Traffic
Polar Traffic 2010-2011
Notes:   Traffic pattern growth by month.

## Slide 5: Edmonton ACC Traffic
Polar Traffic by Fix - 2011
Notes:   Traffic pattern growth by month.

## Slide 6: Yukon Random Route Trial
Commenced May 5, 2011
  No requirement to file via published tracks
No significant increase to workload
Trial to be terminated
Random route 24/7 365 days a year
Transport Canada AIM to be updated

## Slide 7: Technology Improvements

## Slide 8
Technology Improvements
Pre-CAATS
No Reduced MACH Number Technique
No RNP10 reduced lateral – 60 NM

## Slide 9
CAATS- November 2010
Reduced MACH Number Technique supported
No RNP10 reduced lateral - 60 NM
Technology Improvements

## Slide 10
CAATS- Post RNP10
Reduced MACH Number Technique supported
RNP10 reduced lateral supported – 50 NM
Technology Improvements

## Slide 11: ADS-B HUDSON BAY
Effective November 24
  ADS-B certified can random route
  Non ADS-B fly via published tracks
Correct filing is essential

## Slide 12: Sample Data from 2011-11-01

## Slide 13: Filing Requirements
In order to correctly process and display ADSB status, two elements required:
  The aircraft Civil Registration must be listed under the current ADSB Canadian Eligibility Document.
  The ADSB data filed in Field 18 of the ICAO Flight Plan must be correctly formatted.
If the aircraft is not eligible – DO NOT FILE - RMK/ADSB

## Slide 14: Field 18 - Accepted Format
The only format acceptable is:
  RMK/ADSB
  ADSB must be the first element listed after the “RMK/”, or re-insert a new “RMK/”, and
  There must be a space inserted after the “B” in order to correctly parse the next element of the remarks.
  Examples: RMK/ADSB_TCAS, or
  RMK/ADSB RMK/TCAS
Notes: <number>
<footer>
<header>
<date/time>
Montreal-Pierre Elliot Trudeau International Airport is one of Canada’s busiest airports, handling 12 million passengers and more than 243,000 aircraft movements each year.
INTAS has been operational here since 2004. NAV CANADA has plans in place for the extension of the INTAS network into the Montreal Airports Gate Management Facility.
The next major enhancement to the INTAS system here will be to take advantage of the latest EXCDS features and the integration of Sensis multilateration.

## Slide 15: Common Formatting Errors
  1. Aircraft is eligible, but ADS-B was not filed as the first element after “RMK/”
    RMK/NRP ADSB TCAS
    NAV/RNP10 ADSB
    RMK/POLAR // ADSB// TCAS
  2. RMK/ADSB is filed, but aircraft is not on eligibility list.

## Slide 16: DOTS Plus Online (DPO)
DPO connection was established Aug19th, 2011
Evaluate over the Winter of 2011 / 2012 on the following criteria:
  “user friendliness” of the application
  potential upgrades and/or changes
Compare GRL times to actual times
Full report at the next CPWG

## Slide 17: CPDLC
Montreal December 15
Edmonton December 18
Four phases

## Slide 18: RVSM 2011
Edmonton is still following the same process – early identification
Benefits observed
      Most noticeable FL360
        Allows more aircraft FL340

## Slide 19: Questions