## Slide 1
<number>
Beijing, China
6 - 9 Dec. 2011
CPWG/12

## Slide 2
<number>
SCAS
Specifying CFDT for Arrival Spacing
Program
One of the techniques of ATFM by issuing CFDT* to the in-flight aircraft.
  *CFDT：Calculated Fix Departure Time
  Departing time at a specified fix on the route of flight

## Slide 3
<number>
Trial of SCAS has commenced
since 25 Aug. 2011
Aircraft subject to this trial are
those bound for Tokyo
international airport (RJTT)
AIC Nr 034/11

## Slide 4
When traffic volume is expected to exceed the capacity of an airport or a sector‥
-
Traffic volume exceeds the capacity of an airport or a sector
<number>
Why is SCAS necessary?
ATMC
Air Traffic Management Center expects traffic volume will exceed the capacity of the airport in 2 or 3 hours.
RJTT
Notes: <number>

## Slide 5
When traffic volume is expected to exceed
the capacity of an airport or a sector‥
-
<number>
Why is SCAS necessary?
EDCT will be assigned to aircraft
at departure airport .
ATMC
ATMC expects safe ,orderly and efficient flow after several hours.
EDCT will be assigned to aircraft concerned by ATMC through ACC.
※EDCT:
Expected Departure
Clearance Time
Before airborne
ACC
EDCT
RJTT
Notes: <number>

## Slide 6
When traffic volume is expected to exceed
the capacity of an airport or a sector‥
-
<number>
Why is SCAS necessary?
EDCT will be assigned to aircraft
at departure airport.
Unexpected airborne delay often make congestion within approach control area. Air Traffic Controller must deal with such delay by radar vector or speed adjustment etc in the Approach control area.
ATC in charge of approach radar control
Before airborne
Air Traffic Flow Management for in-flight aircraft(=SCAS) is necessary .
RJTT
However,
Notes: <number>

## Slide 7
-
<number>
Why is SCAS necessary?
ATMC
When traffic volume is expected to exceed
the capacity of an airport or a sector‥
ACC will issue CFDT (time of passage over a fix) calculated by ATMC to aircraft
ACC
CFDT will be assigned to in-flight aircraft
From Korea, China
From China
From Taiwan・Hong Kong
CFDT is assigned to both domestic and international flights
SCAS will improve traffic congestion within approach control area caused by in-flight time adjustment.
After airborne
CFDT
RJTT
Notes: <number>

## Slide 8
Tokyo International Airport(RJTT)
FIX
<number>
Pilots shall cross the specified fix at CFDT by adjusting speed etc.
CFDT will be issued about 30-80 min before ETA of RJTT.
Procedures of SCAS
ACC
2.PILOT : Response
If pilot accept the CFDT ,read back the time . If not, pilots shall report the acceptable time closest to CFDT to ATC.
1.ACC : Issue CFDT
Cross <FIX> at <CFDT> due to flow control.
3.ACC : Issue revised CFDT
ACC issues revised CFDT the pilot has reported.
1.CFDT
2.Response

## Slide 9
<number>
Congestion of air traffic can be improved by
adjusting crossing time of the specified fix,
which leads to the reduction of ATC work load.
Fuel consumption will be reduced by avoiding
excessive radar vector, especially in lower
altitude .
Equality and effectiveness of ATFM can be
enhanced by covering aircraft from foreign
airports under CFDT, which are not covered by
EDCT.

## Slide 10
<number>
Thank you.
Questions?