## Slide 1: ISAVIA
Cross Polar Meeting
Reykjavik June 19. – 22. 2012

## Slide 2
Delegates from Isavia:
Silli (ATM Specialist)
Steinunn A. Arnardottir (Airspace & Procedures)
Bjarni Stefansson (ATM Development and Implementation specialist)
Leifur Hakonarson (ATM Specialist)
Thordis Sigurdardottir (Manager Operation)

## Slide 3: Government owned limited company
Airports including terminals and duty free
Air Navigation Services
Air Traffic Services
Iceland Radio
Tern Systems ltd
(Software company)

## Slide 5: Sectorization

## Slide 6
BIRD current radar coverage
Notes: The Reykjavik Control Area has a somewhat unique position among ocean areas because of flexibility with respect to both flight routes and flight altitudes. This is made possible by the Flight Control Center's superb technical equipment and unique equipage of radar within the oceanic control area.

## Slide 7: Reykjavik Control Area
Free route airspace
No fixed routes, user preferred tracks
No permanent military airspace

## Slide 10: Communications
HF – Iceland Radio
General Purpose VHF – Iceland Radio
SATCOM – Iceland Radio (and Controller)
DCPC VHF – to support Radar Services
CPDLC – also in Radar Controlled Airspace
  currently only south of 82N

## Slide 11: ATM Systems
FDPS (Flight Data Processing System)
Radar + Situation Display
Integrated Situation Display (ISDS)
Requested flight levels are stored and monitored

## Slide 13: International Traffic in BIRD CTA

## Slide 14: International Traffic in BIRD CTA

## Slide 15: International Traffic in BIRD CTA

## Slide 16: Cross Polar traffic numbers
first 4 months of 2011/2012:

## Slide 17: Cross Polar Traffic
Oceanic clearances north of 70N issued by Reykjavik
CPDLC only south of 82N
  Ask for alt/speed change before 82N
Renewal of maps at Reykjavik Centre
  ULMM – RVSM
  Reykjavik issues oac clr to points at the boundary of ULMM dom/oca. Airlines do not always FPL according to that.
HF blackout. Cross Polar traffic vulnerable to HF blackout.
  Use SATCOM in these instances (or VHF Greenland FIC, Thule)
  Make altitude/speed requests prior to 82N

## Slide 18: Cross Polar Traffic - difficulties
Coordination between centres on traffic routing 65N060W
Flights entering Gander Oceanic and then proceeding either through Montreal airspace and Edmonton airspace, or directly into Edmonton before entering Reykjavík Oceanic shall file as follows:
Aircraft routing over 65N, at or east of 060W, shall file a waypoint at 65N;
Aircraft routing over 65N, west of 060W, shall file via named waypoint by the boundary between Edmonton and Reykjavik, or a waypoint within Edmonton area.
Traffic flying along bdry of Reykjavik/Edmonton

## Slide 19: Cross Polar Traffic
Reqest different altitude/speed when within BIRD area.
Not always optimal altitudes due to crossing traffic
Use of directional levels

## Slide 20: ADS-B Implementation

## Slide 21
BIRD expected ADS-B coverage

## Slide 22
NAT Surveillance Corridor
Current thinking:
No mandates in the surveillance corridor

## Slide 23: Other Current and Pending Projects
50 NM Lateral Separation between MNPS aircraft
ITP
  Trials in radar airspace
  ITP processing has been integrated into the FDPS
2012 FPL
Data Link Mandate
CPDLC Route Reclearances (UM79)
NAT AIDC
5 minutes longitudinal separation (RLongSM)
25 NM lateral separation (RLatSM)
ADS-C CDP

## Slide 24: Questions?