## Slide 1
Edmonton Area Control Centre presentation to the CROSS POLAR WORKING GROUP “DPO Update – A NAV CANADA Perspective”
Reykjavik, Lýðveldið Ísland
June 19-22, 2012
Presented by:
Bryon Carlson
Edmonton ACC North High & Shield Supervisor
Notes: <number>
<number>
<number>
Also Present at CPWG –
Robert Fiege, Manager, Edmonton Area Control Centre Operations

## Slide 2: Getting Started with DPO
Edmonton ACC/NAV CANADA gained access to DPO (“DOTS Plus Online”) in August, 2011, after over 1 year of preparations with the FAA at the IT level.
Fall of 2011 - the connectivity was evaluated.
All “logon/logoff” connections functioned!
Potential for future use of DPO was then further evaluated.
This evaluation took place from Fall/2011 to Spring/2012.

## Slide 3: Evaluating DPO
Initial access level was “Airline Dispatcher,” which is mostly “read only.”
NAV CANADA requires the ability to make changes to DPO…..…
Access level was later upgraded to “TMU” – a level between “Airline Dispatcher” and “Administrator” giving the ability to change the GRL and override TKA’s.
NAV CANADA is the only agency in the world currently with TMU level access.
This access level allows update of DPO/GRL to show “real time” vs. “planned” information.

## Slide 4: Interacting with DPO
If the ability exists to update DPO, the accuracy of entered data must be verified.
Methodology was then developed to verify accuracy, and consistency, of Edmonton’s entered data.
This included a comparison of initial ATC estimates, vs. final pilot estimates (from 141W position), for Russian entry points.

## Slide 5: Interacting with DPO
365 flights were evaluated from Oct 12, 2011 to January 24, 2012.
A sample size of about 12% of all Polar westbound flights between ORVIT & DEVID during that time period.
Sample included most airlines and types across 24 hour range.

## Slide 6: Distribution by Airline & Type
 | Total | B772 | B77L | B77W | B744 | A346 | A388
COA | 9 | 9 |  |  |  |  | 
UAL | 57 | 24 |  |  | 33 |  | 
CES | 31 |  |  |  |  | 31 | 
CCA | 27 |  |  |  | 27 |  | 
ACA | 41 |  | 13 | 28 |  |  | 
KAL | 54 | 9 |  | 13 | 9 |  | 13
DAL | 63 | 8 | 43 |  | 12 |  | 
CPA | 37 |  |  | 37 |  |  | 
CHH | 9 |  |  |  |  | 9 | 
AAL | 19 | 19 |  |  |  |  | 
AAR | 17 | 17 |  |  |  |  | 
EVA | 1 |  |  | 1 |  |  | 

## Slide 7: Interacting with DPO
Three main steps:
1) An initial calculation of 141°W & Russian entry fix times when Current Flight Plan data was received from ATC units to the south (Winnipeg, Montreal, Gander).
2) A second calculation upon actual entry into the Edmonton FIR.
3) A comparison of the calculations in steps #1 & #2, vs. the pilot estimate for the Russian entry point from the 141°W position.

## Slide 8
1st Edmonton Calculation
~-2500NM/-5hr
1st Edmonton Calculation
~-2500NM/-5hr
1st Edmonton Update
~-1700NM/-3.5hr
1st Edmonton Update
~-2200NM/-4.5hr
141ºW Position
-30NM to -150NM
-4’ to -20’
141ºW Position
-150NM to -350NM
-20’ to -45’

## Slide 9: Analysis results
On average, the initial Edmonton calculations were made 5 hours and 7 minutes before the times for the Russian entry points!
On average, the first Edmonton update calculations were made 4 hours and 31 minutes before the times for the Russian entry points!

## Slide 10: Calculation Sheet Sample
Key data:
Time of initial calculation
Speed & altitude for calculation
Initial estimate for 141ºW & Russian entry
Entry time into CZEG
Speed &/or altitude adjustments
1st update for 141ºW/Russian entry
Final 141ºW speed, altitude & time, with ETA for Russian entry

## Slide 11: Analysis results
When comparing the initial Edmonton calculation for the Russian entry point, vs. the final pilot estimate for the Russian entry point (from the 141°W position report), Edmonton was “off” by an average of……………
6 seconds!
As compared to the GRL times being off by an average of 9 minutes!!!
This data includes 2 CPA flights that were cleared off ETOPS routes on to more direct routes, saving 9 & 10 minutes.
Notes: Average/Mean = In mathematics and statistics, the arithmetic mean, or simply the mean or average when the context is clear, is the central tendency of a collection of numbers taken as the sum of the numbers divided by the size of the collection.
Mode = In statistics, the mode is the value that occurs most frequently in a data set or a probability distribution.

## Slide 12
Standard deviation was 2 minutes 20 seconds!
The standard deviation is “a measure of how widely values are dispersed from the average value (the mean).”
Notes: <number>
A negative value occurs when the flight reaches the fix earlier than the estimate. The formula used was actual time minus estimated time.
+9 value was due to a CAATS software error.

## Slide 13
Standard deviation was 1 minute 53 seconds.
Notes: -9 & -10 values were due to a more direct routing for a CPA flight off ETOPS route to direct route.

## Slide 14: Other data collected
Verified average aircraft altitudes & speeds – critical for calculating accurate “long range” estimates, and for determining altitude priority when needed:
Type | Average. Alt. | Mode Alt | Avg. Speed | Mode Speed
A388 | FL368 | FL380 | M.844 | M.840
B772 | FL344 | FL340 | M.829 | M.830
B77L | FL339 | FL340 | M.830 | M.830
A346 | FL335 | FL340 | M.823 | M.820
B744 | FL335 | FL340 | M.850 | M.850
B77W | FL332 | FL340 | M.830 | M.830
Notes: <number>
Altitude averages at 141W. Data also available for individual airlines.

## Slide 15: Altitude distribution @ 141°W
FL300 – 2
FL320 – 81
FL340 – 237
FL350 – 4
FL360 – 29
FL380 – 9
= 358/365 Flights.
+ 141°W data for 5 flights never collected,
+ 2 ACA flights diverted prior to 141W,
= 365 Flights.
Notes: Flights at FL350 @ 141W were cleared to FL360 to reach FL360 by 165W.

## Slide 16: Going forward…
TMU access granted. Attempted to use some of the data calculated in previous slides.
Software issues:
- DPO not updating.
- Old information “stuck” in DPO.
- Able to logon & view, but not always change, even with TMU level access.

## Slide 17: Going forward…
Several discussions with FAA technical support in Atlantic City.
New FAA software deployment on May 30th, 2012 with several issues to be addressed.
Possible “Parallel/test bed” system access in future???

## Slide 18: Going forward
Evaluate May 30th, 2012 software changes.
Create local Edmonton protocol for daily, consistent, updating of DPO.
Addition of DPO to NAV CANADA portal/NOC page.

## Slide 19
The ATC estimated times for RAMEL for ACA031 & CPA831 (both flights were still south of CZEG air space) were: 0136Z & 0143Z – 7 minutes in trail.
ACA was unable faster than M.83, so CPA was reduced to A.82- while still in YUL airspace.
In this screen shot, internal CZEG comments showed Assigned speeds.
DPO was updated to show revised ATC estimated times.
DPO Example

## Slide 20
90 minutes later, ACA was able M.84, and was assigned A.84+. CPA maintained the reduced A.82-.
In this screen shot, internal CZEG comments showed Assigned speeds.
DPO was updated to show revised ATC estimated times.

## Slide 21: NAV CANADA’s DPO Objective
To consistently enter accurate data for the benefit of all DPO users.

## Slide 22
ATC – ATC link
FAA/ATC - Dispatch
Dispatch-Flight

## Slide 24: Questions/Discussion
??