## Slide 1: CPWG14
Isavia - update
Chicago – December 2012

## Slide 2: Traffic - increase
Approx 20% increase in polar traffic first 9 months of 2012, compared to 2011
Average traffic decrease 2-3% in Reykjavik CTA, compared to 2011

## Slide 3: AIDC
Edmonton – feb/march 2013
Bodö 2014
Murmansk 2016

## Slide 4: ADS–C contracts
On Feb 7th the following change will be implemented:
ADS-C contracts default set up with each ADS-C capable aircraft that logs onto Reykjavik (BIRD)
A periodic contract with an 18 minute reporting interval
A event contract with the following characteristics
  Lateral deviation change event with a 5 NM threshold
  Altitude range change event with a 200 feet threshold
  Vertical rate change event with a 6000 feet per minute descent threshold

## Slide 5: Satellite communication
Irridium / Inmarsat communication go through Iceland Radio
Dial Reykjavik directly – preferrably only in emergency

## Slide 6: CPDLC/ADS-C – 82N
Currently FANS 1/A ADS-C and CPDLC service is provided in the Reykjavik CTA south of 82°N.
This is about to change for aircraft equipped with HF datalink and FOI. CPDLC/ADS-C will not be logged off at 82N.
  Approx. Date of change: Spring 2013

## Slide 7: Trials
ITP
ENGAGE
SESAR 7.5.3 User Preferred Routings