## Slide 1: Performance Based Communication and Surveillance
Introduction to RCP and RSP
Date: 13 December 2012
Presented to: CPWG/14
By: Tom Kraft, FAA

## Slide 2: Why do we need RCP and RSP?
Air traffic management operations are becoming more dependent on communication and surveillance capabilities and performances

## Slide 3: Application of RCP – RSP
Air traffic services (ATS) provision and prescription
Operator authorization
Post-implementation monitoring, analysis, and corrective action, as appropriate
Can mean different things

## Slide 4: Application of RCP – RSP
Data link operations
Reduced separation minima
  Air traffic services (ATS) provision and prescription
  Operator authorization
  Post-implementation monitoring
Other applications, where beneficial
What it means in terms of ATM initiatives

## Slide 5: RCP basis (SARPs and PANS)
Annex 11 (SMS, RCP prescription and ATS system)
Annex 6 (Operational authorization)
Doc 4444 (Reduced separation minima and flight plan requirements)
Doc 7030 and related AIPs (or equivalent publication)
RSP basis in work by OPLINKP

## Slide 6: RCP – RSP guidance material
June 2013 – Performance Based Communication and Surveillance Manual (ICAO Doc 9869)
March 2013 – GOLD, 2nd Edition
Safety and Performance Standard for Air Traffic Data Link Services in Oceanic and Remote Airspace (Oceanic SPR Standard) (RTCA DO‑306/EUROCAE ED‑122)
Guidelines for Approval of the Provision and Use of Air Traffic Services Supported by Data Communications (RTCA DO‑264/EUROCAE ED‑78A)
RSP in work by OPLINKP and GOLD Working Group
Currently “Manual on RCP”
Where to find more information

## Slide 7: Interoperability Standards
Interoperability standards allow choices that can affect operational performance
  Different technologies
  Different implementations

## Slide 8: Safety oversight framework
ANSP
Aeronautical Station and/or ATSU
CSP
SSP
Service
Agreement
Service Agreement
Aircraft Operator
Aircraft
Earth Station
Satellite
Network Access
AOC
Service
Agreement
Dedicated Network
Airworthiness, Operations and Maintenance
Air Navigation Services
Appropriate Authority
ICAO SARPs
Regional/National Safety Rules

## Slide 9: RCP 240 – RSP 180 specifications
Provided in GOLD (same as RTCA DO­306 / EUROCAE ED­122, but augmented)
  RCP 240 operational requirement (ICAO Doc 9869)
  RCP 240 – RSP 180 time requirements based on standards for application of 30 and 50 NM longitudinal separation minima (ICAO Doc 4444)
  RCP 240 – RSP 180 continuity, availability and integrity requirements based on operational safety assessment (RTCA DO-264 / EUROCAE ED-78A)

## Slide 10: RCP 240 specification
Applies to controller’s intervention capability
Controller composes and sends ATC instruction
Controller receives indication of response and understand it
RCP Parameters
Communication transaction time
RCP continuity
RCP availability
RCP integrity
Interoperability & functional definition

## Slide 11: RSP 180 specification
Applies to surveillance data
X
Event
Interval
Interoperability & functional definition
Time at position
ATSU/controller receives the surveillance data
RSP Parameters
Surveillance data transit time
RSP continuity
RSP availability
RSP integrity

## Slide 12: RCP 240 time and continuity
 | RCP specification (communication transaction time) |  |  |  |  |  |  |  |  | 
RCP | 240 |  |  |  |  |  |  |  |  | RCP
 | Controller composes and sends message | Operational Performance (Monitored) |  |  |  |  |  |  | Controller receives indication and confirms response | 
 |  | Communication transaction time |  |  |  |  |  |  |  | 
99.9% | Part of 30 | 210 |  |  |  |  |  |  | Part of 30 | ET
95% | Part of 30 | 180 |  |  |  |  |  |  | Part of 30 | TT
 |  | RCTP (Ground to Air) |  |  | PORT | RCTP (Air to Ground) |  |  |  | 
99.9% |  | P(150) |  |  | 60 | P(150) |  |  |  | 99.9%
95% |  | P(120) |  |  | 60 | P(120) |  |  |  | 95%
 |  | ATSU system | CSP | Aircraft system |  | Aircraft system | CSP | ATSU system |  | 
99.9% |  | P(15) | P(120) | P(15) |  | P(15) | P(120) | P(15) |  | 99.9%
95% |  | P(10) | P(100) | P(10) |  | P(10) | P(100) | P(10) |  | 95%
Interoperability & functional definition

## Slide 13: RSP 180 time and continuity
 | RSP specification (surveillance data transit time) |  |  |  |  | 
RSP | 180 |  |  |  |  | RSP
 | Time at position (RNP at +/-1 sec UTC) | Operational Performance (Monitored) |  |  | ATSU receives surveillance data | 
 |  | Surveillance data transit time |  |  |  | 
99.9% |  | 180 |  |  |  | OD
95% |  | 90 |  |  |  | DT
 |  | Aircraft system | CSP | ATSU system |  | 
99.9% |  | 5 | 170 | 5 |  | 99.9%
95% |  | 3 | 84 | 3 |  | 95%
X
Event
Interval
Interoperability & functional definition

## Slide 14: RCP 240 – RSP 180 availability
RCP 240 – RSP 180 aircraft availability requirement
  0.999 availability – a single system can meet requirement
  Carriage requirements for multiple communication radios are typically specified only for voice communications
RCP 240 – RSP 180 communication services availability requirements are as follows
RCP 240 – RSP 180 availability requirements |  |  | 
Availability parameter | Efficiency | Safety | Compliance means
Service availability (ACSP) | 0.9999 | 0.999 | Contract/service agreement terms
Unplanned outage duration limit (min) | 10 | 10 | 
Maximum number of unplanned outages | 4 | 48 | 
Maximum accumulated unplanned outage time (min/yr) | 52 | 520 | 
Unplanned outage notification delay (min) | 5 | 5 | 
Note.— DO 306/ED 122 specifies a requirement to indicate loss of the service. Unplanned outage notification delay is an additional time value associated with the requirement to indicate the loss to the ATS provider per the RCP/RSP related safety requirement (SR) 4 for the ANSP. |  |  | 

## Slide 15: RCP 240 – RSP 180 integrity
RCP 240 – RSP 180 provide safety requirements for the components of the operational system
  Integrity issues discovered post-implementation are reported to the appropriate Regional/State monitoring agency and/or authorities for appropriate action
For RSP 180, the integrity criteria include accuracy of navigation position data and time at the position provided in the surveillance data (e.g., RNP 4 at +/- 1 sec UTC)
RCP 240 – RSP 180 availability requirements |  | 
Integrity parameter | Integrity value | Compliance means
Integrity (I) | Malfunction = 10-5 (per flight hour) | Analysis, safety requirements, development assurance level commensurate with integrity level, (compliance shown prior to operational implementation). See also RCP related safety requirement SR‑26 for the ATSP. CSP contract/service agreement. See also RCP integrity criteria for CSP, paragraph B.2.1.2.

## Slide 16: Compliance determination – initial
Consistent with SMS practices, ANSP specifies and prescribes appropriate safety requirements and ensures systems meet requirements; GOLD and RCP – RSP specifications provide criteria for ATS provision
  ATC system design and procedures
  Controller and other ATS staff training, as appropriate
  Contractual arrangements/service agreements with CSP(s)/SSP(s)
  Operational trials
  Notification of data link services, operator requirements, including aircraft equipage
  Contingency and restoration of service procedures
ATS Provision

## Slide 17: Compliance determination – initial
Aircraft/avionics manufacturer obtains design approval, as appropriate, in accordance with National regulations; GOLD and RCP – RSP specifications provide criteria for avionics
Aircraft/avionics manufacturer demonstrates operational performance with a representative ATS provision
Demonstrations cannot be practically exhaustive
Aircraft/avionics manufacturer
Representative environment (could be operational)
Aircraft system design approval

## Slide 18: Compliance determination – initial
Operator obtains operational authorization, as appropriate, in accordance with National regulations; GOLD and RCP – RSP specifications provide criteria for operations and maintenance
  Contractual arrangements/service agreements with CSP(s)/SSP(s)
Operator demonstrates 6 months of acceptable RCP/RSP performance for the aircraft types in their fleet
If substandard performance, ANSP and/or State of the Operator or State of Registry issues corrective action notice
  Considers severity of the deficiency and magnitude of the change
If non-compliance remains after the date indicated in the corrective action notice State of the Operator or State of Registry could remove the RCP [X] – RSP [Y] authorization
  The operator may still use CPDLC and ADS-C
Operator

## Slide 19: Compliance determination – continued
FANS 1/A
Post-implementation monitoring and RCP – RSP analysis
DLMA or CRA
Operator
CSP
Aircraft manufacturer
Avionics supplier
Satellite operator
Compliance action
Continuous improvement
ATSP
http://www.ispacg-cra.com
Network
Ways to manage change and performance

## Slide 20: Performance based communication and surveillance
Summary

## Slide 21: Safety policy and objectives
RCP/RSP provides means to meet SMS obligations for safety of air traffic management operations that are dependent on communication and surveillance capabilities
  Management
  Commitment
  Responsibility
  Accountability

## Slide 22: Safety risk management
RCP/RSP specifications are prescribed to ATS operations in specified airspace to provide basis for initial and ongoing compliance determination
  Hazard identification
  Risk assessment
  Mitigation strategy – safety argument
  Functional, safety and performance requirements

## Slide 23: Safety assurance
Safety oversight framework allows compliance with RCP/RSP specifications for
  Operator/aircraft type combinations and/or
  ATS provision, including “CSP/SSP” capability
ANSP identifies substandard performance for appropriate action
  Change management – continuous improvement

## Slide 24: NAT PBCS Workshop
To be held in Paris, France on 20-22 February 2013
Will provide training and education