## Slide 1: Agenda Item 8 : JCAB Update Operational Trial for Datalink Departure Clearance (DCL)
CPWG/14
Chicago, U.S.A .
10 - 14 Dec. 2012
Notes: <number>

## Slide 2
Outline
1. Introduction
2. General Image of DCL
3. DCL Trial Operation in Japan
4. Phase 1 DCL Trial Operation
5. Future Plan

## Slide 3
Introduction
DCL (Departure CLearance)
Departure clearance by datalink
Prevent human error
(Routes, ALT, SSR code, Next frequency, etc.)
Mitigate controller/pilot workload
Improve off-block time delay caused by congested voice communication

## Slide 4
RCD (Request clearance)
Drafting DCL message
CLD (Issuing clearance)
ACCEPT
CDA (Readback)
FSM
General Image of DCL
FSM
(Confirmation of receipt)
AEEC623 & ED85A

## Slide 5
DCL Trial Operation in Japan
Study of operational requirements in 2007
System design and installation since 2008
Trial operation started since 28 Jun. 2012 at Tokyo Airport (RJTT) and Narita Airport (RJAA)
  Applicable aircraft are domestic flights which depart from RJTT or RJAA and are previously coordinated with JCAB
Ref. AIC Nr 022/12

## Slide 6
DCL Trial Operation in Japan
Phase 1 (28 Jun. 2012)
Domestic flights via pre-determined SIDs/Transitions
Phase 2
Domestic + International flights via pre-determined SIDs/Transitions
Phase 3
All aircraft
Full operation
Phased Approach
1 year
1 year
1 year

## Slide 7
Aircraft
TWR
ACC
ATM Center
Airlines
1. Request Clearance
4. Issuing Clearance
2. Request Clearance
Ground Delay Time, if necessary
Clearance Information
3. Issuing Clearance
Prevent Human Error
Mitigate Controller/Pilot Workload
Phase 1 DCL Trial Operation

## Slide 8
Cooperating Airlines : JAL, ANA, SKY
Rate of aircraft with DCL
  RJTT: 25% (Total domestic departure 500 flights/day)
  RJAA: 50% (Total domestic departure 40 flights/day)
Evaluation of the trial
  Conducting periodical review
  Favorable outcome
  Satisfy ED-85A* requirement
  Many DCL from not applicable aircraft (foreign airlines) at RJAA
* DATA-LINK APPLICATION SYSTEM DOCUMENT FOR THE “DEPARTURE CLEARANCE” DATA-LINK SERVICE
Phase 1 DCL Trial Operation

## Slide 9
Future Plan

## Slide 10: Thank you Questions?
Notes: <number>