## Slide 1
NAV CANADA
Polar Tactical Re-routes 2013
CPWG 15
May 13-17, 2013
Notes: <number>

## Slide 2: Polar Tactical Re-routes
The daily, standard use, of tactical re-routes has been discussed at past CPWG meetings.
Could be used for traffic/conflict resolution, and for the re-evaluation of flight planned routes by crew/dispatch while already airborne.
Notes: <number>

## Slide 3: Polar Tactical Re-routes
Many operational efficiency gains have been realized through RVSM, reduction of restrictions, and through increased use of collaborative decision making processes.
NAV CANADA feels that further gains can still be made through increased ability to tactically re-route Polar flights, much like what can be currently done with almost all other flights & jurisdictions.

## Slide 4
Mar. 27, 2013 – All Polar flights over ORVIT
Flight Ident. | Polar Fix | GRL Time | GRL Altitude | Actual ATC Estimate
ACA015 | ORVIT | 2015 | 320 | 
CPA841 | ORVIT | 2058 | 320 | 
UAL86 | ORVIT | 2224 | 340 | 
AAL289 | ORVIT | 2310 | 360 | 
ACA087 | ORVIT | 2357 | 340 | 2347
KAL038 | ORVIT | 0007 | 340 | 2359
AAR221 | ORVIT | 2359 | 360 | 2359
UAL89 | ORVIT | 0009 | 360 | 0003
UAL897 | ORVIT | 0005 | 380 | 0011
KAL094 | ORVIT | 0019 | 360 | 0011
DAL181 | ORVIT | 2347 | 340 | 0016
DAL189 | ORVIT | 0017 | 340 | 0017
UAL851 | ORVIT | 0027 | 340 | 0024
AAR235 | ORVIT | 2329 | 360 | 0032
UAL895 | ORVIT | 0040 | 360 | 0036
KAL082 | ORVIT | 0015 | 380 | 0044
KAL036 | ORVIT | 0045 | 340 | 0046
ACA031 | ORVIT | 0145 | 320 | 
CPA831 | ORVIT | 0155 | 320 | 
CPA807 | ORVIT | 0226 | 340 | 
UAL117 | ORVIT | 0236 | 340 | 
CES588 | ORVIT | 0321 | 340 | 
CCA982 | ORVIT | 0341 | 340 | 
CHH7976 | ORVIT | 0350 | 320 | 
Notes: All flights were over ORVIT!
No other Polar fixes were used!

## Slide 5
Mar. 27, 2013 “those in conflict”
Flight Ident. | Polar Fix | GRL Time | GRL Altitude | Actual ATC Estimate | Actions Taken
ACA087 | ORVIT | 2357 | 340 | 2347 | A.84 later A.85
KAL038 | ORVIT | 0007 | 340 | 2359 | A.81
AAR221 | ORVIT | 2359 | 360 | 2359 | Plan FL380, A.83/A.82
UAL89 | ORVIT | 0009 | 360 | 0003 | A.83, later no speed
UAL897 | ORVIT | 0005 | 380 | 0011 | A.83, later no speed
KAL094 | ORVIT | 0019 | 360 | 0011 | Plan FL340 & A.83
DAL181 | ORVIT | 2347 | 340 | 0016 | Plan FL320
DAL189 | ORVIT | 0017 | 340 | 0017 | Plan FL360 & A.82
UAL851 | ORVIT | 0027 | 340 | 0024 | A.81 later A.83
AAR235 | ORVIT | 2329 | 360 | 0031 | 
UAL895 | ORVIT | 0040 | 360 | 0036 | Plan FL340 & A.84
KAL082 | ORVIT | 0015 | 380 | 0044 | 
KAL036 | ORVIT | 0045 | 340 | 0046 | Plan FL360
Traffic was in three main “groups”
1) ACA087, KAL038, AAR221 & UAL89
2) UAL897, KAL094, DAL181 & DAL189
3) AAR235, KAL036, KAL082, UAL895 & UAL851
Notes: There is overlap between group #1 and group #2, and between #2 and #3. These are broken into three main groups for illustration purposes.

## Slide 6
Mar. 27, 2013 “those in conflict”
Flight Ident. | Polar Fix | GRL Time | GRL Altitude | Actual ATC Estimate | Actions Taken
ACA087 | ORVIT | 2357 | 340 | 2347 | A.84 later A.85
KAL038 | ORVIT | 0007 | 340 | 2359 | A.81
AAR221 | ORVIT | 2359 | 360 | 2359 | Plan FL380,A.83/A.82
UAL89 | ORVIT | 0009 | 360 | 0003 | A.83 later no speed
UAL897 | ORVIT | 0005 | 380 | 0011 | A.83 later no speed
KAL094 | ORVIT | 0019 | 360 | 0011 | Plan FL340 & A.83
DAL181 | ORVIT | 2347 | 340 | 0016 | Plan FL320
DAL189 | ORVIT | 0017 | 340 | 0017 | Plan FL360 & A.82
UAL851 | ORVIT | 0027 | 340 | 0024 | A.81 later A.83
AAR235 | ORVIT | 2329 | 360 | 0032 | 
UAL895 | ORVIT | 0040 | 360 | 0044 | 
KAL082 | ORVIT | 0015 | 380 | 0046 | Plan FL340 & A.84
KAL036 | ORVIT | 0045 | 340 | 0036 | Plan FL360
In the 1st group, AAR221 gave an able FL380 time of 2230Z. At time 2200Z, AAR221 changed it’s FL380 time to 0230Z.
Possible reasons – fuel, turbulence, space weather etc..
Controllers had two options:
1) Plan AAR221 at FL360, UAL89 at FL340, & KAL038 at FL320; or,
2) Descend AAR221 to FL320 in VHF coverage, leaving UAL89 @ FL360 and KAL038 @ FL340.
AAR221 was descended FL320.
Notes: There is overlap between group #1 and group #2, and between #2 and #3. These are broken into three main groups for illustration purposes.
The main point to note is the prevalence of altitude and/or speed restrictions.

## Slide 7
Mar. 27, 2013 “those in conflict”
Flight Ident. | Polar Fix | GRL Time | GRL Altitude | Actual ATC Estimate | Actions Taken
ACA087 | ORVIT | 2357 | 340 | 2347 | A.84 later A.85
KAL038 | ORVIT | 0007 | 340 | 2359 | A.81
AAR221 | ORVIT | 2359 | 360 | 2359 | Plan FL380, A.83/A.82
UAL89 | ORVIT | 0009 | 360 | 0003 | A.83 later no speed
UAL897 | ORVIT | 0005 | 380 | 0011 | A.83 later no speed
KAL094 | ORVIT | 0019 | 360 | 0011 | Plan FL340 & A.83
DAL181 | ORVIT | 2347 | 340 | 0016 | Plan FL320
DAL189 | ORVIT | 0017 | 340 | 0017 | Plan FL360 & A.82
UAL851 | ORVIT | 2329 | 360 | 0032 | A.81 later A.83
AAR235 | ORVIT | 0027 | 340 | 0024 | 
UAL895 | ORVIT | 0040 | 360 | 0036 | Plan FL340 & A.84
KAL082 | ORVIT | 0015 | 380 | 0044 | 
KAL036 | ORVIT | 0045 | 340 | 0046 | Plan FL360
In the 2nd group, DAL181 was restricted to FL320.
KAL094 was restricted to FL340.
DAL189 was restricted to A.82 due to UAL89 from the 1st group.
Notes: There is overlap between group #1 and group #2, and between #2 and #3. These are broken into three main groups for illustration purposes.
The main point to note is the prevalence of altitude and/or speed restrictions.

## Slide 8
Screen Shot March 27
All flights over ORVIT
None over AMATI or NIKIN!
Many factors go into planning routes and reroutes.
AMATI &/or NIKIN could have been possible reroute options at little extra cost.
One of these airlines was contacted later that day and was asked to run flight plans over AMATI & NIKIN for comparison…
Notes: The choice to flight plan over ORVIT could have been forced by many factors such as air temperature, turbulence forecasts, space weather, airspace restrictions further down line etc., but overall cost was likely the deciding factor.

## Slide 9: Mar. 27, 2013 Comparison
Routing over AMATI or NIKIN instead of ORVIT:
NIKIN was ~ $700 more
AMATI was ~ $100 more
…and no likely speed or altitude restriction(s) in either case
Was ORVIT really the least costly?

## Slide 10
Current reroute process is very challenging due time constraints.
Up to 3+ hours required, including coordination with dispatch, dispatch with flight, dispatch with Anchorage and Russia.
Ideally this would be able to be implemented “near the boundary”
Resulting in higher probability of every flight attaining requested speed and altitude.
Mar. 27, 2013 scenario

## Slide 11: Going Forward…..
Airlines: Greater use of ETMS/ASD, GRL/DPO to “route away” from busy fixes during the flight planning stage, and also during the “airborne” stage, is encouraged.
NAV CANADA will continue to identify conflicts, and work towards implementing a process to update DPO.
NAV CANADA encourages USA & Russia to re-open previous negotiations to allow tactical rerouting of aircraft to be more timely and efficient.
Notes: DPO (DOTS Plus Online). Updating of DPO by NAV CANADA will allow all DPO Users to view “real time” estimates for any Polar fix, and will affect an airlines’ decision to consider a route change or not.

## Slide 12: Questions/Discussion

## Slide 13
For further questions or comments please contact:
Jeff Dawson 613-563-7341
Stephen Middleton 780-890-8397