## Slide 1: Assistance to avoid conflict by OCAP
CPWG/15
May, 2013
Presented by JCAB
Notes: イントロダクション

## Slide 2: Outline of OCAP
Oceanic Conflict detection
and Assistance Processor
OCAP server is a component of ODP system
(Oceanic ATC data processing system).
OCAP server has started operation on October, 2012.
OCAP provides following functions
-Detect predicted conflict several hours in advance
-Present and manage the procedure to avoid conflict

## Slide 3: Detection of conflict
OCAP can find the conflict several hours in advance between aircraft and aircraft, or between aircraft and restricted airspace.
This function is almost the same as the one provided by host computer of ODP before OCAP server has started operation.

## Slide 4: Presentation of the way to avoid conflict
OCAP can present to the controller how to avoid the predicted conflict.
The procedures to avoid conflict provided by OCAP are as follows,
- by assigning mach number
(to apply mach number technique)
- by changing altitude

## Slide 5: Presentation of the way to avoid conflict
Situation that CAB001 and CAB004 will conflict 1 hour later

## Slide 6: Presentation of the way to avoid conflict
Predicted situation when ATC separation between CAB001 and CAB004 is going to be below minimum

## Slide 7: Presentation of the way to avoid conflict
OCAP alerts controller to predicted conflict between
CAB001 and CAB004, and presents the procedure to avoid.

## Slide 8: Presentation of the way to avoid conflict
Procedure can be completed with 1 step
Procedure can be completed with 2 steps
Procedure to apply mach number technique

## Slide 9: Management of the way to avoid conflict
Example for executing procedure No.3

## Slide 10: Management of the way to avoid conflict
CAB001
CAB002
FL350
FL340
FL360
CAB003
FL370
CAB004
FL380
CONFLICT
3
1
1. issue the clearance for CAB003 to climb to FL380
2. receive the report CAB003 has reached FL380
3. issue the clearance for CAB004 to climb to FL370
2
In this procedure, OCAP provides the step to -

## Slide 11: Management of the way to avoid conflict
Status of step 1 is “available now”,
and step 2 is “wait”.
1. Procedure No.3 was started.

## Slide 12: Management of the way to avoid conflict
Next step is not available until CAB003 reaches FL380.
2. Controller issued the clearance to climb to FL380 for CAB003.

## Slide 13: Management of the way to avoid conflict
Next step is enabled to execute.
3. ODP system received the report CAB003 has reached FL380

## Slide 14: Management of the way to avoid conflict
All steps of the procedure were done, and the conflict was resolved.
4. Controller issued the clearance to climb to FL370 for CAB004

## Slide 15: Parameter setting for presentation
Order of the procedures to avoid conflict indicated in list is based on following items. The weights of each items are defined in parameter setting.
Number of steps in the procedure
Kind of the way to avoid (change altitude or mach number)
Range of changing altitude or mach number
Distance from departure airport
Distance to destination airport
and others (more than 30 items)

## Slide 16: Parameter setting for presentation
OCAP records following data as statistic data.
Person in charge of ODP system sets the parameter of OCAP while referring to the statistic data for optimizing order of the procedures in list.
Detected conflict
Presented procedures to avoid conflict
Procedure which selected by controller

## Slide 17: Schedule for introduction
The function of assistance to avoid conflict by OCAP is under evaluation in Systems Development, Evaluation and Contingency management Center (SDECC).
Assistance to avoid conflict by OCAP will be utilized at Air Traffic Management Center (ATMC) from June, 2013.

## Slide 18
Thank you!
Questions?