## Slide 1: Mach Number Technique

## Slide 2: ICAO Doc 9426 (ATS Planning)
2.2.1 a) To ensure continued longitudinal separation between successive aircraft on long route segments with minimum ATC intervention
2.2.1 b) to obtain improved utilisation of such routes, thus contributing to the economy of flight operations

## Slide 3: Doc 9426 para 2.2.3
Aircraft concerned are normally subject to approximately the same wind and temperature conditions
Minor variations in speed which might temporarily increase or decrease the spacing

## Slide 7
10 Minutes

## Slide 13: 2.3 PREREQUISITES
MNT is particularly suitable for areas where the environment is such that position reporting and ATC intervention with individual flights can, at times, be subject to delay

## Slide 14: 2.3 PREREQUISITES
MNT is particularly suitable for areas where the environment is such that position reporting and ATC intervention with individual flights can, at times, be subject to delay - Direct Controller Pilot Communication (DCPC) NOT REQUIRED

## Slide 15: 2.3 PREREQUISITES
MNT is particularly suitable for areas where the environment is such that position reporting and ATC intervention with individual flights can, at times, be subject to delay - Direct Controller Pilot Communication (DCPC) NOT REQUIRED
aircraft generally follow the same or diverging tracks until they are provided with other forms of separation

## Slide 18: 2.3.2 Aircraft requirements
“Calibrated instruments that show Mach Number”
Asia/Pacific has added an additional requirement of INS (or VLF-OMEGA?) as per Regional Supps

## Slide 19: 2.3.3 ATC requirements
“Access to forecast upper wind information, or
position information obtained from previous aircraft (to calculate longitudinal separation at the exit point)”

## Slide 20: Other
“Pilots will strictly adhere to last assigned Mach number (para 2.4.7)”
“ATC will assume that last assigned Mach number will be maintained (para 2.3.4)”

## Slide 21: 2.4 Procedures
“ATC clearance must include the assigned Mach Number”
“Important that the estimates for the entry point to the area provided by pilots are as accurate as possible”

## Slide 22: 2.4 Procedures
“The prescribed longitudinal separation between successive aircraft flying at the same level must be provided over the entry point, or exist when climb or descent to the level of another aircraft”
MNT can be used entering into a designated (oceanic) area by defined entry point, or
applied en-route for step climbs/descents without use of an entry point

## Slide 23
2.5.3 En-route step-climbs and step-descents
2.5.3.1 “The Mach number technique may be used as a means of applying longitudinal separation between aircraft carrying out step-climbs or step-descents and other en-route traffic on the same track provided that the prescribed minimum longitudinal separation between the climbing/descending aircraft and other affected en-route traffic exists at the time a climb/descent clearance is issued and will exist during climb/descent, as well as at each further significant point along track and at the exit point.”

## Slide 24: In the words of Doc 4444
8.4.3 Provided that:
a) the aircraft concerned have reported over the same reporting point and follow the same track or continuously diverging tracks until some other form of separation is provided; or

## Slide 25: In the words of Doc 4444
b) if the aircraft have not reported over the same reporting point and it is possible to ensure, by radar or other means, that the appropriate time interval will exist at the common point from which they either follow the same track or continuously diverging tracks; when Mach number technique is applied, minimum longitudinal separation between turbojet aircraft on the same track, whether in level, climbing or descending flight shall be:

## Slide 26: 2.4 Procedures
Thereafter, provided that aircraft maintain their last assigned Mach numbers, intervention by ATC for the portion of flight where the MNT is used, should normally only be necessary if an aircraft, for some reason, is obliged to change its number

## Slide 27: Longitudinal Separation (MID/ASIA/RAC-6)
Operating within Bombay, Calcutta, Delhi, Karachi, Kota Kinabalu, Kuala Lumpur, Lahore, Madras, Muscat, Naha, Tehran Tokyo and Yangon FIRs; and
Using inertial nav systems on controlled routes within Bangkok, Hong Kong, Manila, and Singapore FIRs, and extended areas of responsibility where applicable; and

## Slide 28: Longitudinal Separation (MID/ASIA/RAC-6)
On controlled oceanic route segments between Australia, Indonesia, New Zealand and Singapore

## Slide 29: 6.2 Longitudinal Separation (MID/ASIA/RAC-6)
Shall be 10 minutes, or 80 NM, derived by RNAV when MNT is applied and whether in level, climbing or descending flight
  aircraft report over a common point and follow same track or diverging track
  if aircraft have not reported over common point then the State must ensure by other means that the appropriate time interval will exist at the common point

## Slide 31
“Centre - SQ17 over
ALPHA at time 0000,
flight level 330”

## Slide 32
“Centre, TG409 with you
estimating ALPHA at 0010,
flight level 290 requesting
flight level 330”

## Slide 33
“SQ17, Maintain Mach point 84 or greater.”
“TG409, Maintain Mach point 84 or less, climb
and maintain flight level 330.”
ATC:
TG409
SQ17, FL330

## Slide 34: 6.2 Longitudinal Separation (MID/ASIA/RAC-6)
Between 9 and 5 minutes
  9 minutes with .02 in front
  8 minutes with .03 in front
  7 minutes with .04 in front
  6 minutes with .05 in front
  5 minutes with .06 in front

## Slide 37: Doc 9426 para 2.5 Specific Procedures
Separation at entry point when the following aircraft is the faster
Can be used for climbs or descents provided that the prescribed minimum longitudinal separation exists during climb/descent as well as at each further significant point along track, and at the exit point

## Slide 40: 2.5.4.2 “Rule of Thumb” for faster in back
“For each 600 NM in distance between the entry and exit points of the area where the MNT is used, add one minute for each 0.01 difference in Mach number for the two aircraft concerned to compensate for the fact that the second aircraft is overtaking the first aircraft”

## Slide 41
Appendix A
Table - Application of MACH Number Technique
when the Following Aircraft is the Faster

## Slide 42: Faster in Back Scenario 1

## Slide 43
CX102
FL330 (progressed
ALPHA at 0000)
“Centre, QF5 over ALPHA at
0014, FL 290 requesting FL330”
Entry
Point
ALPHA

## Slide 44
1000 NM
0.02 Mach Difference
Entry
Point
ALPHA
QF5 CX102
What is the required
spacing between
aircraft?
1000 NM
0.02 Mach Difference
QF5, FL290 CX102, FL330

## Slide 46
14 or greater
minutes spacing
required
1000 NM
0.02 Mach Difference
QF5, FL290 CX102, FL330

## Slide 47
14 or greater
minutes spacing
required
1000 NM
0.02 Mach Difference
ATC: “CX102 maintain Mach point 84
or greater”.
“QF5 maintain Mach point 86 or
less, climb and maintain FL330”
QF5, FL290 CX102, FL330

## Slide 48: Faster in Back Scenario 2

## Slide 49
700 NM
0.05 Mach Difference
“Centre, MH71
estimating ALPHA
at 0120, FL290 requesting
FL330”
GA202, FL330
progressed ALPHA at 0100

## Slide 51
700 NM
0.05 Mach Difference
20 or greater
minutes spacing
required

## Slide 52
700 NM
0.05 Mach Difference
“GA202 maintain Mach point 81 or greater”
“MH71 maintain Mach point 86 or less - climb and maintain FL330”
ATC: