## Slide 1: Proof of Concept Trial SATCOM Voice Northern Canada
NAM/EUR ATFM Meeting
May 2-3, 2007
Brest, France

## Slide 2: SATCOM Voice Trial
SATCOM Voice currently limited to emergency and non routine ATS communications in NAT and Canadian airspace
Assess the feasibility of using SATCOM voice for routine ATS communications
Conducted a Proof of Concept Trial with limited participation (BAW, CPA, JAL, SAS, UAL)

## Slide 3: SATCOM Voice Trial
Trial conducted between November 1, 2006 and December 20, 2006
SATCOM used for all ATS communications normally on HF through Arctic Radio
In March HF frequencies transferred to Gander IFSS
All costs borne by the initiator of each SATCOM call
Results were shared with NAT SVTF

## Slide 4: Trial Objectives
  gain operational and technical experience
  validate aircrew and radio operator procedures
  the effect of the SATCOM shadow
  connection times compared to HF Radio for ground and airborne initiated calls
  impact on existing ATS and flight crew procedures
  clarity of voice communications
  security issues
  system performance
  reliability, availability and integrity
  costs associated with use of SATCOM voice

## Slide 5: Trial Results
Lead time required for crew training
Reticence on the part of some flight crews noted
Teleconferences held during and after the trial to assess progress
Aircrew and Aeradio procedures reported to be valid, relevant and sufficiently robust
No impact on other Aircrew or ATS procedures

## Slide 6: Trial Results
Nominal SATCOM shadow considered to be north of 80N
Some SATCOM connections as far as 84N
64 calls initiated by Arctic Radio
Average connection time 27.3 seconds
198 calls reported as readability 4 or 5
23 calls reported as readability 3 or less
13 of those from within SATCOM shadow

## Slide 7: Trial Results
NAVCAN STAR used for secure, efficient and accurate dialling
Unique PIN built into automated dialling string
Recommend Q12 be reserved for ATS communications and Q10 reserved for AOC
Important for crews to display priority of incoming calls
NAVCAN STAR proved reliable and efficient

## Slide 8: Trial Results
Positive feedback from Air Crews and Aeradio Operators
Arctic Radio reported SATCOM Voice superior in delivering clearances during poor HF conditions
UAL pilots reported SATCOM superior when conducting complex negotiations approaching Polar Route entry fixes

## Slide 9: Costs
NAV CANADA incurred a cost of $1,500.00 USD to conduct trial
Includes testing and training costs
SAS reported a cost of $197.50 USD to participate in trial
Based on arrangement wherein fixed rate for set number of minutes
$197.50 is excess

## Slide 10: Conclusions
SATCOM Voice has proven to be a viable and reliable medium to conduct routine ATS Communications.
Contingent on robust operational procedures and automated system capable of secure, efficient and accurate SATCOM dialling.

## Slide 11: Next Steps
Integrate NAVCAN STAR functionality into voice switch equipment
Amend CFS to allow for use of SATCOM Voice for routine ATS communications with Gander IFSS and Arctic Radio
Will not replace HF but be available as an alternative
Consultation with Transport Canada to determine feasibility of long-term goals

## Slide 12: Future Advantages ???
Fewer instances of lost communications
Support HF regression as backup to CPDLC
MEL relief
Continue random route operations during poor HF conditions
Greater intervention capability
Used to support distance based separation applications if CPDLC equivalent
Develop procedures and software to allow direct SATCOM calls to ATC sectors