## Slide 1: Overview of DOTS Plus Online
Cross Polar Work Group
September 19, 2007
Originally presented at
User Demonstration and Workshop
July 18, 2007

## Slide 2: Agenda
Overview of DOTS+ Online
Demonstration of DOTS+ Online
Feedback from dispatchers/air carrier users
Review suggested improvements

## Slide 3: Overview of DOTS+ Online
Document Number Here
© 2006 The MITRE Corporation. All rights reserved.
<number>

## Slide 4: Problem Identification
Coordination and communication of gateway reservation information
  Need for latest Gateway Reservation List (GRL)
  DOTS+ Track Advisory (TA) employs cumbersome, text-message interface for air carrier users
    Concerns that GRL is not updated
  Users have limited insight into TA decision process
    GRL must be repeatedly requested to check for updates
    Air carrier users perceive that TA is inhibiting their ability to depart at desired time
    Users have limited information on gateway availability changes once flights depart
  ATCSCC (FAA Command Center) manually assigns departure times to Towers for ZAN tracks
Forecasts for significant increase in oceanic traffic
Notes: Track Advisory (TA) is a computer based program that is designed to assign altitude and time for oceanic departure release for aircraft on specific oceanic tracks based on airline preferences. It is accessed by airline operators and FAA facilities outside the oceanic Traffic Management Units (TMUs) by an AFTN/NADIN II command-line interface. Track Advisory assigns each flight a time and altitude at the oceanic gateway fix. Based on the gateway fix time, the flight is also assigned a departure time. These times are listed in the Gateway Reservation List (GRL) which is sent to users.

## Slide 5: Proposed Solution
DOTS Plus Online
  user-friendly, online interface to DOTS+ Track Advisory
  secure web server front-end
  early demonstration of System-Wide Information Management (SWIM) concepts
DOTS Plus Online (like TA) will primarily be used to coordinate gateway times/altitudes in the pre-departure phase

## Slide 6: Benefit  Awareness
DOTS Plus Online will improve coordination and communication between various TA users
  Air carrier users
    Improved interface – more likely to update information
    Updated GRL automatically displayed
  Additional gateway information
    Estimated gateway times updated based on actual departure times
  Departure information
    Automatically sent to Center TMU, reducing ATCSCC workload

## Slide 7: Operational Concept
Capabilities in 2004 Prototype
  Web-based interface
  Secured sign-on procedures
  Templates and saved gateway requests
  Format and logic checks
  Real-time updated Gateway Reservation list
  Customized Gateway Reservation list
    Acid
    Requested Departure time
    Requested Gateway Time
    Assigned Track/ Crossing Fix (Gateway)
    Departure airport
    Arrival Airport
    Assigned Departure Time
    Assigned Gateway Time
    Assigned Altitude
    Assigned Track
  Metrics/Archive of latest state of information
Additional Capabilities
  Slot availability (pre-departure)
  DOTS+ Online/ETMS interface
    Departure time information forwarded to Domestic TMU
    ETMS Departure time forwarded to DOTS+ Online
  Additional columns in GRL for users to view
    Requested Altitude
    Requested Track
    Actual Departure Time
    Estimated gateway time.
      Update estimated gateway time based on actual departure time (no change to reservation, but shows how close flight is expected to make reservation)
      Capability for user to update estimated gateway time
    Remarks (local to user)
Basic DOTS+ Online based on capabilities in 2004 prototype plus some additional capabilities

## Slide 8: Implementation Plan
Target: Operational demonstration for ZAN operations in first quarter FY08
April 2007: Requirements definition completed. Internally coordinated (FAA ATCSCC, ZOA and ZNY TMUs)
April 2007: Coordinated with NavCanada
July 2007: Coordinate with Airspace Users
In Progress
  prototype development
  review and evaluation

## Slide 9: Demonstration of DOTS+ Online
Document Number Here
© 2006 The MITRE Corporation. All rights reserved.
<number>

## Slide 10: DOTS+ Online Demonstration
Secure Login
Track Information Page
Gateway Reservation Request
  Stored Planning List
Gateway Reservation List
  Table View
  Graphical View

## Slide 11: Open Discussion
Document Number Here
© 2006 The MITRE Corporation. All rights reserved.
<number>

## Slide 12: Open Discussion
General - How do airspace users currently use Track Advisory?
  Single or multiple dispatchers send in their Gateway request
  Gateway reservation is complied with in planning and/or shared with pilot
User Messaging Requirements
  Would you call other users and the TMU or would you prefer e-mail or chat capability
  Options: E-mail, Chat, Forum
Track Information Page - Is there additional information that would be useful to airspace users?

## Slide 13: Open Discussion (Continued)
Gateway Reservation Request Capability
  General feedback on process
  How entries are validated
Gateway Reservation List
  What information is not useful
  Any other information that may be useful
  Filter - Do you want to see all tracks and all flights or just specific tracks and own flights only?
  Sort - Do you want different sorts? How many?

## Slide 14: Open Discussion (Concluded)
Graphical Display
  Feedback
  What “estimated GW time” should be shown, and is this a window
GRL Modify
  Feedback on modifying gateway request capability
  Are you able to determine when slots are available?

## Slide 15: List of Potential Fields in GRL
Aircraft ID
Aircraft Type
Requested Departure Time (wheels up)
Requested Gateway Time
Requested Altitude
Requested Gateway Fix
Assigned Gateway Fix
Departure Airport
Arrival Airport
Assigned Departure Time
Assigned Gateway Time
Assigned Altitude
Assigned Track
Estimated Time En Route (ETE) (Gateway time minus departure time)
Assigned TA Delay (assigned minus requested departure time)
Actual Departure Time
Estimated Gateway Time
Estimated TA Delay (Estimated gateway minus assigned gateway time)
Time between adjacent flights
Remarks

## Slide 17: OLTA GRL Worksheet Example