## Slide 1: Anchorage ARTCC
Airspace/Procedures and Traffic Management Update - Cross Polar and Russian Trans East Working Group / 4
CPWG/4
Anchorage ARTCC
Sept. 18-20, 2007

## Slide 2: Topics:
Anchorage ARTCC Airspace Review
Automation
Procedures
Communications
Polar and RTE Traffic Count

## Slide 3: Airspace Review
Initiated at the request of Anchorage ARTCC
Conducted by an independent team formed by FAA’s Western Service Center.
Team composition includes members from Terminal and Oceanic backgrounds.
Preliminary work was completed by core group summer 2007.
Full team will continue work at Anchorage during late September.
Report and recommendations to be forwarded by Feb. 2008.
Emphasis on operations to/from Anchorage Intl Airport, however -.
Entire Anchorage ARTCC airspace is being reviewed.

## Slide 4: Automation
Two automation platforms in use at ZAN
Ocean21
FDP2000

## Slide 5: Automation

## Slide 7: Automation – Ocean21 Next Step
Incorporation of the Anchorage Arctic FIR into Ocean21 Platform.

## Slide 8
Notes: Red and blue outlined area depicts Anchorage Center’s current Sector 4. Red area depicts the Anchorage Arctic FIR. Blue area depicts Domestic airspace.

## Slide 9: Automation – FDP2000
Automated delivery of HF messages to control position.
Improved connectivity with the Enhanced Traffic Management System (ETMS).

## Slide 10: Procedures
Mach Number Technique*
With Murmansk ACC
Effective Oct. 25th
Permits a reduction in track slot allocation
*Only effective for same track flights.

## Slide 11: Procedures
“Reverse” Mach Number Technique*
With Murmansk and Magadan ACC
Effective Oct. 25th
Provides greater flexibility for “faster in back” situations
*Only effective for same track flights.

## Slide 12: Procedures
ERNIK – B240
Available in DOTS+ effective Oct. 25th
Westbound only
Routing via either OME (Nome) or ENM (Emmonak)

## Slide 13: ZAN Traffic Count
Notes: Other oceanic traffic count numbers not currently available due to programming issue within Ocean21 system. FAA Automation researching problem and resolution due shortly.

## Slide 14: Polar and RTE Traffic Count
 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006* | 2007
JAN | 384 | 493 | 457 | 477 | 483 | 750 | 1119 | 1818
FEB | 366 | 558 | 306 | 356 | 497 | 723 | 1279 | 1119
MAR | 470 | 464 | 476 | 390 | 574 | 930 | 1546 | 1306
APR | 403 | 544 | 421 | 292 | 633 | 698 | 1277 | 1634
MAY | 336 | 246 | 447 | 218 | 578 | 748 | 1310 | 1530
JUN | 449 | 438 | 400 | 189 | 583 | 799 | 1057 | 996
JUL | 352 | 410 | 363 | 220 | 408 | 707 | 1175 | 924
AUG | 369 | 427 | 361 | 357 | 535 | 758 | 810 | 1275
SEP | 378 | 452 | 441 | 370 | 657 | 1134 | 1112 | 
OCT | 588 | 417 | 518 | 466 | 1038 | 1233 | 1521 | 
NOV | 593 | 409 | 544 | 521 | 1029 | 964 | 1195 | 
DEC | 617 | 525 | 552 | 670 | 1163 | 1055 | 2056 | 
Total | 5305 | 5383 | 5286 | 4526 | 8178 | 10499 | 15457 | 
% Increase |  | 1% | -2% | -14% | 81% | 28% | 47% | 

## Slide 15: Polar and RTE Traffic Count
2007 | DEVID | RAMEL | NIKIN | ORVIT | LISKI | FRENK | KUTAL | KOKES | VALDA | MARCC | TOTAL
JAN | 12 | 196 |  | 143 | 193 | 64 |  | 1 | 987 | 222 | 1818
FEB | 11 | 179 |  | 97 | 68 | 54 |  | 1 | 559 | 150 | 1119
MAR | 53 | 184 |  | 97 | 85 | 48 |  | 2 | 628 | 209 | 1306
APR | 19 | 161 |  | 178 | 120 | 49 |  | 0 | 867 | 240 | 1634
MAY | 57 | 109 |  | 116 | 168 | 47 |  | 1 | 869 | 163 | 1530
JUN | 37 | 88 |  | 100 | 167 | 68 |  | 1 | 471 | 64 | 996
JUL | 37 | 135 | 8 | 62 | 99 | 58 | 60 | 1 | 378 | 86 | 924
AUG | 47 | 185 | 27 | 109 | 187 | 125 | 81 | 0 | 392 | 122 | 1275
SEP |  |  |  |  |  |  |  |  |  |  | 
OCT |  |  |  |  |  |  |  |  |  |  | 
NOV |  |  |  |  |  |  |  |  |  |  | 
DEC |  |  |  |  |  |  |  |  |  |  | 
Notes: Traffic numbers include new NIKIN and KUTAL crossing points.

## Slide 16: Polar and RTE Traffic Count

## Slide 17
Questions?