## Slide 1: CPWG/6 – WP/9
Action Item 090734
ATFM procedures for Polar Fixes and Russian Trans East Fix
Notes: <number>

## Slide 2: CPWG/5 Discussions
Presentation was given on the successful trial outcome of eliminating Gateway Reservation List (GRL) buffer times on Polar routes DEVID, RAMEL, NIKIN and ORVIT
Permanent Procedures were proposed and agreed upon for DEVID, RAMEL, NIKIN and ORVIT.
Proposal for a similar trial for Russian Trans East Fix LISKI was proposed

## Slide 3: LISKI Trial
The LISKI trial ran from April 7, 2008 through May 10, 2008.
Reviews of the trial were conducted weekly by telcon with the Air Traffic Control System Command Center (ATCSCC), Anchorage ARTCC (ZAN), NAV CANADA National Operations Center (NOC), Edmonton ACC, and interested airspace operators.
ATCSCC monitored the LISKI flow via Traffic Flow Management (TFM) tools and the Dynamic Ocean Tracking System (DOTS+)
NOC and ZAN utilized TFM tools along with speed control and vectors to mitigate conflicts to provide 10 minute separation over LISKI

## Slide 4: LISKI Trial Results
Flights denied requested altitude dropped from 10% to 8%
The final telcon on May 9, 2008, including the ATCSCC, Anchorage ARTCC, NAV CANADA NOC, Edmonton ACC, IATA, Continental Airlines, United Airlines and Delta Airlines allowed a consensus decision permanently adopting the trial procedures.
Permanent procedures were effective May 11, 2008

## Slide 5: PILUN Fix
PILUN fix was a added to the Polar Fix procedures on July 31, 2008

## Slide 6: Track Advisory User’s Guide for Dispatchers
Amended October 1, 2008 to include:
For flights transiting LISKI and North, tactical sequencing will be utilized to ensure required in-trail spacing for aircraft at the same altitude. This may include speed control and/or vectors to accomplish the required spacing. For flights transiting via FRENK and south, aircraft must arrive at the gateway fix at the GRL gateway time or no more than 10 minutes later to increase the probability of being assigned the GRL altitude for the waypoints with 20 minutes-in-trail trackload spacing

## Slide 7: Thank You
Notes: <number>
Based on the successful outcome of the trial of ATFM) procedures on Polar routes DEVID, RAMEL, NIKIN and ORVIT, and discussions during the 5th Mtg of the Cross Polar Trans East ATM Providers' Working Group (CPWG/5) held earlier this month in Ft Worth, Texas, the FAA and NAV CANADA have agreed that the procedures will be made permanent for DEVID, RAMEL, NIKIN and ORVIT.
The trial procedures have now been expanded to include Russian Trans East (RTE) fix LISKI. The trial started at 1430 UTC on April 7, 2008 and will continue through May 10, 2008.
Reviews of the trial will be conducted weekly by telcon hosted by the ATCSCC, permitting a consensus decision to be made at the end of the trial period concerning the permanent adoption of the trial concept and procedures. Changes to the agreed procedures will be coordinated with the customers in advance of implementation.
Telcon participants will be Anchorage ARTCC, NAV CANADA NOC, Edmonton ACC, and interested airspace operators. Telcons will be conducted on Fridays through May 9 at 1900 UTC. Participants may dial in by calling +1 703 925 5387 and entering PIN 2777#.
Procedures:
The ATCSCC will no longer issue CDTs for flights destined to RTE entry fix LISKI.
Flight crews are still expected to depart during their 10-minute departure window. Dispatchers must continue to comply with all current Anchorage ARTCC track advisory procedures and will provide feedback during ATCSCC hosted review telcons. This will permit flight dispatchers to remain aware of other traffic which may have flight planned over LISKI.
DOTS+ will provide 10 minutes longitudinal separation between flights going to LISKI at the same altitude. No additional buffer will be provided.
Both the ATCSCC and the NOC will continue to monitor ETMS and DOTS+ to identify possible flight conflicts and implement conflict resolution as needed. The ATCSCC will coordinate with dispatch when appropriate and U.S. ATC units if a conflict or resolution takes place in U.S. airspace. The NOC will coordinate with dispatch when appropriate and Canadian ATC units if a conflict or resolution takes place in Canadian airspace.
The appropriate facility or facilities will determine the appropriate mitigation.
In conjunction with airline operators, the NOC, and Anchorage ARTCC Traffic Management Unit (TMU), will collect documentation related to the test on flights filed over LISKI. Documentation may include, but is not limited to actual departure times, flight planned altitude at LISKI, and actual altitude crossing at LISKI.

## Slide 9
Procedures:
The ATCSCC will no longer issue CDTs for flights destined to RTE entry fix LISKI.
Flight crews are still expected to depart during their 10-minute departure window. Dispatchers must continue to comply with all current Anchorage ARTCC track advisory procedures and will provide feedback during ATCSCC hosted review telcons. This will permit flight dispatchers to remain aware of other traffic which may have flight planned over LISKI.
DOTS+ will provide 10 minutes longitudinal separation between flights going to LISKI at the same altitude. No additional buffer will be provided.
Both the ATCSCC and the NOC will continue to monitor ETMS and DOTS+ to identify possible flight conflicts and implement conflict resolution as needed. The ATCSCC will coordinate with dispatch when appropriate and U.S. ATC units if a conflict or resolution takes place in U.S. airspace. The NOC will coordinate with dispatch when appropriate and Canadian ATC units if a conflict or resolution takes place in Canadian airspace.
The appropriate facility or facilities will determine the appropriate mitigation.
In conjunction with airline operators, the NOC, and Anchorage ARTCC Traffic Management Unit (TMU), will collect documentation related to the test on flights filed over LISKI. Documentation may include, but is not limited to actual departure times, flight planned altitude at LISKI, and actual altitude crossing at LISKI.