## Slide 1: CROSS POLAR AND TRANS EAST
POLAR COMMUNICATIONS

## Slide 2: POLAR COMMUNICATIONS
POLAR COMMUNICATIONS

## Slide 3: POLAR COMMUNICATIONS
INTRODUCTION
Capabilities
  VHF-Voice
  VHF-Data Link
  HF-Voice
  HF-Data Link
  SATCOM-Voice
  SATCOM-Data Link

## Slide 4: POLAR COMMUNICATIONS
HF HISTORY
  Developed in 1920’s and 1930’s
  Standard Comm in US airspace until 1960
  New HF Technologies
    Single Side Band (SSB)
    Digital Tuning

## Slide 5: POLAR COMMUNICATIONS
THE BASICS
  Radio Frequencies 2.0 to 29.999 MHz
  Greatest Value – Reliable Long Range Comm
    HF Signals Reflected back to Earth by Ionosphere
    Power into Audio Signal
  Ground Waves
  Sky Waves

## Slide 6: POLAR COMMUNICATIONS
HF LIMITS
  HF Propagation
    Higher Frequencies daytime
    Lower Frequencies nightime
  Multi-layered Ionosphere
  Ionosphere Reflector effectiveness
  Solar Flares
  Magnetic Storms
  Quality of Communications

## Slide 7: POLAR COMMUNICATIONS
HF SERVICES
  Standard for Oceanic en-route ATC services
    Flight following
    Weather forecasts
    Communications
  HF Data Link
    Polar through Barrow, AK
    Better than voice
  ICAO assigns frequencies for ATC use

## Slide 8: POLAR COMMUNICATIONS
HF SERVICES
  HF radio checks
    Primary
    Secondary
  General Purpose (GP) radio
    3rd Party Radio Operators
    Relay both ATC and AOC
  Long Distance Operational Control (LDOC)
    Flight Regularity Messages
    Operation of Aircraft
    Aircraft Load

## Slide 9: POLAR COMMUNICATIONS
HF Services
  LDOC
    Stockholm Radio – Directional Antennas
    ARINC Radio – Barrow Alaska Location
    Portishead Radio – Europe Location
  HF Radio Propagation
    WWV and WWVH Frequencies
    “K” Index – Scale One to Nine, (Higher # Poor Propagation)
    Solar Flux – 65 to 400, (Higher # Better Propagation)

## Slide 10: POLAR COMMUNICATIONS
HF TECHNIQUES
  Digital Tuning
  Antenna Coupler
    Auto Tuning
    Auto Optimization
    Identifies Action with Tone
  Try Different frequencies
    GP Radio
    LDOC Radio
    VHF relay with other aircraft
  Patience

## Slide 11: POLAR COMMUNICATIONS
SATCOM VOICE
  Inmarsat
    Geo-Synchronous Orbit Satellites
    No service above approximately 82° North or South
  Iridium
    Pole to Pole coverage
    Single GES Phoenix, AZ
  Comm through 3rd Party Radio Operator
  Potential as future LRCS

## Slide 12: POLAR COMMUNICATIONS
GP RADIO
  ARINC
  SITA
  ICELAND RADIO
  EDMONTON
  ANCHORAGE
  GANDER RADIO
  BODO RADIO
  MAGADAN
  MURMANSK
SATCOM
  INMARSAT SATCOM
  DATA & VOICE
  IRIDIUM SATCOM
  DATA & VOICE
  LDOC
  ARINC
  STOCKHOLM
  PORTISHEAD
  CEDAR RAPIDS

## Slide 13: POLAR COMMUNICATIONS
CONCLUSION
HF
  Easy to operate
  Extremely powerful
  Reliable
  Spectrum of services
  Need training
  Need patience

## Slide 14: POLAR COMMUNICATIONS
QUESTIONS
?