## Slide 1
Joe Kunches
NOAA Space Weather Prediction Center
Boulder, Colorado
USA
joseph.kunches@noaa.gov
CPWG/7
June 3-5, 2009
Paris

## Slide 2: Overview
Solar Radiation Storms affect polar operations in two ways:
  Degrade/eliminate HF communications
  Increase radiation dose to aircrew
New products in development offer improved response by airlines
  D-Region Absorption Prediction (D-RAP) release 2
  Nowcast of Atmospheric Ionizing Radiation for Aviation Safety (NAIRAS)
Update on CPWG Space Weather Subgroup Requirements

## Slide 3
D Region Absorption Prediction: Release 2
Requirement
Product
Validation
Feedback
Plans
S. Hill, R. Akmaev, M. Codrescu, R. Craver, J. Vickroy,
C. Schulz, L. Mayer, A. Newman
NOAA Space Weather Prediction Center
H. Sauer
National Geophysical Data Center
Notes: <number>

## Slide 4
Requirement
Communication - FAR 121.99 requires reliable communication over the entire flight route - SATCOM is unavailable above 82N
During solar activity communications can be impacted and HF propagation can be poor
Operational SWPC D Region Absorption Prediction (D RAP) did not accurately represent HF absorption in polar regions
HF Communication only
Notes: <number>

## Slide 5
The Product – Global Map
Accurate HF fade anywhere on Earth
Graphical displays of absorption
Numerical data for download
Feedback survey and product documentation links
Accessible from main SWPC page and operational D-RAP page
http://www.swpc.noaa.gov/drap/index.html
Notes: <number>
New SWPC model to be deployed for testing later this year
Combines low-to-middle latitude absorption driven by solar X-rays with high latitude absorption driven by energetic particles
Use GOES XRS to measure X-rays
Use GOES EPS to measure particles
Challenges include different magnitudes and time scales of absorption
Different physical mechanisms and models different latitude ranges
Different timeliness for supporting model inputs

## Slide 6
Polar Views, Tabular Data
Notes: <number>
New SWPC model to be deployed for testing later this year
Combines low-to-middle latitude absorption driven by solar X-rays with high latitude absorption driven by energetic particles
Use GOES XRS to measure X-rays
Use GOES EPS to measure particles
Challenges include different magnitudes and time scales of absorption
Different physical mechanisms and models different latitude ranges
Different timeliness for supporting model inputs

## Slide 7
Validation and Testing
Purpose
  Expand upon previous validation of each component model (x-ray and proton)
  Establish a basis for ongoing product validation
  Establish basis for integrated system regression testing
Validation Approach
  13 event validation periods including three with combined x-ray and proton events from 1998 to 2005
  Comparison between model results and measurements from up to 9 ground riometer stations
  Calculate means and variances for both data and model, and root mean square differences
Notes: <number>
New SWPC model to be deployed for testing later this year
Combines low-to-middle latitude absorption driven by solar X-rays with high latitude absorption driven by energetic particles
Use GOES XRS to measure X-rays
Use GOES EPS to measure particles
Challenges include different magnitudes and time scales of absorption
Different physical mechanisms and models different latitude ranges
Different timeliness for supporting model inputs

## Slide 8
Product Presentation Feedback Requests
Absorption Thresholds: Will color presentation of frequency using a threshold of 10db on the polar plots (to avoid saturation) versus 1db on the global plot prove more confusing than useful?
Map Gridlines: Is a finer gird of latitude and longitude on images desirable?
Numerical Data: Would a format such as NetCDF or GRIB offer better integration into customer systems than the current ASCII format?
NOTAM/SIGMET messages: Would NOTAM/SIGMET alerts be a beneficial addition?
Absorption Presentation: Would presentation of absorption at a specified frequency be a beneficial addition?
Notes: <number>
New SWPC model to be deployed for testing later this year
Combines low-to-middle latitude absorption driven by solar X-rays with high latitude absorption driven by energetic particles
Use GOES XRS to measure X-rays
Use GOES EPS to measure particles
Challenges include different magnitudes and time scales of absorption
Different physical mechanisms and models different latitude ranges
Different timeliness for supporting model inputs

## Slide 9
Plans
Contact Information:
Dr. Steven M Hill
Development and Transition Section Lead
NOAA Space Weather Prediction Center
325 Broadway
Boulder, CO 80305
303-497-3283
steven.hill@noaa.gov
Summer 2008 – Summer 2009: Customer Feedback Period on NWS enhanced product
Spring 2009 – Summer 2009 – Continued validation, improvements for operational robustness, user requested changes
Fall ’09 – Deploy as an operational NWS product and discontinue old D Region product
Sometime, anytime, an x-ray or proton event please!
Notes: <number>

## Slide 10: Nowcast of Atmospheric Ionizing Radiation for Aviation Safety (NAIRAS) Model
Christopher J. Mertens
NASA Langley Research Center
Hampton, Virginia
Notes: <number>

## Slide 11: Nowcast of Atmospheric Ionizing Radiation for Aviation Safety NAIRAS Model
Develop prototype operational aircraft radiation exposure model (adopt meteorological paradigm)
  Global
  Real-Time
  Data-Driven
  Dynamic Geomagnetic Shielding
  Physics-based radiation transport and dosimetry
Team Organizations
  NASA Langley Research Center
  Space Environment Technologies, Inc.
  Dartmouth College
  NCAR High Altitude Observatory
  NOAA/SWPC
  CDC/NIOSH

## Slide 12: Nowcast of Atmospheric Ionizing Radiation for Aviation Safety NAIRAS Unique Features
Global
  Geographic coverage: pole-to-pole
  Altitude converge: Surface to 100 km
Real-time
  1 hr SEP
  3 hr GCR
Data-Driven
  Solar-Cycle GCR Modulation: Ground-based neutron monitors
  SEP spectra: NASA/ACE + NOAA/GOES
  Geomagnetic storm effects on cutoff rigidity: NASA/ACE solar wind measurements
  Atmospheric density: NCEP Global Forecasting System (GFS) Reanalysis (8x daily)
Geomagnetic Shielding (solar wind-magnetosphere coupling)
  Internal Field: IGRF
  Magnetospheric magnetic field
    Tsyganenko T05 (semi-empirical)
    LFM MHD (physics-based)
  Cutoff rigidities: Dartmouth-CISM (physics-based)
Physics-based transport and dosimetry
  High Charge and Energy Transport (HZETRN) Model

## Slide 13
NAIRAS Operational Distributed Network System

## Slide 14: Nowcast of Atmospheric Ionizing Radiation for Aviation Safety Step 1 in NAIRAS Transition to Operations
Experimental Data Products for Community Evaluation
  4-D Effective Dose (netcdf)
  Global Effective Dose Graphics
  Routine Flight Planning tools
    Professional aviation community
  Browsers and Google Earth
    Frequent flyers and public education
Data Availability
  NOAA Aviation Digital Data Service (ADDS) experimental data products web interface
    Commitment from NOAA NWS Aviation Services Branch
  Space Environment Technologies (SET)
    IPS MeteoStar

## Slide 15: Nowcast of Atmospheric Ionizing Radiation for Aviation Safety Step 1 in NAIRAS Transition to Operations
Verification and Validation
  We are establishing a core team to propose new aircraft dosimetric measurements
  We are interested in comparing with previous aircraft dosimetric measurements. Contact me!
Project Status, News, Milestones, and Sample Output
  Register to keep informed at our public website
    Receive Quarterly Reports
  http://sol.spacenvironment.net/~nairas/

## Slide 16: CPWG Space Weather Subgroup Requirements Document
In draft to be released for comment soon
Aim for submission to CPWG/8
Integrating Space Weather
Observations & Forecasts into
Aviation Operations
“Aviation Space Weather User Requirements”