## Slide 1
Edmonton Area Control Centre presentation to the CROSS POLAR WORKING GROUP “Step Climb Trial” Atlanta, Georgia, U.S.A Dec 2-4, 2009 Presented by:
Bryon Carlson, Edmonton ACC North High Supervisor
Notes: Also Present at CPWG –
Butch March, Manager Area Control Centre Operations, Edmonton
Chris Collins, Team Supervisor, Edmonton ACC

## Slide 2
Step Climb Trial
Standard cruising altitudes are not always most efficient.
Best fuel efficiency may be attained by continuous (or step) climb.
Notes: Flying at standard cruising altitudes does not always result in optimal fuel efficiency for many flights.
The best fuel efficiency for aircraft in the cruise portion of flight may be attained by maintaining a continuous (or step) climb rate of ~ 10 – 200 feet/minute.

## Slide 3
Emirates Request
Photo source: www.emirates.com
Emirates (UAE) contacted NAV CANADA in Sept./09 with a request to commence a step climb trial using block altitudes to improve fuel efficiency.
The request presented a challenge.
Notes: Emirates (UAE) contacted NAV CANADA in Sept./09 with a request to commence a step climb trial using block altitudes to improve fuel efficiency.
The request presented a challenge.

## Slide 4
What Was The Challenge?
Block altitudes allow operational flexibility for many instances such as icing, aerial surveys, flight checks, turbulence, and fuel. The MANOPS direction for issuing block altitudes is:
432.2 B.
“An aircraft requests it because of icing,
turbulence, or fuel considerations provided:…”
432.2 B. Note:
“Fuel considerations” means that an aircraft will
make a request only to avoid a fuel situation that
might cause an otherwise unnecessary technical
stop short of flight planned destination.
MANOPS block altitude rules did not support requests for the reason of “fuel efficiency.”
Notes: Block altitude. Block altitudes do currently allow operational flexibility for many instances such as icing, aerial surveys, flight checks, turbulence, and fuel. The (abbreviated) MANOPS (Manual of Operations) direction for issuing block altitudes, as it pertains to this discussion, is:
432.2 B.
“An aircraft requests it because of icing,
turbulence, or fuel considerations provided:…”
432.2 B. Note:
“Fuel considerations” means that an aircraft will
make a request only to avoid a fuel situation that
might cause an otherwise unnecessary technical
stop short of flight planned destination.
MANOPS block altitude rules did not support requests for the reason of “fuel efficiency.”

## Slide 5
What has NAV CANADA done?
A revised trial procedure is being proposed by NAV CANADA.
It is being integrated into MANOPS:
“WHEN READY”
“WHEN READY” allows the option of commencing the altitude change at some point in the future.
“WHEN READY” allows the option of climbing and/or descending at any given rate; and,
“WHEN READY” allows the option of levelling off at any intermediate altitude.
Notes: What did NAV CANADA do to allow more flexible step climb procedures?
A new trial procedure is being proposed NAV CANADA, and consideration is being given to integration into MANOPS:
“WHEN READY”
The use of “WHEN READY” with an altitude assignment allows the pilot the option of commencing the altitude change at some point in the future.
“WHEN READY” also allows the pilot the option of climbing and/or descending at any given rate, as well as the option of levelling off at any intermediate altitude.

## Slide 6
Operational Considerations
The Edmonton FIR is an ideal geographical area to test this procedure.
7 of the top 10 longest range scheduled flights in the world regularly enter the Edmonton FIR.
  Many are operating near the limits of aircraft endurance.
Notes: Operational considerations:
The Edmonton FIR is an ideal geographical area to test this new procedure. NAV CANADA would like to accommodate as many flights as possible in this trial.
Pros:
Many of the flights crossing the Edmonton FIR are amongst the longest range flights in the world. Therefore, they can benefit the most from this trial as many are operating near the limits of aircraft range and endurance. From the attached list, it is seen that 7 of the top 10 (and 13 of the top 20), longest range scheduled flights in the world regularly enter the Edmonton FIR (and not all are “polar” either!)

## Slide 7
World’s Longest Range Flights
Rank | Departure | Destination | Flight | Type | Distance | Duration
1 | KEWR | WSSS | SIN21 | A345 | 8285 | 18+50
2 | KLAX | WSSS | SIN37 | A345 | 7621 | 17+20
3 | FAJS | KATL | DAL201 | B77L | 7334 | 16+15
4 | OMDB | KLAX | UAE215 | B77L | 7246 | 16+35
5 | KLAX | VTBK | THA795 | A345 | 7186 | 17+30
6 | OMDB | KIAH | UAE211 | B77L | 7097 | 16+20
7 | OMDB | KSFO | UAE225 | B77L | 7041 | 16+00
8 | KJFK | VHHH | CPA831 | B77W | 7014 | 16+00
9 | KJFK | VHHH | CPA841 | B77W | 7014 | 16+00
10 | KEWR | VHHH | COA99 | B772 | 7009 | 15+50
7/10 flights regularly enter the Edmonton FIR (in italics)
Including UAE 215 & UAE225 (in bold)

## Slide 8
Operational Considerations
Although many flights operate at “peak times” of day, some operate at “off peak times” allowing greater operational flexibility on the part of ATC.
Traffic conflicts/density.
Daily changes in the Jet Stream and/or MTT’s.
Communications (or lack thereof). HF and Sat. Comm. limitations.
Controller workload.
Coordination with other units and agencies may prevent utilization.
Notes: Although many flights operate at “peak times” of day, some operate at “off peak times” allowing greater operational flexibility on the part of ATC.
Cons:
Traffic conflicts/density.
Daily changes in the Jet Stream and/or MTT’s.
Communications (or lack thereof). HF and Sat Comm. limitations.
Controller workload.
Coordination with other units and agencies may prevent utilization

## Slide 9
General Traffic Patterns
to/from Alaska/Asia
to/from Asia
to/from Asia
to/from India/Middle East
to/from India/Middle East
Notes: These traffic patterns relate to CPWG only, and do not include NAT or domestic.
The generalised traffic flows are:
Canada & USA (lower 48) to/from Japan, China, South Korea & SE Asia.
Canada & USA (lower 48) to/from India and Middle East.
Canada & USA (lower 48) to/from Alaska.

## Slide 10
Parameters for “WHEN READY”
Clearance will be in the form of being cleared to cross a down-line fix at standard cruising altitude, or in the form of being cleared to reach a standard cruising altitude by a particular time.
1000-2000’ climbs over a 1-3 hour time frame expected.
Dispatchers should flight plan at standard cruising altitudes for the duration of their flights through Edmonton FIR in the event that a “WHEN READY” request is denied.
Once vacated, the pilot may not return to that altitude.
Pilots are expected to advise ATC of altitude change and of levelling-off at an intermediate altitude.
ATC can cancel the clearance at any time and re-clear a flight to a standard cruising altitude.
Notes: When requested, a flight will normally be issued a “WHEN READY” clearance in the form of being cleared to cross a down-line fix at standard cruising altitude, or in the form of being cleared to reach a standard cruising altitude by a particular time in accordance with a flight’s initial request. It will generally be expected that such requests will be for 1000-2000’ climbs over a 1-3 hour time frame, but other permutations will be available.
It is expected that all affected airlines will advise their flight crews of the availability of this test trial. It is also cautioned that airlines should flight plan at standard cruising altitudes for the duration of their flights through Edmonton FIR in the event that a “WHEN READY” request is denied by ATC.
Once an altitude has been vacated, the pilot may not return to that altitude.
Pilots are expected to advise ATC when the altitude change is initiated and whether any levelling-off at an intermediate altitude occurs. should also be noted that once a “WHEN READY” clearance has been issued, that ATC can cancel the clearance at any time and re-clear a flight to a standard cruising altitude.

## Slide 11
Going Forward (next 6 months)
Timeline ~ 6 months.
We are initiating this trial procedure with UAE215 & UAE225 only.
Why?
- requested
- #4 & #7 longest flights in the world
- easy to accommodate (traffic & workload)
- good evaluation of trial
Follow up at CPWG/9
Notes: Timeline – 6 months??
We are initiating this trial procedure with UAE215 & UAE225 only.
Why?
- requested

## Slide 12
Questions???
?

## Slide 13
Thank you / Merci