## Slide 1
Edmonton Area Control Centre presentation to the CROSS POLAR WORKING GROUP “FL360 at RAMEL – an Edmonton Perspective” Montreal, Quebec, Canada April 28-30, 2010 Presented by: Bryon Carlson, Edmonton ACC North High Supervisor
Notes: Also Present at CPWG –
Butch March, Manager Area Control Centre Operations, Edmonton
Dave Rose, Manager NOC, Ottawa
Corey Ness, Air Traffic Controller, Edmonton ACC

## Slide 2: FL360 at RAMEL
The ability to use FL360 at RAMEL has been very positively accepted in Edmonton
Edmonton plans westbound traffic flow at RAMEL
Allows Controllers more options for planning traffic
Climbing to FL380 after RAMEL, instead of before RAMEL, has been the difference between reaching, and not reaching, FL380 for some flights
Notes: The ability to use FL360 at RAMEL has been very positively accepted in Edmonton
Edmonton plans westbound traffic flow at RAMEL
Allows Controllers more options for planning traffic
Climbing to FL380 after RAMEL, instead of before RAMEL, has been the difference between reaching, and not reaching, FL380 for some flights

## Slide 3: Altitude Transitions at RAMEL
FL380
FL360
RAMEL
FL381/11600m
FL340
FL348/10600m
FL320
FL300
FL315/9600m
Notes: FL360 & FL380 transition to the same altitude – FL381/11600m
FL300 & FL320 transition to the same altitude – FL315/9600m
FL340 transitions exclusively to FL348/10600m

## Slide 4: FL360 at RAMEL
One challenge has been noticed with the use of FL360:
“What is the altitude expectation after passing RAMEL?”
FL360 transitions to FL381/11600m.
FL360
FL380
FL381/11600m
Notes: One challenge has been noticed with the use of FL360:
“What is the altitude expectation after passing RAMEL?”
FL360 transitions to FL381/11600m. It is not evident that all Controllers and Pilots understand this. This is not normally a problem when dispatch files FL360 over RAMEL, but has been a problem when flights previously planned at FL340 have been tactically moved to FL360.

## Slide 5: FL360 at RAMEL
Dispatch plans FL381/11600m……..most of the time……..
Instances have been noted of FL360 filed in GRL with FL348/10600m planned after RAMEL
Doesn’t work very well with another flight at FL340!
FL360
FL348/10600m
FL340
RAMEL
Notes: Dispatch plans FL381/11600m……..most of the time……..
Instances have been noted of FL360 filed in GRL with FL348/10600m planned after RAMEL
Doesn’t work very well with another flight at FL340!

## Slide 6: Tactical use of FL360 at RAMEL
Flights planned at FL340 have been tactically climbed to FL360, but are sometimes unable to climb higher after RAMEL
Both flights would then transition to FL348/10600m
Doesn’t work very well either!!
FL360
FL348/10600m
FL340
RAMEL
Notes: Flights planned at FL340 have been tactically climbed to FL360, but are sometimes unable to climb higher after RAMEL
Both flights would then transition to FL348/10600m
Doesn’t work very well either!!

## Slide 7: What should happen….
Altitudes appropriate for both
Efficient, planned, & productive!
FL348/10600m
FL360
FL340
FL315/9600m
RAMEL
FL381/11600m
Notes: Altitudes appropriate for both
Efficient, planned, & productive!

## Slide 8: What might happen…...
A flight might be able to use FL364/11100m “wrong way” if unable FL381/11600m
Depends on presence of eastbound traffic
Efficient altitude, but based on luck!
FL348/10600m
FL360
FL340
RAMEL
FL364/11100m
Notes: A flight might be able to use FL364/11100m “wrong way”/inappropriate for direction of flight
Depends on presence of eastbound traffic
Efficient altitude, but based on luck

## Slide 9: What might happen……
Altitude penalties for both
Inefficient, not planned, and counterproductive!
FL348/10600m
FL360
FL340
FL315/9600m
RAMEL
FL381/11600m
Notes: Resulting in altitude penalties after RAMEL for both aircraft as one would transition to FL348/10600m & the other to FL315/9600m
Inefficient and counterproductive!

## Slide 10: FL360 at RAMEL
What can be done to mitigate such scenarios?
Greater awareness on the part of pilots, dispatchers, and ATC that FL381/11600m is expected after RAMEL.
Notes: What can be done to mitigate such scenarios?
Greater awareness on the part of pilots, dispatchers, and ATC that FL381/11600m is expected after RAMEL.

## Slide 11: Going forward…..
Why is Edmonton opposed to combining FL340 & FL360 at RAMEL/NIKIN instead of the current arrangement of FL360 & FL380?
FL348/10600m is popular, and would become more crowded
Aircraft pushed to FL300/FL320 when FL340/360 combined
Notes: Why is Edmonton opposed to the idea of combining FL340 & FL360 at RAMEL instead of the current arrangement?
Edmonton supports the inclusion of NIKIN in the FL360 trial, but opposes combining FL340/Fl360 at either RAMEL or NIKIN
FL348/10600m is popular, and would become more crowded
Increased use of FL300/FL320

## Slide 12: Going forward…..
FL380
FL360
RAMEL/NIKIN
FL381/11600m
FL340
FL348/10600m
FL320
FL300
FL315/9600m
Notes: Why is Edmonton opposed to the idea of combining FL340 & FL360 at RAMEL instead of the current arrangement?
FL348/10600m is popular, and would become more crowded
Flights that could usually transition to FL381/11600m would be forced to FL348/10600m, only to climb to FL381/11600m shortly thereafter (especially in the case of B772/B773)
There would be increased use of FL300/FL320 as a result of flights descending from FL360 to FL340.

## Slide 13: Going forward…..
Edmonton supports “status quo” FL360/380
Edmonton supports the inclusion of NIKIN in the FL360 trial
Customer input is crucial to the way ahead
Greater awareness on the part of pilots, dispatchers, and ATC that FL381/11600m is expected after RAMEL is better than treating FL340 & FL360 as one altitude.
Notes: Edmonton supports “status quo” in regards to combining FL360 with FL380, but supports the inclusion of NIKIN in the FL360 trial.
Greater awareness on the part of pilots, dispatchers, and ATC that FL381/11600m is expected after RAMEL is better than treating FL340 & FL360 as one altitude.

## Slide 14: FL360 at RAMEL
Comments from Russia &/or FAA?
Questions???