## Slide 1
CPWG/9
Montreal
April 28-30, 2010
CPDLC Processing
With PAZA
CP06-02

## Slide 2: CPDLC processing with PAZA
CPDLC processing begins with an ATS Facilities Notification (AFN) logon
The IATA address for PAZA is ANCXFXA
PAZA will accept any logon. No flight plan or tail number on file is required
Once an AFN logon has been established, the CPDLC connection is automatically requested

## Slide 3: CPDLC processing with PAZA
CPDLC messages are sent directly to the responsible controller
They are displayed on a 20” monitor at the controller workstation

## Slide 4: CPDLC processing with PAZA
ATC clearances automatically update the flight profile
Position reports automatically update flight times
Controllers do not know by what means (SATCOM, HF or VHF) that a CPDLC message is being transmitted

## Slide 5: CPDLC processing with PAZA
PAZA does address forwarding of the AFN logon. This is a VSP that is adaptable per adjacent FIR
The Next Data Authority (NDA) uplink is generally sent 30 minutes prior to exiting the FIR
The End Of Service (EOS) uplink is generally sent 10 minutes before exiting the FIR

## Slide 6
Questions ?