## Slide 1: Cross-Polar and Trans-East Airways in Database and Charts
JEPPESEN PROPRIETARY
Volker Meyer
Manager International Relations
CPWG/9
Montreal, 28 - 30 April, 2010
Notes: <number>

## Slide 2: AGENDA
TOPICS
01 Jeppesen in the Data Supply Chain
02 Timelines for Database
03 Timelines for Charts
04 Jeppesen Chart-Production Process
JEPPESEN PROPRIETARY

## Slide 3: Commercial Data Providers in the Data Supply Chain
Quotes from ICAO Annex 15
JEPPESEN PROPRIETARY

## Slide 4: Primary AIM Stakeholders
There are generally four tiers of AIM stakeholders, each with different roles, responsibilities, obligations and needs.
State Civil Aviation Authority
End user
Commercial Service Provider
State Designated Service Provider
State government organization responsible for the safety, regularity and efficiency of aviation within its borders, per the Chicago Convention.
An organization, often referred to as an ANSP, designated by a State to fulfill some of the State obligations for AIS/AIM provision. ANSPs are often „corporatized“ organizations..
An organization that creates value-added services from the „official“ facts, data and aeronautical information of the State and delivers these services to end users.
Pilots, aircraft operators, ATM organizations, flight support organizations and other entities that use aeronautical information and the resulting value-added services to support safe, efficient and orderly flight operations.
JEPPESEN PROPRIETARY

## Slide 5: The Aeronautical Data Supply Chain … Downstream Data Operation during each AIRAC Cycle
AIP source
Data Coding
Verification
Edits (on-line, Graphic, human, etc)
ARINC 424 Data
FMS Data Extracts
FMS Data Pack
Data Verification
FMS Databases
FMS Data Reports
Aircraft Load
Commercial Data Providers
FMS Database
Processors
ARINC 424 Data Extracts
Numerous database extracts are needed to support all legacy FMS systems and to meet airline and operator needs
ARINC 424 Data QC
Avionics Edits
Source Management
Edit Reports
Notes: <number>

## Slide 6: The best data in respect to accuracy, resolution and integrity does not help if it comes too late.
JEPPESEN PROPRIETARY
Quotes from ICAO Annex 15

## Slide 7
6 MAY
8 APR
Publication
Date
11 MAR
14 Days
Shipping
-42 Days
-28 Days
Data Due
to Recipient*
28-Day AIRAC Cycle
0 Days
Effective Date
-56 Days
for Major Changes
25 MAR
16 APR
-20 Days
Database
Cut-Off
Jeppesen Navigation Database
Updated every 28 days (AIRAC system)
No updates outside AIRAC system
An airway will not be in the database at the effective date if
  the effective date is outside the AIRAC system
  source was received late
  the ANSP is not responding to clarifications
Cancellation of changes has to follow the AIRAC system as well
Adherence to the AIRAC system will ensure that the airway is in the database
Source received on paper or PDF
JEPPESEN PROPRIETARY
Jeppesen Production Process in sync with ICAO Publication Dates according to Annex 15
Notes: Aeronautical Information in the 21st Century, CHAIN Awareness Workshop Malta
Presented by Werner Kurz, Jeppesen
<number>

## Slide 8
6 MAY
8 APR
Publication
Date
11 MAR
14 Days
Shipping
-42 Days
-28 Days
Data Due
to Recipient*
28-Day AIRAC Cycle
0 Days
Effective Date
-56 Days
for Major Changes
25 MAR
23 APR
-13 Days
1st Publication Date
Jeppesen Enroute Charts
Not updated every 28 days
Updated in accordance with Jeppesen chart process criteria
May be updated outside AIRAC system
Changes covered by Chart Change Notices each cycle
An airway will not be on the chart if
  source was received late
  the ANSP is not responding to clarifications
Source received on paper or PDF
30 APR
-6 Days
2nd Publication Date
14 APR
-22 Days
Production
Cut-Off
JEPPESEN PROPRIETARY
Jeppesen Production Process in sync with ICAO Publication Dates according to Annex 15
Notes: Aeronautical Information in the 21st Century, CHAIN Awareness Workshop Malta
Presented by Werner Kurz, Jeppesen
<number>

## Slide 9
Jeppesen Chart-Production Process
Source for Jeppesen is the Aeronautical Information Package / Contact is the ANSP
Source from US, Canada, Japan processed in Denver
Source from Russia, Iceland, Norway, China, Mongolia processed in Frankfurt
FE charts and AP (HI) 1 / NP (HI) 2 made in Denver
EA charts and AT charts made in Frankfurt
Overlap area requires additional coordination
AP (HI) 1 – “aeronautical information is complete for the polar routes”?
Polar Orientation Chart – “for the plotting of position and course information”?
All charts printed in HQ for hemisphere where customer is based
Enroute data in data-driven charts (JeppView, eLink for Windows, FliteStar,
JetPlanner) comes out of a database, which is updated every 28 days
Jeppesen Navigation Charts
Notes: Aeronautical Information in the 21st Century, CHAIN Awareness Workshop Malta
Presented by Werner Kurz, Jeppesen
<number>

## Slide 10
History of New ATS Routes from LISKI and PILUN (G912, B969), eff. 30 JUL 09
Jeppesen Chart-Production Process
Notes: Aeronautical Information in the 21st Century, CHAIN Awareness Workshop Malta
Presented by Werner Kurz, Jeppesen
<number>

## Slide 11
10 JUL
30 JUL
2 JUL
Publication
Date
14 Days
Shipping
-42 Days
-28 Days
Data Due
to Recipient*
28-Day AIRAC Cycle
0 Days
Effective Date
18 JUN
-20 Days
Database
Cut-Off
15 JUN
AIRAC Amendment received at Jeppesen
30 JUL
Database in FMS
14 AUG
Charts printed and distributed
5 AUG
Charts to printing
5 AUG
14 AUG
+6 Days
Production
Cut-Off
+15 Days
Publication Date
Jeppesen Chart-Production Process
JEPPESEN PROPRIETARY
History of New ATS Routes from LISKI and PILUN (G912, B969), eff. 30 JUL 09
24 JUL
Chart Change Notice
24 JUL
Notes: Aeronautical Information in the 21st Century, CHAIN Awareness Workshop Malta
Presented by Werner Kurz, Jeppesen
<number>

## Slide 12
Changes from States – each cycle
Jeppesen navigation database – each cycle
Jeppesen charts updated – not every cycle:
  EA (H/L) 11/12
  18 JAN 08, 25 APR 08, 22 AUG 08, 7 NOV 08, 5 DEC 08,
  22 MAY 09, 14 AUG 09, 6 NOV 09
  est. 23 APR 10
  AP (HI) 1 / NP (HI) 2
  11 JAN 08, 7 MAR 08, 25 JUL 08, 3 OCT 08,
  6 MAR 09, 7 MAY 09, 4 SEP 09
  8 JAN 10, 19 FEB 10
Changes included in database and covered by Chart Change Notices each cycle
Transition to electronic charts (data driven)
Proactive coordination between airlines and Jeppesen
Jeppesen Enroute Charts
Jeppesen Chart-Production Process
JEPPESEN PROPRIETARY
Notes: Aeronautical Information in the 21st Century, CHAIN Awareness Workshop Malta
Presented by Werner Kurz, Jeppesen
<number>

## Slide 13: Thank you
JEPPESEN PROPRIETARY
Volker Meyer
Manager International Relations
Government & Industry Affairs
______________________________________
Jeppesen
A Boeing Company
phone: +49 6102 50 7240
fax: +49 6102 50 7239
volker.meyer@jeppesen.com
www.jeppesen.com
Notes: <number>