## Slide 1
Tactical Reroutes Test
April 30, 2010
FAA, Anchorage ARTCC
Greg Howard

## Slide 2: Original Flight Plan
FPL-UAL803-IS
-B772/H-SGHIJPRWXYZ/SD
-KIAD1643
-N0479F320 DCT JERES J220 MICAH DCT PSB J61 BUF/N0488F320 DCT YYZ/N0485F320 J556 YEE J557 YSB DCT YYU NCA19 YGX DCT 59N100W DCT BENAX
NCA25 EBGUT/N0480F340 NCA25 YVQ/N0481F360 NCA24 FIORD/N0480F360 NCA24 GAL J122 OME/K0896S1160 DCT ERNIK B240 PAKLI/M082F380 B337 AWE V7 CHE Y10 GOC R211 KASMI DCT
-RJAA1303

## Slide 3: Initial Evaluation & Collaboration with ZAN TMU
UAL803 and estimating ERNIK at 0013Z with a slot at 0011Z
UAL Dispatcher reviewed route options, after a simulated call from UAL803 advised of a possible flight level constraint due to traffic. UAL808 slot at ERNIK was for 11600M.
UAL Dispatcher called ZAN TMU and collaborated, making a decision to “test tactical re-route via FRENK G902 at 10600M
ZAN TMU made initial coordination internally with ZAN controllers

## Slide 4: Coordination of Flight Plan with MATMC
UAL dispatcher sent the following SITA message to MATMC at 2314Z
QU MOWYWYA CHI80D HDQDH
.CHIARUA 072314 043272 438/260918
****** TEST ONLY ******
REQUEST YOUR APPROVAL FOR TACTICAL RE-ROUTE VIA FOLLOWING FPL PLS ACK AND SEND APPROVAL TO CHI80UA AND HDQDHUA
FPL-UAL803-IS
-B772/H-SGHIJPRWXYZ/SD
-KIAD1641
-N0488F320 DCT JERES J220 MICAH DCT PSB J61 BUF/N0488F310 DCT YYZ/N0485F320 J556 YEE J557 YSB DCT YYU NCA19 YGX DCT 59N100W DCT BENAX NCA25 EBGUT/N0480F340 NCA25 YVQ/N0481F360 DCT BITRO DCT POTAT/K0883S1060 DCT FRENK G902 UTILI/K0898S1160 G902 ASBAT B337 BUMAT B484 OTLIM B962 OLAMA B337 PAKLI/M082F380 B337 AWE V7 CHE Y10 GOC R211 KASMI DCT
-RJAA1303
Shortly after this message was sent, the UAL dispatcher called the MATMC by telephone to confirm receipt

## Slide 5: Tactical Reroute Acknowledgement
  The following SITA message was received from Moscow at 2326Z
  QU CHIARUA CHI80UA HDQDHUA
  .MOWYWYA 072326
  SUBJ: RE:
  FROM: YURY YEGORUSHKIN
  ACK AND CONFIRM THE TACTICAL RE-ROUTE VIA ROUTE STATED IN
  FPL BELOW IS APPROVED.
  THANKS AND REGARDS,
  YURY EGORUSHKIN
  OSD TEAM DUTY OFFICER
  MAIN ATM CENTER OF RUSSIA
  -------------------------
  //// TEST ONLY ////
  UAL dispatcher then called ZAN TMU to confirm “TEST” approval from MATMC

## Slide 6: Summary & Discussion
Overall, the process worked well. The UAL dispatcher suggested that after being made aware of the altitude/slot concern, the best course of action would be to call ZAN TMU and ask for TMU’s initial recommendation of route options to speed the process of determining a possible reroute entry fix.
The other “To Be Determined” aspect is once approval is received from Moscow, what are the next steps?
After receipt of approval, the dispatcher calls ZAN and advises approval received. Does the dispatcher then transmit a new FPL from departure airport to destination airport (entire route behind us included) and address this FPL to PAZAZQZX and all Russians FIRs, and Japan? Or do they send it only to Russian FIRs and have Anchorage coordinate the transfer of control based on this “verbal” approval?
It should be noted that it is not customary for an operator to re-file an FPL once en-route, however operators have done this on occasion with Anchorage for flights over Russia that have changed routes. We need to come to a resolution that makes this easy and affective for all parties.

## Slide 8
QUESTIONS
COMMENTS
FEEDBACK