## Slide 1: FAA CRA Problem Report Activity Since IPACG-22
IPACG-23/FIT-10
Tokyo, Japan
11-12 July, 2005
Gordon Sandell

## Slide 2: Problem Reports
Problems Closed at ISPACG-19/FIT-12
Problem Reports Received by FAA CRA
Problems Reported Since IPACG-22/FIT-9
  New Problem Reports
  Problem Reports Requiring Discussion
SATCOM Issue

## Slide 3: Problems Reports Closed at ISPACG-22/FIT-12
Closed by FANS A+
To Be Closed by 777 AIMS Block Point ’05
  Block Point 03C
Other Closed PRs

## Slide 4: Closed by FANS A+ Standard
462 A340 - Old freetext appended to Pos Report
468 A340 - Loss of ADS

## Slide 5: PRs to Be Closed by 777 Block Point 05
To be certified 4Q05 (AIMS-2), 1Q06 (AIMS-1)
FIT PRs to be fixed:
  287 difficulties establishing CPDLC connection with B777
    BP ’03 fix resulted in null characters in [icaoidentification] variable
    BP ’05 fix correctly encodes active center ID
  448 777 - Unable to Load Uplinked Route Clearance after WILCO
  449 777 - Flight Number Synchronization Problem
  463 777 - Position encoding difficulties
  470 777 BP '03 Unable to datalink over satcom

## Slide 6: Block Point 03C
Corrects PR 470 for AIMS 1-equipped aircraft.
Boeing released Service Bulletin 777-31-0104, dated 2 June 2005
  allows for retrofit installation of the AIMS BP03C software upgrade on AIMS-1 platform equipped 777 airplanes.
  Service Bulletin 777-31-0104 is available on the MyBoeingFleet website.
  A Boeing service letter will be released within the next few weeks on this topic that provides relevant details for incorporating this retrofit.
Correction will be incorporated into BP 05 for AIMS II - equipped aircraft (1Q '06)

## Slide 7: Other PRs Closed at ISPACG-22
456 A340 - downlink timestamps ahead of actual time
457 A340 - responded to emergency free text uplink with error
465 Intermittent difficulties establishing CPDLC connection with one ATSU
473 Failure to forward media advisories
475 Delayed CPDLC downlink
482 Early transfers causing logon rejections

## Slide 8: Problem Reports Received by FAA CRA Relating to NOPAC
2 NOPAC problems notified to FAA CRA since IPACG-22
DATALINK LOST while logging on to ATC Center
  Problem occurred at the time of DSP’s SATCOM GES outage
  Known SATCOM event, no PR written
UNABLE TO SEND MESSAGE in scratchpad on 767
  Occurs when there is protocol problem with FMC-ACARS
  Can also occur with ARINC 429/wiring problems
  System working as designed, no PR written

## Slide 9: New Problem Reports
New Problem Report Summary
Specific Reports for Discussion

## Slide 10: New Problem Report Summary
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
455 | 747-400 - incorrect timestamp in ADS report | SOPAC | Air | There were two events reported for this aircraft. The first was that the airplane sent the same waypoint change event report five times over a period of 10 minutes. The second event was that the airplane sent a waypoint event report with an erroneous timestamp. | OPEN | No
456 | A340 - downlink timestamps ahead of actual time | SOPAC | Air | Per the reporting individual, "It appears that the times in the timestamps are in advance of actual time. I base this on the fact that our system receipt timestamp is earlier than the message timestamp". This appears to have been the result of a dual GPS failure. | CLOSED | No
457 | A340 - responded to emergency free text uplink with error | SOPAC | Air | When the emergency level free text message "FOR<SP>TEST<SP>PURPOSES<SP>" was uplinked, the airplane responded with, error (insufficient data). It appears that the avionics discarded the message due the intermittent failure of the flight phase source. | CLOSED | No

## Slide 11: New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
458 | 767 encoded 60 minutes in [minuteslatitudelongitude] variable | NOPAC | Air | Pegasus FMC encoded 60 minutes in [minuteslatitudelongitude] variable. The vendor has identified the source of the problem. The FMC vendor has identified the source of the problem. | OPEN | Yes
459 | 747-400 FMC encoded 512 degrees for wind direction in Pos Report | SOPAC | Air | 747-400 FMC encoded 512 degrees for wind direction in Pos Report. This was supposed to have been fixed in Load 15 but code analysis has revealed that the fix was incomplete. | OPEN | No
460 | A340 - ATSU unable to establish connection with airplane | SOPAC | Air | Per the reporting individual, "ADS appeared to be working OK. CPDLC Connection established, but aircraft did not receive any of the messages sent". | OPEN | No

## Slide 12: New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
461 | Aircraft unable to logon to one ATSU | SOPAC | Ground | The ground automation did not recognize that a particular aircraft was no longer logged on. When another logon was received, it was ignored. This continued for a number of days, until the problem was (inadvertently) corrected by a scheduled air ground processor switchover. | OPEN | No
462 | A340 - Old freetext appended to Pos Report | SOPAC | Air | Per the reporting individual, an 'old' free text message that may have been previously sent by the aircraft managed to get appended to a position report sent some time later. This issue is corrected in the FANS A+ avionics. | CLOSED | No
463 | 777 - Position encoding difficulties | SOPAC NOPAC | Air | It is possible to downlink a message element that includes the [position] variable with either no data encoded for the [position] or with the last valid value encoded. This problem will be corrected in BP '05 | To be closed when BP05 certified | Yes

## Slide 13: New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
464 | 767 sent altitude request with garbage free text appended | NOPAC | Air | An ATSU reported receiving the following message from a 767: 11,,08:57:43 0(9) : Request Climb To [alt] alt(fl): 350 1(65) : Due To Weather 2(67) : [freetext] freetext(): [40][01][60][00]C[7A][00][00]F[1C][40][00]F[0C]<SP>[00][00][00][00][00]RJAA | In Progress | Yes
465 | Intermittent difficulties establishing CPDLC connection with one ATSU | SOPAC | Ground | Flight crews on two aircraft tried a number of times to log on. Each time the ATSU system acknowledged the logon, but failed to send the CR1 uplink to establish the CPDLC connection. ADS appeared to be working fine. This problem was corrected in September, 2004. | CLOSED | No

## Slide 14
New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
466 | Message sent to wrong aircraft | SOPAC | Ground | The flight crew had requested and been granted climb to FL370. Approx 3 minutes later they received uplink indicating "ATCA UNABLE DUE TO CROSSING TRAFFIC. REQUEST ON FILE". There was concern as to whether or not they had been cleared to FL 370. A free text message was received confirming cleared FL370 and backed up with voice. The crew suspected the message had been sent to them in error. There was no explanation provided as to reason for message. | In Progress | No
467 | 747-400 - The 41-downlink salute | NOPAC | Air | The same CPDLC Position Report was repeatedly down linked 41 times over about five hours, at an interval of three minutes or thirteen minutes. It is suspected that the ACARS MU was at fault. The brand installed on that aircraft is known for sending duplicate downlinks. (Though, this case was extreme). | OPEN | No
468 | A340 - Loss of ADS | SOPAC | Air | Despite several attempts, ATC was unable to establish an ADS contract with the airplane. This issue is corrected with the FANS A+ standard. | CLOSED | No

## Slide 15: New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
469 | ADS Emerg ACT without crew selection | SOPAC | Ground | ATS automation indicates to controller that ADS is in emergency mode when the aircraft is not reporting ADS Emergency. | OPEN | No
470 | 777 BP '03 Unable to datalink over satcom | SOPAC NOPAC NAT | Air | The anomaly occurs as the aircraft flies out of range of a VHF station. When the airplane loses contact with a VHF station, the DCMF attempts to contact another VHF station by transmitting a Link Test downlink. If an application downlink (e.g., a downlink from the FMC or Flight Deck Comm Function) is initiated at very near the same time as the link test, this anomaly can occur. The DCMF does not direct the downlink to SATCOM for transmission. Due to the structure of some routes, an ADS periodic downlink report is often due at approximately the same time as the airplane flies out of VHF range. This is the reason that the anomaly may appear to be route-specific. This problem will be corrected in BP '05. | To be closed when BP05 certified | Yes
471 | Transfer failure due to ground station fault | SOPAC | Ground | Autotransfers sometimes do not occur due to a software fault in the ground automation. | OPEN | No
472 | KC-135s send the occasional empty message | SOPAC | Air | KC-135s send the occasional empty message (header and CRC only, but no actual message). | OPEN | No

## Slide 16: New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
473 | Failure to forward media advisories | SOPAC | Ground | Between 31 Oct and 9 Nov ARINC were not forwarding the media advisories. As a result, SITA was unable to deliver uplinks to some airplanes. The problem has been corrected. | CLOSED | No
474 | Duplicate downlinks from two 747-400s | SOPAC | Air | 3 copies of a waypoint change event report were received from one airplane, and 3 copies of a periodic report were received from another. | In Progress | No
475 | Delayed CPDLC downlink | SOPAC | Ground | Per the reporting individual, "ADS-C reports were received OK, but CPDLC downlink was delayed by approximately 7 minutes, resulting in the inability to assign a change of level to a crossing aircraft". Per the analysis, it appeared that there may have been a short period of satcom no comm, and the preceding uplink was the message that was delayed. | CLOSED | No

## Slide 17: New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
476 | Service Advisory | SOPAC | Ground | An ATSU reported comm difficulties with a particular aircraft. Analysis revealed that there appeared to have been a problem with the GES. This event highlighted the need to receive service advisory from both DSPs. | OPEN | No
477 | Offsets vs Weather deviations | SOPAC | Air | Flight crews occasionally request offsets (fixed distance) when they really want a weather deviation (variable distance). This results in increased workload for the controllers | OPEN | Yes
478 | 747-400 - Downlink Error indication immediately after selecting send | SOPAC | Air | An ATSU reported being unable to get a CPDLC downlink from a particular airplane. The pilot reported that they were getting a 'downlink error" about 5 seconds after sending the position report. Selecting ATC Comm Off and logging on again corrected the problem. | OPEN | No
479 | NEXT DATA AUTHORITY YBBB | SOPAC | Ground | A flight crew reported receiving an uplink: "Next data Authority XXXX". This is a known software fault at the ATSU. | OPEN | No

## Slide 18: New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
480 | 737 - CPDLC half-connected after in-air FMC restart | test | Air | If a CPDLC connection exists and the FMC subsequently goes through a restart, the connection is retained internally, but the CDU pages act as if no connection exists. The flight crew can re-connect and receive uplinks, but cannot send downlinks. | OPEN | No
481 | Difficulty with "Descend to Reach by Time" clearance | SOPAC | Air | A flight crew was issued a clearance to Descend to reach F360 by time 2029'. The flight crew apparently missed the "by time" aspect of the clearance, so were descending too slowly. | OPEN | Yes
482 | Early transfers causing logon rejections | SOPAC | Ground | For a brief period of time, one ATSU reported receiving a large number of (very) early logons. This resulted in logon rejections. | CLOSED | No
483 | 737 downlinked "insufficient data" error in response to valid AFFIRM uplink | SOPAC | Air | 737 downlinked "insufficient data" error in response to valid AFFIRM uplink | In Progress | No

## Slide 19: New Problem Report Summary (cont’d)
PR | Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT
484 | 777 dropped ADS waypoint change event contracts | NAT | Air | FMC appears to ignore an ADS event contract request which arrives very close to an AFN Acknowledgement. | In Progress | No
485 | KC-135 dropped ADS waypoint change event contracts | NAT | Air | Appears to be similar symptoms to 777 in PR485 | In Progress | No
486 | 747 classic doesn’t report altitude at reported waypoint | NOPAC SOPAC | Air/ground | The FMC on this airplane does not provide reported waypoint altitude or predicted data for the ADS predicted route group. | In Progress | Yes
? | Bad timestamp | SOPAC | Air | Military airplane provided a message with a time stamp about 5 seconds ahead of UC | In Progress | No
? | UNABLE response rejected | SOPAC | Air | A military airplane responded to an UNABLE uplink by rejecting it. | In Progress | No

## Slide 20: Specific Reports for Discussion
458 767 encoded 60 minutes in [minuteslatitudelongitude] variable
  Minutes in latitude/longitude encoded as 60.0
  Should be 0.0 to 59.9
463 777 - Position encoding difficulties
  Similar to PR331 (for position reports)
  Old or missing data for [position] in other reports
  Corrected in BP05
464 767 sent altitude request with garbage free text appended
  Free text consisting of unprintable characters and the destination appended to climb request
  2 reports of this

## Slide 21: Specific Reports for Discussion (cont’d)
470 777 BP '03 Unable to datalink over satcom
Occurs as airplane flies out of range of a VHF station
When contact with a VHF station is lost, DCMF attempts to contact another VHF station by transmitting a Link Test (q0) downlink
If an application downlink is initiated at very near the same time as the link test, this anomaly can occur
  DCMF does not direct the downlink to SATCOM
Due to the structure of some routes, an ADS downlink report is often due at about the time the airplane flies out of VHF range
  This is why the anomaly may appear to be route-specific.
This anomalous condition can be corrected by a maintenance procedure accomplished on the ground
  If this procedure is not accomplished the anomaly will persist through subsequent flights.
This problem was corrected for AIMS-1 aircraft in BP03C, and will be corrected in BP '05 for AIMS-2 aircraft.

## Slide 22: Specific Reports for Discussion (cont’d)
477 Offsets vs Weather deviations
  Flight crews occasionally request offsets (fixed distance) when they really want a weather deviation (variable distance).
  This results in increased workload for the controllers.
481 Difficulty with "Descend to Reach by Time" clearance
  A flight crew was issued a clearance to Descend to reach F360 by time 2029'.
  The flight crew apparently missed the "by time" aspect of the clearance, so were descending too slowly.

## Slide 23: Specific Reports for Discussion (cont’d)
486 747 classic doesn’t report altitude at reported waypoint
  PMS on 747 classic is “advisory-only” for performance data
    Altitude at “FROM” waypoint is not available
    Predictions not approved other than as “advisory”
  Position reports do not contain reported waypoint altitude or next waypoint data
  This data is optional (per DO-219)
  ADS predicted route group also omits this data
    Non-compliance notification
  ATSUs have objected to the missing data

## Slide 24: SATCOM Issue
Addition of MTSAT-1R adds a fifth satellite to the ORT (Owner Requirements Table)
On some Rockwell-Collins SDUs, this can cause continuous system resets
  Use of un-initialized memory
  Requires new ORT creation tool
See SIL 05-1 for SDU-906