## Slide 1: JCAB CRA Problem Report Activity Since IPACG/22
IPACG/23 FIT/10
Tokyo, Japan
11-12 July, 2005
Attachment 2

## Slide 2: JCAB CRA Activity Since FIT/10
Problem Reports Proposed for Closure
  To be closed at IPACG/23
New Problem Reports
  Specific Reports

## Slide 3: Lesson Learned PRs at IPACG FIT/10
Consultation with | Title | Rationale | PR
 |  |  | Number
DSP/GES | Incorrect position displayed of an aircraft | Concerning the air/ground data link | 10,363
Operator | Confirmation of ADS-EMG | Cockpit procedure | 10,329
 | Position reports with incorrect | Cockpit procedure | 10,338
 | latitudinal/longitudinal |  | 
 | representation |  | 
 | Resequencing at Weather Deviation | Cockpit procedure | 10,358
 | Position report | Cockpit procedure | 10,346
 | CPDLC position report |  | 10,351
 | without altitude information |  | 10,352
 |  |  | 10,353
 |  |  | 10,355
 | Unable to log on | Cockpit procedure | 10,366
Notes: Chart7ですが、
こちらは、プロシジュアに起因するプロブレムレポートで、１４件発生しました。
内訳は
・ multi-blockメッセージに関するレポートが３件
・ 逸脱に関するレポートが１件
・ ADS-EMGに関するレポートが１件
・ CPDLC POSITION REPORTに設定される緯度／経度情報の形式に関するレポートが６件
・ CPDLCのリクエストに関するレポートが１件
・ ログオンに関するレポートが２件
です。

## Slide 4: Dialog in Confirmation of ADS-EMG
PR Title: Dialog in confirmation of ADS-EMG
PR Number: 10329
PR Status: Lesson Learned
ADS-EMG was downlinked.
The controller took an action based on the FANS1/A Operations Manual (FOM).
In response to the controller’s inquiry, the pilot did not reply with the message prescribed in FOM, instead downlinked “ROGER” and “ADS ARM. SPEED .845”.
Pilot training is required.

## Slide 5: CPDLC position report with ARINC 424 fix names of latitude/longitude
PR Title: Position report with ARINC 424 fix names
PR Number: 10338
PR Status: Lesson Learned
A CPDLC position report was downlinked in the form of five figures of latitude/longitude (ARINC 424 fix names). Although the pilot was asked to downlink the position report in ICAO form of latitude/longitude, the report was downlinked again in the five figures representation.
Pilots are required to change ARINC format to ICAO form according to FANS1/A Operations Manual.
Pilot training is required.
ARINC 424 fix names: 35E60 35N160E
Notes: PR10233, 10292, 10293, 10300, 10301, 10305
CPDLC Position reportの位置情報がARINC 424fix names 形式でダウンリンクされました。 ARINC 424fix names 形式とは、例えば、３５Ｎ１６０Ｅを３５Ｅ６０というように表現します。
管制官が通常の、７桁から１１桁の形式でダウンリンクするように伝えましたが、緯経度情報は指定された形式でダウンリンクされませんでした。
FANS1/A Operations Manualには通常の形式でダウンリンクするよう記載されています。
またATSUエンドシステムはARINC 424fix names 形式に対応していません。
参考
FIT-8: DAL(10204,10208):未連絡 CAL(10209):連絡済み CPA(10213):連絡済み
KAL(10223):連絡済み、社内では使用禁止
FIT-9予定：DAL(10233), CPA(10305), KAL(10293), NWA(10292,300,301): 全て未連絡
DAL:DELTA AIR LINES CAL: CHINA AIRLINES CPA: CATHAY PACIFIC
KAL: KOREAN AIR NWA: NORTHWEST AIRLINES

## Slide 6: Position report
PR Title: Position report
PR Number: 10346
PR Status: Lesson Learned
An ATSU reported about an aircraft that in response to its request of a CPDLC position report, the pilot down linked the [IS YOUR ADS INOPERATIVE]
According to a communication log recorded at the ATSU, the aircraft was sending its position reports via ADS. The ATSU requested the aircraft several times to send CPDLC position report because it had not received any CPDLC position reports from the aircraft.
In the FIR under the service of the ATSU, flight crew is requested to send CPDLC position report in addition to send ADS report. The flight crew seems to have understood that there was no need to send the CPDLC position report while sending ADS report.
The operator should confirm the rule that aircraft are requested to make position report with CPDLC in addition to ADS in this FIR.

## Slide 7: CPDLC position report without altitude information
PR Title: CPDLC position report without altitude information
PR Number: 10351, 10352, 10353, 10355
PR Status: Lesson Learned
An ATSU reported about some aircraft which were recently retrofitted with FANS equipment, that the altitude information in the reported waypoint information part of the CPDLC position report downlinked from the aircraft was not displayed on the ATC screen, and that the ATSU received a NCN (Noncompliance Notification: meaning that the aircraft was unable to comply with the request to provide its altitude information at the Next and Next+1 Fixes) in response to the up linked ADS Periodic/Event CONTRACT request.
The ATC operation needs the altitude information in the waypoint report, in general.
This event was resulted from the detailed specification of the FANS software.

## Slide 8
PR10351
3602N14430.5E 19:45 FL330 COMFE 19:53 DRIVR 04:07
-34C 260/159 M0.83 ABETS 19:44 FL330
An image of CPDLC position report
The fix where SEND button depressed, Time stamp, Flight level
Next waypoint, ETA
Next+1 waypoint
Reported waypoint, ATO, Flight level
Missing!

## Slide 9
Deviation Flight caused abnormal display of flight path
PR Title: Abnormal display of an ADS aircraft on ATC screen
PR Number: 10358
PR Status: Lesson Learned
An ADS aircraft was depicted on the ATC display, as if it were flying in a direction opposite to its real route.
The aircraft seemed to have flown in heading select.
The type of avionics on board the aircraft cannot recognize passing a waypoint if the aircraft is more than 21 miles off track on passing the waypoint. In this event the aircraft made 40 NM deviation could not recognize passing the waypoint. Therefore, even after it passed the waypoint, the point was still designated as the PRED.ROUTE/NEXT and the FIXED INT in the ADS Reports.
Pilots are required to apply re-sequence in this case.

## Slide 10
Weather
Planned Route
fix-a
Heading Select
21/7 NM
PR10358
Target symbol
Displayed on ATC Screen
Real flight
Notes: An aircraft position gained with ADS report was depicted on the ATC display, as if it were flying in a direction opposite to its real route.
The aircraft seemed to have flown in heading select.
The type of avionics on board the aircraft cannot recognize passing abeam a waypoint if the aircraft is more than 21 miles off track. Therefore, even after it passed the waypoint, the point was still designated as the PRED.ROUTE/NEXT and the FIXED INT in the ADS Reports.
Then the aircraft appears, on ATC display, flying back toward the waypoint that has already passed.
However, the aircraft is actually flying to the next waypoint as shown on the slide.
Note: Operators shall develop appropriate airborne procedures to ensure correct waypoint sequencing.

## Slide 11: Incorrect position displayed of an aircraft on ATC screen
PR Title: Incorrect position displayed of an aircraft
PR Number: 10363
PR Status: Lesson Learned
An ATSU reported about an ADS capable aircraft displayed on the ATC screen that its current position reverted to a previous position.
The ATSU End system displayed the data of the two reports in order of their arrival that the current position of the aircraft was displayed as if it had reverted to an old position.
This sort of sequencing problem could occur from a timing difference in data link communication.

## Slide 12
VHF Coverage
PR10363
Real Flight
Display on ATC Screen
Target Symbol

## Slide 13
PR Title: Unable to logon
PR Number: 10366
PR Status: Lesson Learned
An operator reported that an aircraft failed to logon.
According to the flight plan submitted by the operator, the aircraft was not to fly in the airspace datalink communication available.
The ATS End system of the ATSU is designed not to accept any logon attempt from aircraft that is not planned to fly in the datalink communication applied airspace.
The operator is requested to reconfirm the ATS data link operational airspace.
Unable to logon

## Slide 14: New Problem Reports
  Categories of Problem Reports
  - Of the 47 Problem Reports;
  ADS 5
  CPDLC 17
  Connection 3
  Datalink, General 22
  Summary
  Specific Reports

## Slide 15: New Problem Reports (1)
(1) ADS problem |  |  |  |  |  | 
PR # | Problem Report Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT?
10,345 | Delayed down link message | NOPAC | Air Ground | After entering the domestic airspace the aircraft continued to down link ADS reports. | Open | YES
10,358 | Incorrect position display with ADS | NOPAC | Air | An ADS capable aircraft was indicated on the ATC screen, as if it had been moving in the opposite direction of its real flight. | Lesson | YES
10362 | Differences in awareness about the aircraft position between air and ground systems | NOPAC | Ground | The flight path of the aircraft was to going through the Pred. Route (Next), by way of the Pred. Route (Next+1) toward the Fixed Intent point. Since the ATSU End system does not use Pred. Route (Next+1) and the Intermediate Intent , the aircraft was displayed as if it had been flying from the Pred. Route (Next) directly toward the Fixed Intent point. | Open | YES
10363 | Incorrect position displayed of an aircraft | NOPAC | Air | ADS Waypoint Event Reports down linked from the aircraft, and arrived at the ATSU End system in reverse order from their occurrence. | Lesson | YES

## Slide 16: New Problem Reports (2)
(2) CPDLC problem(1/2) |  |  |  |  |  | 
PR # | Problem Report Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT?
10337 | The use of FREE TEXT [DISTRESS] (DL68) | NOPAC CENPAC | Air | An aircraft requested to deviate from its planned route by means of a FREE TEXT [DISTRESS] (DL68) message. | Open | Yes
10338 | Incorrect latitude and longitude representation in a CPDLC Position Report | NOPAC | Air | The latitude and longitude of fixes in a CPDLC Position Report were described in the form of ARINC 424 fix names (5 figures) | Lesson | Yes
10340 10343 10354 10360 | A position report including an incomprehensible character | NOPAC CENPAC | Air | An aircraft down linked a CPDLC position report ,which was displayed on the CPDLC screen, included an incomprehensible character. | Waiting | Yes
10346 | Position report | NOPAC | Air | An ATSU reported about an aircraft that in response to its request of a CPDLC position report, the pilot down linked [IS YOUR ADS INOPERATIVE]. | Lesson | Yes
10347 | Unable to establish a CPDLC connection | NOPAC | Air | An ATSU reported about an aircraft that while its down link messages successfully reached the ATSU, up link from the ATSU was unsuccessful. | Waiting | Yes

## Slide 17: New Problem Reports (3)
CPDLC problem(2/2) |  |  |  |  |  | 
PR # | Problem Report Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT?
10348 | A CPDLC position report repeatedly down linked | CENPAC | Air | An aircraft down linked more than one CPDLC position reports about a Waypoint | Waiting | Yes
10350 | Message transmission delay and NO ACK occurred | NOPAC | Air | The ATSU up linked a CPDLC CONTACT message, to which the aircraft did not respond with a WILCO. In response to the ATSU's inquiry , the flight crew replied with "we did not receive the CONTACT message". | Waiting | Yes
10351 10352 10353 10355 | CPDLC position report without altitude information | NOPAC CENPAC | Air | The altitude information was not set in the reported waypoint information part of the CPDLC position report. | Lesson | Yes
10356 | Re-logon after the termination of a CPDLC connection | NOPAC | Air | Communication with the aircraft was conducted through SATCOM and for a certain period of time no down link messages delivered to the ATSU. | Open | Yes
10365 | CPDLS downlink message delay | NOPAC CENPAC | Air | A CPDLC message was doubly delibered. The duplicate one was about two hours late. | Waiting | No

## Slide 18: New Problem Reports (4)
(3) Connection/Transfer Problem |  |  |  |  |  | 
PR # | Problem Report Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT?
10326 10332 | Unable to Logon | NOPAC CENPAC | Air | Two different Tail Numbers were set in a down linked message. | Open | Yes
10366 | A Logon from Non-datalink-service airspace | NOPAC CENPAC | Air | A Logon was conducted from the airspace where data link service was unavailable. | Lesson | Yes

## Slide 19: New Problem Reports (5)
(4) Datalink, General Problem(1/2) |  |  |  |  |  | 
PR # | Problem Report Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT?
10322 10324 10325 10327 10330 10333 10341 10342 | Message transmission delay and NO ACK occurred | NOPAC CENPAC | Air Ground | An ATSU reported about an aircraft that its down link message was delayed and NO ACK occurred in response to up linked messages. | Open | Yes
10323 | Message transmission delay and NO ACK occurred | CENPAC | Ground | An ATSU reported about an aircraft that NO ACK occurred in response to up linked messages and that a Logon attempt conducted by the aircraft was unsuccessful. | Open | Yes
10328 | Data link in trouble | NOPAC | Air Ground | An ATSU could not receive a position report from an aircraft and when it requested for the report, the aircraft replied with a message to the effect that it already down linked the report. | Open | Yes

## Slide 20: New Problem Reports (6)
Datalink, General Problem(2/2) |  |  |  |  |  | 
PR # | Problem Report Title | Region | Air or Ground | Comments/Notes/Description | Status | Discuss at FIT?
10334 | Unrecognized Message Reference Number | NOPAC | Air | An ATSU up linked a message of approval to a climb request, to which the aircraft down linked an UNRECOGNIZED MSG REFERNCE NUMBER. | Open | Yes
10344 10359 10367 | Delayed message | NOPAC CENPAC | Air | Afre an aircraft got out of the FIR, its ADS report was down linked about eight hours late and displayed on the ATC screen. | Waiting | Yes
10349 10357 10364 | Message transmission delay and NO ACK occurred | NOPAC CENPAC | Air | An ATSU reported about an aircraft that its down link message was delayed and NO ACK occurred in response to up linked messages. | Open | Yes

## Slide 21: Specific PRs (1)

## Slide 22: Delayed downlink message
PR Title: Delayed downlink message
PR Number: 10345
PR Status: Open
An ATSU reported about an aircraft that after it came into the domestic airspace from the oceanic airspace it continued to downlink ADS reports.
According to a communication log recorded at the ATSU, the ATSU End system up linked a CTC to disconnect the ADS connection and waited for a DIS to be downlinked. But the aircraft downlinked an ADS event report of a flight level change event and the ATSU End system automatically uplinked an event request. After that, the ATSU End system received the DIS and terminated the ADS connection, but even after the aircraft entered the domestic airspace it continued to downlink ADS reports.
This sort of event can rarely occur out of timing difference between message transmission and reception in the current air/ground data link communication technology.
An operational procedure is required to mitigate the impact to ATC operation.

## Slide 23
Domestic Area
Oceanic Area
PR10345
ATSU
CTC
Event
report
DIS
Event
Request
Connection Established
Connection Terminated
Event
report
Connection Terminated

## Slide 24: Incorrect position displayed of an aircraft on ATC screen
PR Title: Differences in awareness about the aircraft position between air and ground systems
PR Number: 10362
PR Status: Open
An aircraft operator reported that while one of its aircraft was flying, the ATSU informed the flight has deviated 20 NM off the track and after the crew checked its FMC they learned the flight was on track and course.
The last ADS report down linked just before the detection of the deviation was an ADS Periodic report containing the following data: the reported point = a preceding point of the fix-2; next waypoint = fix-2; next+1waypoint = fix-3; Fixed Intent = near the fix-4.
Since the ATSU End system does not use the data of Pred. Route (Next+1) and the Intermediate Intent included in the ADS Periodic report for the purpose of displaying aircraft position, the aircraft was displayed on the ATC screen as if it had been flying from the Pred. Route (Next) directly toward the Fixed Intent point.

## Slide 25
PR10362
fix-3
fix-4
fix-2
fix-1
20NM
Fixed intent
Route 1
Route 2
Next Waypoint
Next +1
Waypoint
:Real Flight
: Target Symbol
ATC:
Confirm you are deviating 20NM
Pilot: Negative, we are on course

## Slide 26: The use of FREE TEXT [DISTRESS] (DL68)
PR Title: The use of FREE TEXT [DISTRESS] (DL68)
PR Number: 10337
PR Status: Open
An ATSU reported about an aircraft that it requested to deviate from its planned route by means of a FREE TEXT [DISTRESS] (DL68) message. Receiving the message, the ATSU End system (based on its design) displayed the message in red color and put a character [E] on the electronic strip to indicate an EMERGENCY condition. The controller raised a question as to the use of the message.

## Slide 27: A position report including an incomprehensible character
PR Title: A position report including an incomprehensible character
PR Number: 10340, 10343, 10354, 10360
PR Status: Waiting for Info.
An ATSU reported that ATC system rejected CPDLC position report as DECODE ERROR.
With an analysis, an incomprehensible character was detected in the message.
In these cases, the ATSU End system applied the CRC check, but found nothing wrong with it, so that, there is a possibility that the avionics set the character in the report.

## Slide 28
PR10354
ATSU
DSP-X
AT1.aaaaaaa60012?049106EC8
Tail number: aaaaaaa
DSP-Y
AT1.aaaaaaa60012?1049106EC8
ERROR

## Slide 29: Unable to establish a CPDLC connection
PR Title: Unable to establish a CPDLC connection
PR Number: 10347
PR Status: Waiting for Info.
An ATSU reported about an aircraft that while its downlink messages successfully reached the ATSU, uplink from the ATSU was unsuccessful.
According to an ATSU’s log, the ATSU had successfully established a CPDLC connection with the aircraft. But in response to a FN_CON downlinked again, it sent a FN_AK. After that, the ATSU sent a CR, but it received a DR just after it sent the CR, resulting in unsuccessful CPDLC connection.
According to a DSP log, the time stamp in DR given by FMC was earlier than that of FN_CON. In view of the message sequence number of those messages downlinked, ACARS-MU downlinked the FN_CON first and then the DR.
The reason of this reversion of message sequence between FMC and ACARS-MU would be followed up by aircraft manufacturer.

## Slide 30
FMC | 
DSP |  | 
ATSU | RECEIVED | 
 | SENT | 
ACARS-MU | 
Connection Failure
Connection Established
Downlinked in reverse sequence
FN_CON
DR
FN_AK
CR
CC
DR
FN_CON
DR
FN_CON
CC
FN_CON
DR
CC
FN_AK
CR
CC
PR10347

## Slide 31: A CPDLC position report repeatedly downlinked
PR Title: A CPDLC position report repeatedly downlinked
PR Number: 10348
PR Status: Waiting for Info.
An aircraft downlinked several CPDLC position reports about a Waypoint, but with a different time stamp and current position data included in each report.
Each of the consecutively down linked CPDLC position reports has a different MIN (Message Identification Number). It is guessed that a total of seven CPDLC position reports were downlinked.
The aircraft manufacturer is expected to follow up this event.

## Slide 32: Message transmission delay and NO ACK occurred
PR Title: Message transmission delay and NO ACK occurred
PR Number: 10350
PR Status: Open
An ATSU reported about an aircraft that when the aircraft came into the domestic airspace from the oceanic airspace the ATSU uplinked a CPDLC CONTACT message, to which the aircraft did not respond with a WILCO. The flight crew replied that they did not receive the CONTACT message.
The CONTACT message had reached the aircraft because the ATSU End system received a MAS in response to the CONTACT. The loss of the CONTACT, therefore, is considered to be resulted from some problem with the Avionics of the aircraft.
With further review, it was found that the same events occurred in the same type of aircraft purchased simultaneously by the same aircraft operator.
The event was reported to the aircraft operator.

## Slide 33: Re-logon after the termination of a CPDLC connection
PR Title: Re-logon after the termination of a CPDLC connection
PR Number: 10356
PR Status: Open
An ATSU reported about an aircraft that when the aircraft was going out of the FIR the ATSU terminated the CPDLC connection with it and subsequently the ATSU received a Logon downlinked again from the aircraft.
According to a communication log of the ATSU and a DSP, the communication with the aircraft was conducted through SATCOM and from a certain time of the log there were no downlink messages delivered to the ATSU. After that, just before the FIR boundary, several past messages were downlinked.
Examining the time stamps of those DR and FN_CON, it was learned that the messages were accumulated messages which should have been down linked within the FIR. The Re-logon is thought to be resulted from the message accumulation with the avionics.
The aircraft manufacturer is expected to follow up this event.

## Slide 34
D/L
D/L
D/L
D/L
DR
FN_CON
CONTACT+EOS
ATSU
AIRCRAFT
Accumulated message
FIR boundary
Time
PR10356

## Slide 35: Unable to Logon
PR Title: Unable to Logon
PR Number: 10326,10332
PR Status: Lesson learned
An ATSU reported that an aircraft operator informed the ATSU that more than one aircraft could not get CPDLC connection, but the ATSU found no trace of Logon attempts by those aircraft.
According to a log of ATSU, it was learned that, for each unsuccessful Logon, the Tail Number in a FN_CON did not agree with the Tail Number filled in the flight plan. That was the reason why the ATSU End system uplinked a FN_AK (Reason code =4).
Pilot training is required.

## Slide 36
ATSU
End system
Tail number : 12345A
Callsign: ZZZ12345
FN_CON
Tail number : 12345
Callsign: ZZZ12345
With wrong Tail Number
ATC system is
unable to process FN_CON
Flight Plan
Tail number : 12345A
Callsign: ZZZ12345
PR10332
Aircraft
operator

## Slide 37
PR Title: Message transmission delay and NO ACK occurred
PR Number: 10322, 10324, 10325, 10327, 10330, 10333, 10341, 10342
PR Status: Open
An ATSU reported about an aircraft that its downlink message was delayed and NO ACK occurred in response to uplinked messages and that the controller switched the communication with the aircraft to voice communication.
According to a communication log recorded in the DSP-X, which was connected with the ATSU, communication with the aircraft was conducted via VHF datalink at that time. During a period of time, the following events were found:
When the DSP-X transferred a message to DSP-Y to uplink it via SATCOM, the DSP-Y sent a MAF=231(UP INTERCEPT NO STATION TO) back to the DSP-X. After a while, the DSP-X received a MED message from DSP-Y telling there was only SATCOM datalink available to communicate with the aircraft. After that, in response to an up link message transferred from the DSP-X, the DSP-Y returned a MAF=311(NO ACK) to the DSP-X.
Message transmission delay and NO ACK occurred

## Slide 38: MAS=X
PR Title: No acknowledgement received in data link message transmission
PR Number: 10323
PR Status: Open
According to the communication log recorded at the DSP-X that was communicating with the airplane via VHF data link, the DSP-X had received a MED sent from the DSP-Y, indicating the airplane was reachable via either VHF or SATCOM. In response to a FN_CON down linked from the airplane the DSP-X attempted to up link a FN_AK, but failed and transferred the message to the DSP-Y. The DSP-Y did not up link the message but returned a MAS=X instead, which made the DSP-X determine No Acknowledgement received within a specified time limit.
This event has been identified to be the interface problem between DSPs, which are recognized by them.

## Slide 39
PR Title: Data link in trouble
PR Number: 10328
PR Status: Waiting
ATSU-X reported that it could not receive a position report from the aircraft and when it requested for the report, the aircraft made a reply to the effect that it already down linked the report. ATSU-X could not find the message in its End system.
Due to lack of appropriate DSP log, further investigation could not be performed.
Data link in trouble

## Slide 40
PR Title: UNRECOGNIZED MESSAGE REFERENCE NUMBER
PR Number: 10334
PR Status: Waiting for info.
In response to an request from aircraft, ATSU uplinked STANDBY about eight minutes later. Then ATSU uplinked ATC clearance.
In response, the aircraft down linked an UNRECOGNIZED MSG REFERENCE NUMBER.
From the analysis result of the DSP logs, it seems that there were not any problems on SATCOM communication.
Further investigation required inviting aircraft manufacturer.
UNRECOGNIZED MESSAGE REFERENCE NUMBER

## Slide 41
PR Title: Datalink malfunction
PR Number: 10344, 10359,10367
PR Status: Open
An ATSU reported about an aircraft that, the old ADS message of about eight hours before was downlinked.
The aircraft was displayed on the Traffic situation display. The ATSU switched over to voice communication in the middle of the communication with the aircraft.
The ATSU end system is designed that an ADS report without flight plan is displayed for a short period to allow controllers to confirm the situation.
It has been known that the airplanes were furnished with the kind of ACARS MU that, conceivably, have a problem in sending messages from the FMS at certain condition.
Data delay

## Slide 42
PR10344
ADS report
ATSU-A
DSP-X
VHF coverage
DSP-Y
VHF coverage
ADS report
ADS report
ADS report
ADS report
FIR-A
FIR-B

## Slide 43
PR Title: Message transmission delay and NO ACK occurred
PR Number: 10349, 10357, 10364
PR Status: Waiting
An ATSU reported about an aircraft that its down link message was delayed and NO ACK occurred in response to up linked messages and that the controller switched the communication with the aircraft to voice communication.
February 2005 : 11
March 2005 : 22
April 2005 : 24
Message transmission delay and NO ACK occurred

## Slide 44: Questions?