## Slide 1: ADS PROBLEMS THAT AFFECT ATC SERVICES WITH DISTANCE BASED SEPARATION
Presented by JCAB CRA
January 2005 Los Angeles USA

## Slide 2: 1. Introduction
At FIT/8 meeting, the Co-chair asked if specific problems, which are considered to affect the application of distance-based separation minima using ADS/CPDLC, have been received or identified.
The application of distance based separation in the oceanic ATC services requires ADS for surveillance and CPDLC for the direct communication between pilots and controllers.

## Slide 3: 2. Requirements to use ADS for surveillance
Reliable aircraft position information available with Basic and Prediction data.
Timeliness of the aircraft positions updated and displayed on ATC screen.

## Slide 4: 3. Problem Reports affecting distance based ATC operation
3.1 The following events are caused by the incorrect prediction data in the ADS report.
Deviation: Heading select;
In this situation, the prediction data in ADS report depends on the flight planned waypoint, regardless the aircraft position and course actually flying.

## Slide 5
[Event-1]
Despite of continuing deviation from the planned route, the flight path on ATC screen always proceeding back to a waypoint of the flight plan, and incorrect aircraft positions are updated on ATC screen.
[Event-2]
This event always occurs when an aircraft deviates from the planned route with a certain magnitude of miles exceeding the value set at the avionics. (21 NM for Boeing and 7 NM for Airbus aircraft) In this case, though the actual flight path is forwarding to the next waypoint, the aircraft is displayed on ATC screen flying back to the waypoint that has already passed .

## Slide 6
Weather
Original Planed Route
FIX X
Heading Select
FIX Y
FIX Z
Weather
Original Planed Route
FIX X
Heading Select
21NM
[Event-1]
[Event-2]

## Slide 7
[Possible impact on ATC operations ]
The aircraft position and flight path are unreliable and should not be used.
[Countermeasures ]
a. ATC operational procedures:
Controllers should be educated to recognize this situation and to disregard the aircraft position data during the aircraft deviating from the planned route.
b. ATC Systems:
A review of software upgrade on ATC systems is recommended.

## Slide 8
3.2 Missed or delayed ADS report.
The following events are caused by missing or delay of ADS report to arrive at ATC systems.

## Slide 9
[Event-3]
The delivery delay or missing of messages could be occurred with the following situation .
Case-1: Missed ADS report caused by unscheduled
network system stoppage.
Case-2: Missed ADS report caused by unstable
satellite communication.
Case-3: Delay or missing of message caused by
the particular onboard communication unit
with which the aircraft is unable to
communicate via satellite for hours.

## Slide 10
[Possible impact on ATC operations ]
The aircraft which ADS report and/or CPDLC communication are not available will be determined to be an unqualified aircraft for applying distance based separation.
[Countermeasures ]
For the individual aircraft with missing ADS/CPDLC, the contingency procedures for such aircraft should be applied, until such time the ATC established a conventional time separation instead.
For Case-3, the change to airborne system is expected.

## Slide 11
[Event-4]
Capricious ADS reports cause missing, delayed delivery, incomplete contents or multiple forms of message, and, on this occasion, the controllers should take action to obtain the correct aircraft positions by other means.
Case-1: Unstable communication, when aircraft flies near
the fringe of VHF coverage, causes the missing of
aircraft position gained by ADS reports.
Case-2: When the ADS message with incomplete contents
is delivered to ATSU, it is rejected by ATC system.
Case-3: Delayed data processing in avionics causes ADS
report containing unreasonable data.
Case-4: When an unreasonable multiple message with
‘ACK+ADS report+NAK’ in a report is downlinked,
ATC system rejects it

## Slide 12
[Possible impact on ATC operations ]
The accuracy of aircraft position is downgraded or missed, until the correct report received by the ATC system.
[Countermeasures ]
The ATC operational procedures responding to these events are required to develop, such as the procedure to uplink ADS Demand Request for obtaining the position.

## Slide 13: 4. Recommendation
The meeting is requested to note the information in this paper.