## Slide 1: Validation of Applicability of ADS report to Surveillance
Presented by JCAB CRA
January 2005 Los Angeles USA

## Slide 2: Introduction
Tokyo ACC has planned to replace CPDLC-Position Report with ADS-Waypoint Report as the primary means of position reporting associated with aircraft equipped with ATS data link capability flying in the oceanic airspace within the Tokyo FIR.
Validation of Applicability of ADS report to Surveillance
The JCAB CRA decided to investigate the difference between the CPDLC-report (Position Report) and ADS-report (Waypoint Report) for use as the source of position information in the ATC operation.

## Slide 3: Explanation of the CPDLC/ADS
CPDLC-report
IMI : AT1
REG : .JA001G
Time Stamp : 03:00.03
MIN : 16
MRN : -
MSG TYPE : Single
Element No : 048 MSG : POSITION REPORT 3203.5N15956E 03:00 FL340
3616N155E 03:49 CALMA 06:08 -46C 263/94 M0.84 32N160E 02:59 FL340
Next waypoint ETA
Next waypoint
Current waypoint
Current waypoint ATO
ADS-report
Way Point Event Report
Basic ADS 3200N 15959E +34012ft HH:59:22
FOM = 7
Pred.Route(Next ) 3615N 15459E +37996ft Basic ADS Time＋00:49:28
(Next+1) 3937N 15028E +37996ft
Current waypoint
Current waypoint ATO
Next waypoint
Next waypoint ETA information
Validation of Applicability of ADS report to Surveillance

## Slide 4: Method of analysis
Period covered
From March 31 through April 1,2004 (24h)
Surveyed data
ODP system log data
Method of analysis
> To investigate the difference between the number of CPDLC-report and ADS-report,
> To compare CPDLC-report and ADS-report in view of the position information reported are identical,
> When the position information reported is different between the CPDLC-report and ADS-report, investigate the causes of the difference and classify them accordingly,
> To investigate the ratio of identical position information acquired by the ADS-report to position information acquired by the CPDLC-report.
Validation of Applicability of ADS report to Surveillance

## Slide 5
Table-1 The number of CPDLC-report and ADS-report
 | CPDLC-report | ADS-report | Total
Total number of messages | 386 (39.1%) | 601 (60.9%) | 987
Re-sent messages | 12 | 1 | 13
Total number of messages after deducting the number of re-sent messages. | 374 (38.4%) | 600 (61.6%) | 974
The findings (1)
Validation of Applicability of ADS report to Surveillance
Table-2 Ratio of identical/un-identical Waypoint acquired between CPDLC/ADS
 | CPDLC-report | ADS-report
Identical Waypoint | 276 (73.8%) | 276 (46.0%)
Un-identical Waypoint | 97 (25.9%) | 322 (53.7%)
Incorrect messages | 1 (0.3%) | 2 (0.3%)

## Slide 6: The findings (2)
Validation of Applicability of ADS report to Surveillance
Total number of CPDLC-Position Reports = 374 per day
(after deducting the number of re-sent messages)
Number of CPDLC-Position Reports at connection established = 75 (20.1%)
Number of CPDLC-Position Reports over compulsory waypoint = 299 (79.9%)
Number of received CPDLC-Position Reports = 291 (97.3%)
Number of lost CPDLC-Position Reports = 8 (2.7%)
Number of matching to ADS-Waypoint Reports = 276 (96.8%)
Number of un-matching to ADS-Waypoint Reports = 15 (5.2%)
Number of error format reports = 1 (12.5%)
Number of others = 7 (87.5%)
The ratio of acquired ADS-report to necessary CPDLC-report to be down linked
276
299
=
=
92.3%

## Slide 7: Analysis & Discussion (1)
The ratio of acquired ADS-report was 92.3% to the necessary number of CPDLC-report. (Lost 7.7%)
5% of the 7.7% were CPDLC-reports sent from aircraft, to which ADS contracts were unsuccessful.
Validation of Applicability of ADS report to Surveillance
In order for ATSUs to cope with the situation when an unsuccessful ADS contract is detected, they should prepare such procedures as
“depending controller’s judgment retry ADS contract request or request position report.”
Triggered by OVD on ATC display, it is thought to be necessary for controllers to inquire of the pilot as to the ATC waypoint.

## Slide 8: Analysis & Discussion (2)
As far as we investigated ADS-report reported at ATC waypoints, 30% of the Next waypoint data were non-ATC waypoints.
According to the current ATC procedure, controllers are required to check the Next ATC waypoint ETA of the ADS-report down linked at ATC waypoints.
When CPDLC-report are dispensed with, by using ADS-report as the primary means of surveillance, 30% of the ADS-report need complementing in view of the Next ATC waypoint ETA data, by means of CPDLC triggered by controllers or ATC systems (automatically).
Validation of Applicability of ADS report to Surveillance

## Slide 9: Conclusion
This reports one of the necessary verification steps to be taken in evaluating the use of ADS in ATC operations.
Further study and verification activities in various aspects are required in order to extract technical/operational issues to be considered and devise and implement appropriate measures .
Validation of Applicability of ADS report to Surveillance

## Slide 10: Thank you! & Questions?
http://www.crasa.cra-japan.org/
Validation of Applicability of ADS report to Surveillance