## Slide 1: FAA CRA Problem Report Activity Since IPACG-21
IPACG-22/FIT-9
Redondo beach, CA
24/25 January, 2005
Gordon Sandell

## Slide 2: CRA Activity
FAA CRA Activity
New Problem Reports Summary
New Reports Discussion
  Specific Problems
Upcoming software release

## Slide 3: FAA CRA Activity (1)
3 reports from operators
  1 forwarded to CRASA-J
  1 was old problem (PR377, fixed in BP03)
  1 was SATCOM outage
7 reports referred by ATCA-J
  PR 10218 ACARS MU problem
  PR 10229 FMC reset causing odd ADS reports
  PR 10239 ACARS MU retransmitting same report
  PR 10242 ACARS MU problem
  PR 10246 FMC encoding 60 seconds for longitude
  PR 10248 Space in downlink
  PR 10255 FMC stuck sending waypoint change reports

## Slide 4: FAA CRA Activity (2)
Other reports awaiting analysis
  PR 10258
  PR 10260
  PR 10268
  PR 10269
  PR 10278
  PR 10282
  PR 10299
  PR 10313

## Slide 5: New Problem Reports
No reports added to database since last meeting
  PR454 most recent
  Contractual issues (just resolved)
Several problems under investigation
  777 stops sending downlinks
  777 stops sending ADS reports
  Empty Messages
  Dropped Messages on SATCOM
Resolution for KAKES black hole problem

## Slide 6: 777 Stops Sending Downlinks
Airplane doesn’t send downlinks via SATCOM
  Problem duplicated in Boeing Lab
    Problem occurs when downlink attempt coincides with CAT B to CAT A transition
    Problem reported with retrofit (AIMS-1) only, but has been duplicated with AIMS-2
    Problem can be prevented by tuning VHF-C to voice frequency prior to leaving VHF coverage
    Fix under investigation
  Fix will be targeted to BP05

## Slide 7: 777 Stops Sending ADS Reports
Airplane ceases sending reports on one or more connections
  May keep sending on other contracts for a while
Airplane can respond with NACK (“due to congestion”) for contract requests
Seems to be media-independent
Problem reported with AIMS-1 and AIMS-2
Under investigation
  Possibly another version of the previous problem
  Fix will be targeted to BP05 when found

## Slide 8: Empty Messages
KC-135 can send CPDLC messages containing no data
  CRC follows the registration
Problem under investigation by operator and equipment supplier
FIT PR to be written

## Slide 9: Dropped Messages on SATCOM
A340 experienced problems with similar symptoms to 777
Problem under investigation by SITA and airplane manufacturer
FIT PR to be written

## Slide 10: KAKES Black Hole Problem
Affects Aero-H+ and Aero-I
  At the edge of a spot beam, when it transitions to the next spot beam footprint, the SDU does a "relog on"
  This process should only affect the voice channels
  In some cases this "relog on" also affects Data-2, even though it uses the global beam.
Software change applied at Perth GES (Nov 04), but problem still persisting
SITA can provide more details

## Slide 11: 777 Block Point 05
To be certified 4Q05 (AIMS-2), 1Q06 (AIMS-1)
FIT PRs to be fixed:
  287 difficulties establishing CPDLC connection with B777
    BP ’03 fix resulted in null characters in [icaoidentification] variable
    BP ’05 fix correctly encodes active center ID
  331 777 Sends Position Report With Not Enough Bits
    BP ’03 fix corrected Position Report downlink
    BP ’05 fix corrects position encoding in all other applicable downlink elements
  448 777 -Unable to Load Uplinked Route Clearance after WILCO
  449 777 - Flight Number Synchronization Problem