## Slide 1: JCAB CRA Problem Report Activity Since IPACG/21
IPACG/22 FIT/9
California, USA
24-25 January, 2005
Attachment 1

## Slide 2: JCAB CRA Activity Since FIT-8
Proposed Problem Reports for Closure
  To be closed at IPACG/22
New Problem Reports
  Analysis of Specific Reports

## Slide 3: PRs to be closed at IPACG FIT-9

## Slide 4
PR Title: Unsuccessful CPDLC transfer
PR Number: 10081
PR Status: Ready for FIT
During a CPDLC transfer from ATSU-X to ATSU-Y, the airplane could not receive FN_AK uplinked from the ATSU-Y in response to its downlinked FN_CON.
Necessary address setting was missing in a DSP routing table.
Reason for closure
The problem was fixed and it was confirmed with a test that the problem was solved.
Unsuccessful CPDLC transfer
See chart PR10081

## Slide 5: DSP’s Unexpected Service Interruption
PR Title: DWLK delay / UPLK failure
PR Number: 10235, 10240, 10241, 10244, 10245, 10250, 10251, 10252, 10253, 10254, 10256, 10261, 10262, 10263, 10271, 10273, 10277, 10280, 10281, 10285, 10295, 10296, 10309, 10311, 10312
PR Status: Ready for FIT
DSP/GES systems service unavailable.
Notification of these outage were disseminated to the users but reception of the notification by the end users not timely.
Reason for closure
The systems were back on.

## Slide 6
PR Title: Unable to log on
PR Number: 10243
PR Status: Ready for FIT
An ATSU system responded to the downlinked FN_CON with a FN_AK (Reason code=4 : the system does not have the flight plan ).
The flight plan was to be delivered to the ATSU from the originating ATSU.
However it failed to deliver the plan.
At that time, the originating ATSU was under the system conversion process.
Reason for closure
The ATSU managed to manually register the undelivered flight plan.
Undelivered flight plan
See chart PR10243

## Slide 7: Lesson Learned PRs at IPACG FIT-9

## Slide 8: An ADS report with a string of characters of “QTB” appended
PR Title: An ADS report with a string of characters of “QTB” appended
PR Number: 10226, 10227, 10247
PR Status: Lesson Learned
ADS reports were delivered with a string of characters of "QTB" appended to the reports.
When DSPs received a message split and downlinked in multiple parts and did not receive the whole parts within a specific time limit, they would deliver the received parts of the message and append "QTB" to the message, which was in accordance with the DSP’s Specification.
Concerning the air/ground data link communication technology at present, communication failure can happen in rare circumstances. It is almost impossible to prevent the communication failure from happening.
See chart PR10226

## Slide 9: Deviation from the planned route detected
PR Title: Deviation from the planned route detected
PR Number: 10215
PR Status: Lesson Learned
ADS aircraft was displayed with deviating from the planned route. The controller inquired about the next waypoint.
After a while, the aircraft resumed to fly toward the path on the planned route.
According to the investigation of the operator, a wrong waypoint was somehow inserted inadvertently.
See chart PR10215

## Slide 10: Confirmation of ADS-EMG
PR Title: Confirmation of ADS-EMG
PR Number: 10228
PR Status: Lesson Learned
ADS-EMG was downlinked.
The controller took an action based on the FANS1/A Operations Manual (FOM).
In response to the controller’s inquiry, the pilot did not reply with a message prescribed in FOM, instead downlinked “ROGER” and “ADS ARM. SPEED .845”.

## Slide 11: CPDLC position reports with ARINC 424 fix names of latitude/longitude
PR Title: Position reports with ARINC 424 fix names
PR Number: 10233, 10292, 10293, 10300, 10301, 10305
PR Status: Lesson Learned
A CPDLC position report was downlinked in the form of five figures of latitude/longitude (ARINC 424 fix names). Although the pilot was asked to downlink the position report in ICAO form of latitude/longitude, the report was downlinked again in the five figures representation.
Pilots are required to change ARINC format to ICAO form according to FANS1/A Operations Manual.
ARINC 424 fix names: 35E60 35N160E

## Slide 12: CPDLC Request to the next ATSU
PR Title: Inappropriate use of CPDLC
PR Number: 10257
PR Status: Lesson Learned
An aircraft flying in a FIR logged on to next FIR.
The aircraft downlinked a CPDLC message of position report and an altitude change request to next FIR.
The controller of next FIR advised the aircraft to contact current FIR.
See chart PR10257

## Slide 13
PR Title: Unable to logon
PR Number: 10294
PR Status: Lesson Learned
An ATSU reported that an airplane failed to log on.
The airplane was to be transferred from previous ATSU to the ATSU.
The airplane, without having received a NDA from previous ATSU, and without disconnection, attempted to log on to the ATSU.
In response to a CR uplinked from the ATSU, the airplane downlinked a DR.
The aircraft should have disconnected from current ATSU before attempting logging on to the next ATSU.
FOM specifies that pilots should disconnect with current ATSU before logging on to next ATSU.
Double Logon
See chart PR10294

## Slide 14
PR Title: Unable to logon
PR Number: 10319
PR Status: Lesson Learned
An operator reported that an aircraft failed to log on.
According to the flight plan submitted by the operator, the aircraft was not to fly in the airspace datalink communication available.
The ATS End system of the ATSU is designed not to accept any logon attempt from aircraft that is not planned to fly in the datalink communication applied airspace.
Unable to logon

## Slide 15: New Problem Reports
  Categories of Problem Reports
  - Of the 97 Problem Reports;
  ADS 6
  CPDLC 13
  Connection 10
  Datalink, General 68
  (including 25 DSP’s Unexpected Service Interruption)
  Summary
  Specific Reports
  * DSP: Datalink Service Provider

## Slide 16: New Problem Reports (1)

## Slide 17
New Problem Reports (2)

## Slide 18
New Problem Reports (3)

## Slide 19
New Problem Reports (4)

## Slide 20
New Problem Reports (5)

## Slide 21
New Problem Reports (6)

## Slide 22
New Problem Reports (7)

## Slide 23: Specific PRs (1)
FMC Reset (10229)
Unable to up link CPDLC messages due to failure in establishing a CPDLC connection (10236, 10237)
Unable to perform ATC transfer
(10238,10291, 10303)
Incorrect CC (10248)
Switching of satellite (10268, 10269)

## Slide 24: Specific PRs (2)
Deviation Flight caused abnormal display of flight path (10283, 10287, 10308)
ASSIGNED ROUTE Message (10265)
BACK ON ROUTE/BACK ON COUSE? After deviation (10307)
MAS = X
(10232, 10249, 10259, 10264, 10266, 10272, 10276, 10286, 10299, 10310, 10315, 10316)

## Slide 25: FMC Reset
PR Title: Abnormal airplane position displayed
on ATC screen
PR Number: 10229
PR Status: Open
ADS position of an airplane was incorrectly displayed on ATC screen.
The predicted route (Next) of a periodic report downlinked from the airplane was the waypoint , where the airplane had already passed through.
The aircraft manufacturer commented:
It appears that the FMC probably experienced some kind of software reset, resulting in deactivation of flight plan. The flight crew then reactivated the flight plans, and in the reactivation process the FMC probably retained the previous “FROM” waypoint and used that as the “TO” waypoint.

## Slide 26: Unable to up link CPDLC messages due to failure in establishing a CPDLC connection
PR Title: Unable to up link CPDLC messages due to failure in establishing a CPDLC connection
PR Number: 10236, 10237
PR Status: Open
The ATS End system could not get ready for uplinking a CPDLC message to a particular airplane.
The ATS End system received a MAS in response to its uplinked CR, but could not receive a CC (failure in establishing a CPDLC connection).
Analysis made by the aircraft manufacturer is as follows:
Those messages before and after the missing CC were downlinked via SATCOM to the DSP-X. It seemed to be that the airplane was flying near the boundary area of the DSP-Y’s VHF coverage, where it downlinked the CC via VHF to the DSP-Y, but the CC was not delivered to the destination ATSU for some reasons.

## Slide 27
CPDLC Transfer Failure
PR Title: Unable to perform ATC transfer
PR Number: 10238,10291, 10303
PR Status: Open
An aircraft could not establish its CPDLC transfer, when it was entering into FIR-Y from FIR-X.
Usually, the MAS sent from DSP-X has its Flight ID, but the MAS from DSP-Y does not. In this event, the MAS was originated from the DSP-X and via DSP-Y reached the ATSU-Y’s data link system, where the MAS was discarded because the Flight ID information was missing in spite of the MAS being originated in the DSP-X.
Because the ATSU-Y’s End system could not receive MAS in response to its FN_AK, it judged its sending of the FN_AK was unsuccessful and therefore did not send CR.
See chart PR10238

## Slide 28: Incorrect CC
PR Title: Incorrect CC
PR Number: 10248
PR Status: Waiting for Info.
In response to an incorrect CC down linked, the ATS End system up linked an ERROR[UL#159]. Incidentally, the ATS End system subsequently sent CR again and then received a normal CC, which established the CPDLC connection with the airplane.
Investigating a DSP log, it was learned that a space was inserted into the CC message.
According to the aircraft manufacturer, the character in question of the CC appears to have corrupted in the transmission and was replaced with a space. The aircraft manufacturer is continuing to investigate to see if they can determine where in the transmission chain this happened.
See chart PR10248

## Slide 29: Switching of satellite
PR Title: No acknowledgement received in data link message transmission and message transmission delay
PR Number: 10268, 10269
PR Status: Waiting for Info.
Data link communication with the airplane was being conducted via either DSP-X’s VHF or DSP-Y’s SATCOM. DSP-X attempted to up link a message via VHF but failed and transferred it to DSP-Y to be up linked via SATCOM. DSP-Y returned a MAF=231(NO STATION).
SATCOM communication with the airplane was being conducted via either IOR or AOW, but not via POR.
The airplane appears to have had problem in switching between satellites.
See chart PR10268

## Slide 30
Deviation Flight caused abnormal display of flight path
PR Title: Abnormal display of a target ADS aircraft flight
PR Number: 10283, 10287, 10308
PR Status: Open
A target ADS aircraft was depicted on the ATC display, as if it were flying in a direction opposite to its real route.
The aircraft seemed to have flown in heading select.
The type of avionics on board the aircraft cannot recognize passing a waypoint if the aircraft is more than 21 miles off track on passing the waypoint. In this event the aircraft made 40 NM deviation could not recognize passing the waypoint. Therefore, even after it passed the waypoint, the point was still designated as the PRED.ROUTE/NEXT and the FIXED INT in the ADS Reports.
See chart PR10283

## Slide 31
PR Title: All the flight planned route information was downlinked
PR Number: 10265
PR Status: Open
When an airplane returned to its planned route after performing a deviation activity, it down linked an ASSIGNED ROUTE message describing its all the flight planned route information. The behavior, though, poses no problems on the ATC operation, some controllers raised question as to whether it would be necessary for the controller to verify the route information and/or there were some instruction for pilots to do so provided in the operation manual in relation to the avionics’ specification.
ASSIGNED ROUTE Message

## Slide 32
PR Title: Abnormal display of flight path on ATC Screen
PR Number: 10307
PR Status: Open
The airplane’s cleared flight route was FIX1-FIX2-FIX3-FIX4. After passing the FIX1, the airplane requested to deviate due to weather (up to 25NM), got approval of the request and changed its route to FIX2’(NEXT)-FIX3’(NEXT+1), according to its ADS report.
After passing the FIX2’, the airplane down linked a “BACK ON ROUTE” and began to proceed to the FIX3. According to its ADS report, the airplane’s flight route was FIX2’-FIX3-FIX4 at the time.
In response to the controller’s inquiry, the airplane down linked its current position and a message of “NOW BACK ON COURSE”, when it was not flying on the course of originally cleared FIX2 to FIX3, but on the course of FIX2’ to FIX3.
BACK ON ROUTE/BACK ON COUSE? After deviation
See chart PR10307

## Slide 33: MAS=X
PR Title: No acknowledgement received in data link message transmission due to SATCOM outage
PR Number: 10232, 10249, 10259, 10264, 10266, 10272, 10276, 10286, 10299, 10310, 10315, 10316
PR Status: Open
According to the communication log recorded at the DSP-X that was communicating with the airplane via VHF data link, the DSP-X had received a MED sent from the DSP-Y that was serving SATCOM communication, indicating the airplane was reachable via either VHF or SATCOM. In response to a FN_CON down linked from the airplane the DSP-X attempted to up link a FN_AK, but failed and, for the message to be up linked via SATCOM, transferred the message to the DSP-Y. The DSP-Y did not up link the message but returned a MAS=X instead, which made the DSP-X determine No Acknowledgement received within a specified time limit in response to its up link attempt.
After a while, communication via SATCOM with the airplane was performed normally.
See chart PR10232

## Slide 34: Questions?

## Slide 35
PR10081
DSP-X
DSP-Y
ATSU-X
ATSU-Y
FN_AK DELETED
FN_CON
FN_AK

## Slide 36
PR10243
ATSU-Y
Flight plan
ATSU-X
no
Flight plan
FN_CON
FN_AK
No Flight plan
GES-X

## Slide 37
PR10226
DSP
Block1
Block1
Block2
ATSU
Block1+”QTB”
TIMER RUNOUT

## Slide 38
PR10,215
Flight Plan Route
Fix-X
Fix-Y
Fix-Y’
Fix-Z
CONFIRM NEXT WAYPOINT ETA
ATSU

## Slide 39
PR10257
FIR-X
FIR-Y
ATSU-Y
CPDLC
REQUEST CLIMB TO FL380
CPDLC
REQ TO ATSU-X
FIR BOUNDARY
32 min.
ATSU-X

## Slide 40
PR10294
FIR-X
FIR-Y
ATSU-X
FIR BOUNDARY
Try to logon to ATSU-Y
Logged on to
ATSU-X
ATSU-Y
NDA
CONNECTION FAILURE
CONNECTION FAILURE

## Slide 41
ATSU
DSP-X
DSP-Y
AIRCRAFT
FN_CON
FN_CON
FN_CON
FN_AK
FN_AK
FN_AK
MAS
DSP-Y FORMAT
MAS
DSP-Y FORMAT
MAS
DSP-X FORMAT
SENT FROM DSP-Y
MAS
DSP-X FORMAT
SENT FROM DSP-Y
FN_AK
FN_AK
UPLINK FAILURE
PR10238

## Slide 42
PR10248
ATSU
DSP-X
CC1.aaaaaaa60012 1049106EC8
Tail number: aaaaaaa
DSP-Y
CC1.aaaaaaa60012?1049106EC8
ERROR

## Slide 43
PR10268
AOW
VHF
IOR
ATSU
FIX-A
POR
FIR BOUNDARY
CPDLC UPLINK MESSAGE
Position report Fix-A

## Slide 44
Weather
Planed Route
FIX X
Heading Select
21NM
PR10283

## Slide 45
PR10307
FIX-1
FIX-2
FIX-3
FIX-4
Planned Route
FIX-2’
FIX-3’
BACK ON ROUTE
NOW BACK ON COURSE
Notes: <number>
<footer>
<header>
<date/time>

## Slide 46
ATSU
DSP-X (VHF)
DSP-Y (SATCOM)
AIRCRAFT
CPDLC U/L
received
MA timer set
MAS:X
MA timer time out
MAF
(MAS=F)
CPDLC U/L FAILURE
CPDLC U/L
CPDLC U/L
Time
PR10232