## Slide 1: Operational Trial of 30 NM Separation and Use of 50 NM Longitudinal Separation in the Oakland Oceanic Control Area
Presented by the Federal Aviation Administration
Date: November 2007

## Slide 2: Summary
Status update on the use of 30 NM lateral / 30 NM longitudinal separation (30/30) and 50 NM longitudinal separation between appropriately authorized and equipped aircraft throughout the Oakland Oceanic Control Area

## Slide 3: Initial Operational Trial Phases
In December 2005, the FAA began an operational trial of 30 nautical mile (NM) lateral and 30 NM longitudinal (30/30) separation in Oakland Oceanic Control Area (CTA) Sector 3
In March 2007, the trial was expanded, with limitations, to all Oakland oceanic sectors
30/30 and 50 NM longitudinal separation were applied only between eligible aircraft to enable same direction aircraft to climb or descend through the altitude of other aircraft and to enable opposite direction aircraft to climb or descend through or cruise at the altitude of other aircraft

## Slide 4: Current Operational Trial Policies
Since June 2007, the Oakland ARTCC has applied 30/30 separation and 50 NM longitudinal separation between appropriately authorized and equipped aircraft throughout the Oakland Oceanic CTA
Policies for the application of the separation minima:
  30/30 and 50 NM longitudinal separation is applied to “targets of opportunity” throughout the Oakland Oceanic CTA
    “Targets of Opportunity” are proximate pairs of aircraft that are both eligible for either 30/30 separation or 50 NM longitudinal separation
  Published ATS routes and other tracks (e.g. Pacific Organized Track System) continue to be laterally separated by a minimum of 50 NM
  50 NM remains the minimum Automatic Dependent Surveillance (ADS) based lateral and longitudinal separation applied between 30/30 eligible aircraft and Required Navigation Performance 10 (RNP-10) aircraft
    Lateral and longitudinal separation standards applied between RNP-10 and non-RNP aircraft also remain unchanged
  Oakland ARTCC accommodates operators that are not eligible for 30 NM separation throughout Oakland Oceanic CTA
    Lateral, longitudinal and vertical separation minima for aircraft not eligible for 30 NM separation are unchanged.

## Slide 5: FAA Operational Policy Notice
Operational policies, requirements and recommendations for operators planning for 30 nm separation in the Oakland Oceanic CTA are published in an FAA notice entitled “Oakland Oceanic Control Area (CTA): Continuation of Operational Trials for 30 nm Separation And Use of 50 Nautical Mile (nm) Longitudinal Separation”
  Notice is posted on the “Pacific CNS Requirements/Options” webpage: http://www.faa.gov/about/office_org/headquarters_offices/ato/service_units/enroute/oceanic/pacific_cns/
Notice details the operator/aircraft equipage requirements for 30/30 eligibility:
  FANS 1/A package (or equivalent), satellite Controller-Pilot Data Link Communications, RNP 4 navigation and Automatic Dependent Surveillance – Contract (ADS-C)

## Slide 6: Role of the OSRWG Scrutiny Group
FAA Oceanic Separation Reduction Working Group (OSRWG) Scrutiny Group was established to evaluate the operational and technical issues related to 30/30 operations including the performance of the satellite data link system
  Includes subject matter experts from air traffic, flight standards, aircraft certification and safety analysis
  Responsible for recommending to FAA managers the readiness to start 30/30 operational trials and the policies to be applied
  Meets at regular intervals to assess the status of operations

## Slide 7: Scrutiny Group Findings
14-15 August meeting found:
  Oakland Oceanic CTA averages 638 flights per day
    35% of those flights use ADS and 12% of total flights are eligible for application of 30/30
  On major individual traffic flows, the following percentage of flights are 30/30 eligible:
    Approximately 58% of flights between North America and South Pacific destinations
    Approximately 26% of flights between North America and Northern Asia destinations
    Approximately 12% of flights between Japan and Hawaii
    Approximately 10% of flights between Japan and South Pacific destinations
    Approximately 3% of flights between the U.S. mainland and Hawaii

## Slide 8: Scrutiny Group Findings (cont.)
Data link service availability was 99.83% with outages experienced at rate of 15 hours per year
  Availability is defined as the ability of the network data link service to perform a required function, under given conditions, at a given time
Data link service reliability was 99.72% with a mean time between service outages of 352.2 hours
  Reliability is defined as the ability of the data link system to perform a required function under given conditions for a given time interval
For May - July, the target of 1% missing basic (BAS) periodic reports was met

## Slide 9: Scrutiny Group Conclusions
Concluded that 30/30 operations should continue on an operational trial basis and that the group should continue to monitor satellite data link performance
Next Scrutiny Group meeting was scheduled for 30-31 October

## Slide 10: Recommendation
Group is invited to note and discuss the status of 30/30 operational trials as presented in this paper