## Slide 1: NAT SPG Activities
Date: 5-9 November 2007
Presented to: IPACG/27
By: Dale Livingston
Review of Performance-Based Communications Approach and Required Communication Performance (RCP)

## Slide 2: Introduction
NAT SPG/43, Paris, 12 to 15 June 2007
  Closure of Goonhilly Ground Earth Station (GES)
  Convene a Special NAT SPG Meeting, Paris, 15-16 Nov 2007
Prep NAT SPG Meeting held, Paris, 1-3 Oct 2007
Agree to performance-based approach and RCP
Institutional issues not addressed here
Recognized global problem

## Slide 3: Introduction
FOM criteria needs to be reinvestigated
Status of ICAO standards, recommended practices, guidance material (includes RTCA/EUROCAE)
  Amendment 40 to Annex 11, November 2001 Safety Management
  ICAO Doc 9869, September 2005 Manual on RCP
  Amendments to Annexes 6 and 11, November 2007 Provisions for RCP
  RTCA DO-306/EUROCAE ED-122, October 2007 Oceanic SPR Standard
  Amendment to Doc 4444, in work (nearly complete) Flight Plan Provisions for performance-based and RCP

## Slide 4: ICAO Doc 9869
Manual on RCP, September 2005
  Determine RCP type
  Prescribe RCP type
  Compliance initially (Aircraft type design, Operator, ANSP)
  Operational performance monitoring and alerting (Operator and/or ANSP)

## Slide 5: RTCA DO-306/EUROCAE ED-122
Oceanic SPR Standard, October 2007
  Data link services used in lieu of HF voice, includes 50 lateral
  Data link services required for 30 nm lateral/30 nm longitudinal and 50 nm longitudinal separation standards
  Considers route conformance monitoring, reroutes, and weather deviations
Based on RCP Manual and ICAO separation standards

## Slide 6: 50 longitudinal and 30/30 Intervention (DO-306/ED-122, Table 5-6)
Normal means
Alternative means
ET is at the continuity requirement

## Slide 7: RCP Allocations for Intervention (DO-306/ED-122, Figure 5-3)
Aircraft
System
Flight crew/
HMI
Comm.
service
Controller/
HMI
Ground
System
Clearance used for intervention
Acknowledgement of clearance
Information Report
1
3
2
Responder
Initiator
RCTP
TRN
RCP type
Operational communication transaction
Human confident that transaction is complete
Notes: Figure 5-3

## Slide 8: 50 longitudinal and 30/30, Surveillance (DO-306/ED-122, Paragraph 5.2.3.4)
Normal surveillance – The PR service shall deliver a position report within 180 seconds at the continuity requirement and within 90 seconds at 95% probability for:
  Periodic report, from the start of the periodic interval. The start of the periodic interval occurs when the periodic report is sent by the aircraft (see Figure 5‑2); and
  Waypoint change event report, from the actual time the aircraft crosses the waypoint.
Normal surveillance – The IER service shall deliver the lateral deviation event report within 180 seconds at the continuity requirement and within 90 seconds at 95% probability from the time the aircraft system detects that the event has occurred.
Non-normal surveillance – The IER service delivers a position report within 240 seconds at the continuity requirement and within 180 seconds at 95% probability for ADS‑C demand report or CPDLC position report, from the time the ADS‑C demand contract or CPDLC request was initiated by the ATSU/controller.

## Slide 9: 50 longitudinal and 30/30 Surveillance allocations (DO-306/ED-122, Table 5-7)
ET is at the continuity requirement

## Slide 10: > 50 lateral and time-based longitudinal Surveillance (DO-306/ED-122, Paragraph 5.2.4.2)
The PR service shall deliver position reports within 400 seconds at the continuity requirement and within 300 seconds at 95% probability at waypoint crossings from the actual time the aircraft crosses the waypoint.

## Slide 11: > 50 lateral and time-based longitudinal, Surveillance allocations (DO-306/ED-122, Table 5-8)
ET is at the continuity requirement

## Slide 12: Continuity, Integrity, and Availability (DO-306/ED-122, Table 5-9)

## Slide 13: Applicability of RCP types (DO-306/ED-122, Table 5-10)
HF Voice grandfathered in
For SATCOM voice, HFDL, etc

## Slide 14: Additional requirements
Communication service availability
  0.9999 for operational efficiency (0.999 for safety, per DO­306/ED-122)
  On a per Oceanic ATC Centre (OAC) basis
    No more than 4 outages greater than 10 minutes for any 12 month period
    Failures causing outages for multiple OACs are not counted more than once
    No more than 50 minutes of total downtime for any 12 month period
Per Appendix A and Appendix C of IPACG WP/nn

## Slide 15: Additional requirements
Monitoring and alerting requirement
  After an outage begins, the communications service shall provide ATC automation with a positive indication that there is an outage within 5 minutes

## Slide 16: Issue
Based on safety assessment, DO­306/ED­122 specifies continuity requirement for intervention and surveillance of 0.999
This requirement is considered too severe for technical practicality

## Slide 17: Operational considerations (DO-306/ED-122, Paragraph 5.2.5)
Note 1: The values for availability and continuity provide a basis for further operational safety assessment taking into account other factors and operational judgment. These values may be adjusted on the basis of a regional air navigation agreement considering the potential conditions of the airspace when the loss of data link capability occurs, including, but not limited to:
  Air traffic density;
  Proportion of aircraft using the data link service;
  Separation minima being applied;
  Number of aircraft holding a weather deviation clearance in a localized area;
  Capability and performance of detecting and indicating the loss of the data link services;
  Capability and performance of route conformance monitoring, e.g., the amount of time after the loss in which the airspace can be considered to be conflict-free; and
  Capability and performance of the alternative means of communication, including associated procedures for applying an alternative form of separation.

## Slide 18: Issue resolution
Given operational considerations, it is suggested that the continuity requirement for intervention and surveillance be adjusted to 0.99 and applied to the time requirements provided in DO­306/ED­122
Notes
  Continuity adjustment is consistent with current FOM target for continuity
  Per DO-306/ED-122, the technical time requirement (RCTP) associated with intervention is 150 sec at the continuity requirement
  Per the FOM, the target is 360 sec (round trip) at 99%, which is consistent with twice the surveillance latency requirement (one way) provided in DO-306/ED-122

## Slide 19: Recommendation
Agree to participate in and support implementation of a performance-based approach for communication and surveillance capabilities
  Prepare a position statement regarding the material provided in Appendices B and C
  The U.S., on behalf of the IPACG, will present the position statement at the Special NAT SPG meeting

## Slide 20: Position statement
Agree to
  Recognize DO-306/ED-122 as a basis for establishing performance criteria for communications and surveillance capabilities
  Augmented with 0.9999 availability requirement for operational efficiency
  Adjusted with 0.99 continuity requirement
  5 minutes for communication service to indicate to OAC that a service outage has occurred

## Slide 21: Recommendation
Identify points of contact for initial discussions on how to proceed with implementation of a performance-based approach and RCP within the Asia-Pac Region, in coordination with the NAT Region efforts
  U.S. – Tom Kraft (tom.kraft@faa.gov)
  ISPACG data link group – Paul Radford (Paul.Radford@airways.co.nz)

## Slide 22: Thank you
Comments?
Questions?