## Slide 1: Simulation Model for Pacific Oceanic Region Data Link Communication System
Presented To: FIT/16
Presented By: FAA
Date: 28 October 2008

## Slide 2: Contents
Objectives
Introduction
Model Overview
Message Routing
Animation
Output
Conclusion

## Slide 3: Objectives
To create a model of the existing Data Link communication system in the Pacific Oceanic Region (POR)
  Makes it possible to test system quickly at low cost with no risk
  Enables exploration of as many variables as desired
  Aids in prediction of system performance under proposed scenarios
  Easily modified as system evolves
  Allows for sensitivity analysis of system parameters

## Slide 4: Introduction
Simulation model built with ARENA software by graduate students at Rutgers University, includes:
  Message generation, routing and handling logic
  Animation
Simulates message traffic between aircraft and ARTCC
  ADS aircraft only
  NOPAC and CENPAC only
Attempts to model current operations with capability to predict future performance due to changes such as:
  Increase/decrease in traffic density
  Change in RNP
  Modifications to satellite or GES
  Failures and outages of any system components
  Improvements/changes in any system components

## Slide 5: Model Overview
Flights randomly generated with exponentially distributed inter-arrival times
Undergo random assignment of attributes based on distributions calculated from analysis of historical Ocean21 data
  Direction (East or West)
  Entry time, function of direction
  Operator
  Datalink Service Provider (DSP), function of operator
  Speed
  Periodic reporting rate
  Track, 9 representative tracks chosen:
    NOPAC (G344, R220)
    PACOTS (1, 2, 3, A, B, E, F)
Flights log on to GES via AFN downlink message

## Slide 6: Tracks
Notes: <number>

## Slide 7: Model Overview (Continued)
Flights generate six types of downlink messages during their time in the system
  (ADS-C) BAS, according to periodic contract attribute
  (ADS-C) WPC, function of flight progress on assigned track
  (ADS-C) LDC, aperiodic contingent on lateral deviation
  (ADS-C) ACK, acknowledgement of uplink
  (CPDLC) Request for clearance (i.e. flight level change)
  AOC, communication with airline, varies by flight
Downlink message size is assigned according to message type
  Based on historical data analysis
  Used to determine routing path and time through GES channels
Uplink messages are generated:
  To establish new contracts for flights entering system
  In response to downlinks requiring ATC response (i.e. Request for clearance)
  To “demand” position information as result of missing BAS message
Statistics collected as flights exit system

## Slide 8: Flowchart of Message Routing
Oakland ARTCC
ARINC
SITA
Ground Earth Stations
Messages
Messages
Uplink

## Slide 9: Message Routing
Downlink message path:
  Aircraft
  Satellite
  GES
  DSP (ARINC or SITA)
  ARINC messages forwarded to SITA
  ARTCC (except AOC)
Uplink message path:
  ARTCC
  DSP (SITA)
  GES
  Satellite
  Aircraft

## Slide 10: Message Routing: Satellite Data Channels
Each DSP is assigned 1 independent set of satellite channels
Each channel set contains 3 types: P, R, T
  Theoretical data rates
    Low speed: 600, 1200 bps
    High speed: 10500 bps
  Estimated effective bit rates
    Low speed: 234, 500 bps
    High speed: 4500 bps
Routing Time = Message size / Effective bit rate
Each routing time is broken down:
  50% Satellite
  20% GES
  30% DSP

## Slide 11: Message Routing: Satellite Data Channels (Continued)
All ACARS uplinks travel directly via P-channel
Downlink Messages < 33 bytes (AFN and ACK messages)
  Transmit directly through R-channel
Downlink Messages > 33 bytes (most FANS and AOC messages)
  Go through R-channel to get assigned access to T-channel
  Response sent from GES via P-channel (3-4 second delay) with access assignment
  Transmitted via T-channel
Congestion factor added to mimic observed delays experienced during high traffic on T channel (see next slide)

## Slide 12: Message Routing: T-Channel Congestion
Delay vs. T-channel load
Notes: <number>

## Slide 13: Message Routing: Failure Modes
Visible failure
  All channels in one GES fail
  Aircraft logged off
  Competition for re-logon through R-channel
  Aircraft must wait for successful re-logon to re-send messages through new GES channel set
  Delay re-logon attempts for small amount of time to simulate aircraft system reaction and warming up of standby channel
  Backup channel operates at lower performance level
Invisible failure
  CDC computer down
  Aircraft unaware of this failure
  Channels stop processing messages
  New messages are counted and disposed
  Messages retry transmission regularly
Notes: <number>

## Slide 14: Animation: Aircraft Message Status
Flights change color during course of flight according to most recent message type “sent”
BAS (Basic)
WPC (Waypoint)
LDC (Lateral deviation)
AOC (Airline operator)
ACK (Acknowledgement)
Logon and Requests

## Slide 15: Animation: Screen Shot of Running Model
Notes: <number>

## Slide 16: Output: Performance Measures
Routing time statistics
  Overall frequency distribution
  Maximum, mean, standard deviation
  Percent meeting pre-specified criteria
    i.e. Percent of downlink message routing times less than 60 seconds
Utilization of satellite, GES
Consequences of GES Failures
  Lost messages
  Aircraft unable to log-on
  Aircraft requiring controller intervention
  Number of aircraft attempting re-logon at one time
  Time to recovery of system
Notes: <number>

## Slide 17: Conclusions
Simulation model could be a valuable tool for forecasting future system performance and decision making in POR and other regions
With specific input from DSPs, users and others, model could be fine-tuned to more closely resemble realistic operations
  Clarification of existing model details
  More information about non-FANS message traffic (AOC, etc.)
  More information about message routing
    Time associated with each segment, i.e. satellite, GES
    Inter-networking between DSPs
  Details specific to 2 POR GES (Santa Paula and Perth)
    Number of satellite channels
    Failure rates