## Slide 1: Problem Reports
IPACG-29/FIT-16
Fukuoka, Japan
October 28, 2008
Gordon Sandell

## Slide 2: Problem Reports
New Problem Report Summary
New Problem Reports
  Problems Reported Since FIT-15
Specific Reports for Discussion
Existing PR Updates
  AIMS Blockpoint v14

## Slide 3: New Problem Report Summary
Limited number of reports received since IPACG-28/FIT-15
  Some reports documenting multiple events
  Some reports duplicates of documented PRs
5 New Problem Reports generated

## Slide 4: New Problem Reports
PR# | Title | Air/ ground/ link | Region | Status | Discuss at FIT?
627 | Multiple ADS Reports From B772 | Air | SOPAC | In work | Y
628 | Missing Time Stamp in WILCO From B772 | Air | NOPAC | In work | Y
629 | Missing Performance Data in ADS Waypoint Change Event Report From B744 | Air | SOPAC | In work | Y
630 | Um83 Caused FMS Reset on B744 | Air | Multiple | Ready for Review | Y
631 | A345 Sending Multiple ADS Reports | Air | SOPAC | In work | Y

## Slide 5: Specific Reports for Discussion

## Slide 6: PR-627 - Multiple ADS Reports From B772
ADS waypoint change event reports contained duplicated basic and predicted route groups
Periodic reports also included additional reports at a similar rate to those from a previous FIR
Multiple events, multiple airplanes
Under investigation by manufacturer

## Slide 7: PR-628 - Missing Time Stamp in WILCO From B772
WILCO responses from B772 omitted the timestamp
  Multiple events from the same airplanes over several days
  A couple of airplanes
ADS messages included timestamp, as did other CPDLC messages
Still under investigation
  ANSPs encouraged to report similar events

## Slide 8: PR-629 - Missing Performance Data in ADS Waypoint Change Event Report From B744
ADS waypoint change event reports containing default data (indicating no valid performance predictions)
  Airplanes that have just executed an offset
  Airplanes that have just deleted an offset
  Also periodic reports just prior to T/C or T/D
ADS function should wait for performance predictions to complete
Demand contract can be sent to obtain the missing data

## Slide 9: PR-630 - Um83 Caused FMS Reset on B744
Tailored arrival uplink caused FMS reset when flight crew selected LOAD FMC
  Uplink contained the uplinked “position” parameter as the first element of the route clearance parameter
  AT xxxxx CLEARED ROUTE CLEARANCE
  VIA TO
  DIRECT xxxxx
  DIRECT yyyyy
This should be legal but doesn’t make sense and could be confusing
  Implied “direct to” downpath fix
Recommendation is to avoid this construct

## Slide 10: PR-631 - A345 Sending Multiple ADS Reports
A345 started sending multiple ADS reports ~20 seconds apart
Seen on same airplane the following day
Under investigation by manufacturer

## Slide 11: Existing PR Updates
AIMS BP v14
  Pr 564
PR 619

## Slide 12: AIMS BPv14 on Boeing 777
AIMS BP v14 fixed one open FIT PR
  PR 564 Unable to Send Assigned Block Altitude Report
    Response to CONFIRM ASSIGNED ALTITUDE (um135) was limited to dm38 (ASSIGNED ALTITUDE)
    Now added the option to send dm77 (ASSIGNED BLOCK)
AIMS BPv14 to be available for retrofit 1Q2009

## Slide 13: PR 619 - Baffling performance differences amongst operators
PR identified differences in ADS downlink delays between operators and between airplane types
  B777 shown as having longer delays
  Additional analysis by Airways (and others) has shown the B777 issue was a problem with VHF-to-SATCOM transitions
That problem was with VHF router retaining Cat B connections too long
AIMS BP v14 software has replaced the router with a different version not susceptible to this problem
Many thanks to all who participated in the investigation

## Slide 14: Questions?