## Slide 1: Monitoring FANS-1/A Performance (FIT/16 IP/06)
Presented to: IPACG 29 FIT/16
By: Tom Kraft, Federal Aviation Administration
Prepared By: Paul Radford
Manager Oceanic Systems
Airways New Zealand
Email: paul.radford@airways.co.nz
Date: 27 October 2008

## Slide 2: Introduction
Airways NZ has been monitoring aircraft FANS-1/A performance in the Auckland Oceanic FIR against the Oceanic SPR standard requirements since mid 2007.
These requirements are specified in terms of Required Communications Performance (RCP) and surveillance latency.
Data analysis emphasises the importance of end-to-end monitoring of individual airline aircraft types at an ANSP level to detect deviations from the requirements.
Monitoring is used for compliance and for continuous performance improvement.

## Slide 3: Filtering of Raw Data
To get a more accurate representation of actual “system” performance we have found that some filtering of the raw data is required.
Data is currently filtered for:
  Duplicated downlinks
  Known CSP outages
  B777 SATCOM/VHF RGS transition issue (delays from this source have a major impact if not filtered)
  Individual aircraft (“bad” tail numbers)

## Slide 4: Filtering of Raw Data – Duplicated ADS Downlinks
Duplicates Excluded
Raw Data

## Slide 5: Filtering of Raw Data – CSP Outages
Example of ADS data filtered during May 2008.
If not filtered even this small number will impact on measured performance

## Slide 6: Filtering of Raw Data – B777 VHF Transition issue

## Slide 7: CPDLC – Monitoring RCP
Monitoring CPDLC round trip “intervention” messages to give:
  Actual Comm Performance (ACP)
  Actual Comm Technical performance (ACTP)
  Actual Crew Response (PORT)
Only monitor those uplinks that require a Wilco/Unable response. Consistent with ICAO Doc 9882 2.4.7(n)

## Slide 8: CPDLC – Monitoring RCP
Monitor a number of communication paths to get a better overall picture of performance.
  Via SATCOM (i.e MAS and operational response via SATCOM)
  Via VHF (i.e MAS and operational response via VHF)
  Via VHF/SATCOM (i.e MAS and response via different RGS)
  Via any RGS (Overall Performance)
Observed performance in SOPAC has been close to the Oceanic SPR requirements following slides give an overview.

## Slide 9: CPDLC ACTP – All RGS (Note: B777 VHF RGS delays not excluded)

## Slide 10: CPDLC ACP – All RGS (Note: B777 VHF RGS delays not excluded)

## Slide 11: CPDLC Pilot Operational Response Times – All RGS

## Slide 12: CPDLC – SATCOM ACTP for B744 from one airline company

## Slide 13: CPDLC – SATCOM ACP for B744 from one airline company

## Slide 14: CPDLC – SATCOM ACTP for A343 from one airline company

## Slide 15: ADS – Monitoring downlink latency
Currently monitoring individual airline fleet performance via SATCOM.
As with CPDLC the performance seen in SOPAC is within the “ball park” of SPR requirements when filtered.
The DO306 latency requirements for application of reduced distance based separations are 95% downlinks within 90 secs, and 99.9% within 180 secs.
Following slide illustrates performance from our major B777 customer.

## Slide 16: ADS – SATCOM latency for B777 from one airline company (Note: VHF RGS transition delays excluded)

## Slide 17: Monitoring - Overview
Significant performance differences between aircraft types, and between same type operated by different airlines
Current RCP and latency performance is in the ballpark in SOPAC
Aim to date has been one of continuous performance improvement with a number of FANS Problem reports raised against “poor” relative performers.

## Slide 18: Supplementary Slides
Following slides provide additional information pertinent to the monitoring of RCP and ADS latency.

## Slide 19: Supp. #1 - Performance degradation by aircraft use of low speed ACARS channels

## Slide 20: Supp #2– B777 VHF RGS transition Issue
ADS performance data indicated that the performance of the B777 aircraft fleets was significantly lower than that seen from other aircraft.
Analysis of all B772/3 aircraft showed a significant correlation between downlink delays and areas of transition from VHF to SATCOM RGS.
Of the 3035 downlinks monitored in June 2008 105 were received more than 90” after transmission. Of these 105 downlinks:
    8% were not attributable to VHF RGS transitions
    18% attributable to Pacific VHF RGS transitions
    87% attributable to NZ VHF RGS transitions

## Slide 21: Supp #3 – B777 VHF RGS transition Issue
An analysis of downlinks that had a latency of >90 seconds could not identify any VHF/SATCOM transition issues with A343 or A345 aircraft. The performance of B777 and Airbus aircraft when delays due to RGS transition are excluded are similar.
A FANS1/A problem report has been raised and after Boeing investigation an issue was found that was causing delays in transitions from SITA VHF RGS. The fix for this is expected in early 2009.
This issue illustrates the benefits of individual fleet analysis in detecting performance variations.
The data analysis is illustrated in the following slides.

## Slide 22: Supp #4 – NZZO FIR Plot of delayed reports from B777 (VHF RGS Range rings at 200NM – Norfolk Island 200/300NM

## Slide 23: Supp # 5 – B777 Delays vs distance from VHF RGS

## Slide 24: Supp # 6 – Regional SATCOM differences
ARINC provided data in a briefing to the ISPACG Planning Team in October 2008 that illustrates performance differences from the different SATCOM RGS.
This data was for the period 1 June through 30 August and shows that performance from the Pacific POR1 satellite is one of the best observed.
Graph of SATCOM ADS performance seen through the various satellites is on the next slide.

## Slide 25: Supp # 7 – Regional SATCOM differences – ARINC observed ADS latency

## Slide 26: Thank you