## Slide 1: Proposed Changes to FANS 1/A INTEROP Standard (FIT/16 IP/3)
Date: 28 October 2008
Presented to: Informal Pacific ATC Co-Ordinating Group (IPACG/29) FANS 1/A Interoperability Team (FIT/16)
By: Tom Kraft, Chief Scientific and Technical Advisor for Aeronautical Communications, Aviation Safety, Federal Aviation Administration Email: tom.kraft@faa.gov Mobile: +1-202-369-2168
Suggested improvements

## Slide 2: Introduction
FAA is investigating two possible changes to RTCA DO­258A/EUROCAE ED­100A, FANS 1/A Interoperability Standard
  Logon correlation
  Media selection criteria
The proposed changes only affect infrastructure and will not impact any aircraft equipage
Acceptance of the changes are subject to RTCA/EUROCAE document management procedures

## Slide 3: DO258A-ED100A - Logon correlation
B767, B757, B737, and MD11 requires manual pilot entry of aircraft registration number
Aircraft registration number is used to correlate with flight plan information
Incorrect pilot entry leads to ATSP system sending response to incorrect aircraft
Use of ground-ground messaging (e.g. AIDC FANS Application Message (FAN)) can minimize response being sent to incorrect aircraft
No provisions in DO-258A for use of AIDC FAN message

## Slide 4: DO258A-ED100A - Logon correlation
3.4.2 Addressing of Uplink Messages
a) Every uplink message from an ATS Provider shall use the aircraft registration number which is contained within the portion of the AFN logon message (FN_CON) or ground-ground connection transfer message that is encapsulated by the Cyclical Redundancy Check (CRC). The exception to this is an AFN Acknowledgement (FN_AK) message with an overall reason code of 4 which may be addressed using the aircraft registration number contained in the ACARS header (see note).
Note: If an AFN Contact (FN_CON) message is received where the aircraft registration number in the ACARS header and the aircraft registration number in the body of the FN_CON message differ, the FN_AK (with reason code 4) should be addressed using the aircraft registration number that was contained in the ACARS header of FN_CON message to ensure the message is delivered to the correct aircraft. To ensure the message is processed by the FMS the body of FN_AK should use the registration number that was contained in the body of the FN_CON.
Proposed change

## Slide 5: Media selection criteria
RTCA DO-258A, para 2.2.1.e) states, “The requirement for a particular medium on a particular route will be specified by the appropriate authorities based on factors such as performance and coverage.”
Above somewhat contradicts para 3.4.3, “the CSP determines the routing of FANS-1/A messages to the aircraft according to the guidelines given in this document”
Current provisions limit the ability of the ATSP to specify the medium to use under certain conditions

## Slide 6: Media selection criteria
3.4.3 Message Routing
As the CSP determines the routing of FANS-1/A messages to the aircraft according to the guidelines given in this document, the following text elements (described in ARINC Specification 620, section 3.7) are not used by an ATS Provider in uplink messages; AP, GL, TP because the CSPs have the responsibility for routing of uplink messages.
Although the AP, GL or TP text elements should not normally be used because they override the CSP’s own routing algorithms, there are specific cases where their use may be of benefit. Under such circumstances ANSPs may use these TEIs to instruct the CSP to attempt to deliver the message as specified by the TEI. If the CSP's routing tables indicate that station or medium is not available for the aircraft, attempts to deliver as specified in the routing TEI fail, or no routing TEI is included, the CSP determines the routing of FANS-1/A messages to the aircraft according to the guidelines given in this document.
Note: These text elements are used to direct the CSP to deliver a message via a specific air-ground facility i.e., VHF ground station, GES, or HF ground station.
Proposed change

## Slide 7: FIT/16 conclusion
Note the information provided in this paper
Provide input on these proposed improvements

## Slide 8: Thank you
Remarks