## Slide 1: Performance specification template (FIT/16 WP/3)
Date: 28 October 2008
Presented to: Informal Pacific ATC Co-Ordinating Group (IPACG/29) FANS 1/A Interoperability Team (FIT/16)
By: Tom Kraft, Chief Scientific and Technical Advisor for Aeronautical Communications, Aviation Safety, Federal Aviation Administration Email: tom.kraft@faa.gov Mobile: +1-202-369-2168
Communication (RCP) and surveillance

## Slide 2: Overview
Introduction
Current activities
Review of the performance-based approach
Intended uses of performance specifications
Considerations for performance specifications
FIT/16 action

## Slide 3: Introduction
A number of performance specifications are under development
  RCP 240 when applied to data link systems (/D)
  RCP 400 when applied to data link systems (/D)
  RCP 400 when applied to “non-traditional,” (e.g., satellite) voice communication systems (/V)
  new RCP types, such as to support implementation of data link systems in continental (domestic) airspace, e.g., RCP 60/D or RCP 120/D
  criteria for surveillance, e.g., position reporting criteria for different separation standards
The intent is to provide a globally consistent way to convey performance-based criteria.
  For each specification
  Within a common framework
  Guidelines for the framework and template can be found at Appendix C
Specifications could become part of ICAO Doc 9869, Manual on Required Communication Performance (RCP)

## Slide 4: Current activities (1 of 2)
North Atlantic (NAT), Asia-Pacific (ASIA-PAC), …
  Draft ICAO Doc 9869, Manual on RCP
  RTCA DO‑306/EUROCAE ED‑122, Oceanic SPR Standard, Oct 2007
  Using (Draft) RCP 240/D and RCP 400/D (See Appendix A and B of WP, specs are different)
PARC CWG (See FIT/16 IP on PARC CWG, FOI and Sat Voice)
  FANS 1/A over Iridium (FOI) - using (Draft) RCP 240/D
  Satellite voice – (Under development) RCP 400/V

## Slide 5: Current activities (2 of 2)
RTCA SC-214/EUROCAE WG-78, Data Link Standards Group
  DO‑264/ED‑78A, Dec 2000
  RTCA DO‑290/EUROCAE ED‑122, Continental SPR Standard, Apr 2004.
  DO‑290/EUROCAE ED‑122 leaves RCP type specification to States
ICAO Doc 9869, Manual on RCP
  Draft available since Sep 2005
  First Edition, 2008, takes experience gained from practical use

## Slide 6: Performance-based approach (1 of 2)
The performance-based approach characterizes function and performance based on intended operations in any given airspace, not based on technology
Global seamless operations for communication and surveillance; complements performance-based navigation specifications
It may be relevant to specify additional operational criteria to include functional capability or other performance characteristics, not specified by an RCP type (per ICAO Doc 9869)

## Slide 7: Performance-based approach (2 of 2)
The performance specifications are used when we implement a change and the change is predicated on communication and/or surveillance capability and performance
  Provide new operational capabilities, such as reducing separation minimum or increasing airspace capacity
  Employ new systems, including those provided by commercial services, using different technologies, such as satellite voice or data link
  Manage the implementation of the change, such as when the performance and capabilities for communication and/or surveillance are mixed among the population of aircraft in the same airspace

## Slide 8: Intended uses of performance specs
Determine the viability of a particular technology (voice/data)
**Safety oversight of service provisions and operations**
  Mixed-capability fleet operations, e.g., RCP 240, RCP 400, No RCP
  Qualification and acceptance systems and services, e.g., CSP & ANSP automation
Agreements/contractual arrangements with CSPs
**Operational authorizations, flight crew training/qualification**
**Design approval of aircraft data link systems**
**Post-implementation monitoring**
**(See related FIT/16 WP/IP)**

## Slide 9: Considerations for perf specs
Limit RCP types and levels of surveillance performance
Associate performance specifications to the ATS function
Correlate voice and data performance
Distinguish communication from surveillance
Parameters and units of measure
Points of measurement
Allocate according to institutional boundaries

## Slide 10: Framework for com perf specs
Terms and acronyms
RCP 240
  Data, e.g., CPLDC over Satellite or VHF
RCP 400
  Data, e.g., CPDLC over HF data link
  Voice, e.g., Satellite
RCP [future], e.g., RCP 120, RCP 60, or RCP 10
  Data, e.g., CPDLC over VHF (continental (domestic) airspace)
  Data, e.g., CPDLC for new oceanic and remote strategic objectives
  Voice, e.g., new technology voice for (continental (domestic) airspace)

## Slide 11: Framework for surv perf specs
Terms and acronyms
Required surveillance performance
  Data type /180, e.g., FMS WPR or ADS‑C over Satellite or VHF
Required surveillance performance
  Data type /400, e.g., FMS WPR or ADS-C over HF data link
  Voice type /400, e.g., Satellite

## Slide 12: RCP 240 specification
Airspace specific considerations
RCP parameter values
RCP monitoring and alerting criteria
RCP 240/D allocations
  ATS provider
  CSP
  Aircraft system
  Aircraft operator

## Slide 13: Availability terms and measurements
Unplanned outage begins
(and detected)
Notification of restored service
Outage duration limit
Notification of unplanned outage delay
unplanned outage duration
Unplanned outage begins
(and detected)
Notification of restored service
Outage duration limit
Notification of unplanned outage delay
unplanned outage duration
Maximum accumulated unplanned outage time (min/yr) =
sum of unplanned outage duration over a period of time (year),
where unplanned outage duration > outage duration limit
No operational impact
Affects continuity
Affects availability

## Slide 14: FIT/16 action
Note the information in the paper
Agree to the concept of global performance-based specifications for communication and surveillance
Consider this paper as a starting point for the GOLD Ad Hoc Working Group to develop and coordinate performance specifications for communications and surveillance

## Slide 15: Thank you
Remarks